## Slide 1: PETRA IV Lattice Studies
Joachim Keil, DESY
on behalf of the PETRA IV study group
2nd Workshop on Low Emittance Ring Lattice Design
Lund, 1 December 2016

## Slide 2: Outline
Introduction
Layout of PETRA III/IV
Design Parameters of PETRA IV
Lattices under consideration:
  HMBA-Lattice
  Lattice with phase space exchange and arcs with non-interleaved sextupoles
Conclusion & Outlook

## Slide 3: Overview of PETRA III
Parameter | Value
Energy | 6 GeV
Current | 100 mA, Top-Up
Hor. Emittance | 1.2 nm·rad
Ver. Emittance | 12 pm·rad
Bunches | 40, 960
Circumference | 2304 m
Harmonic number | 3840
RF Voltage | 20 MV
Energy loss/Turn | 6.1 MeV
Hall PXN
Hall PXE
Von Laue hall
PETRA III
PETRA I: e± collider (1978-1986), PETRA II: pre-accelerator for HERA (1990-2007)
PETRA III: commissioned 2009; in operation for users since middle of 2010
Von Laue hall: 14 beamlines, PXE, PXN (2014): 7+5 beamlines

## Slide 4: Motivation for PETRA IV
The Multi-Bend Achromat offers new possibilities to reach ultra low emittances
Many facilities world wide have upgrade plans based on MBA designs
With an emittance of 1.2 nm·rad PETRA III will not be competitive in the future
Design goal of PETRA IV: diffraction limited at 1 Å in both planes at 6 GeV
Emittance 10‒30 pm·rad
Round beam to mitigate emittance growth due to IBS
R. Bartolini, IPAC 2016
MBA
DBA, TBA

## Slide 5: Layout of PETRA III
Octagonal shape, circumference 2304 m, emittance 1.2 nm·rad
Eight Arcs (45°), 201.6 m long
  5 pure FODO-arcs
  2 modified FODO arcs with 2 DBA-like cells at the beginning (PXN, PXE)
  One arc build from 9 DBA cells Lcell = 23 m, 5 m ID straight sections
Eight straight sections
  4 long straights N,S,E,W (108 m) 20 damping wigglers in N and W; RF cavities in S (20 MV)
  4 short straights NW,NE,SE,SW (64.8 m)
Beamlines
  von-Laue Hall:14; PXN:5; PXE: 7
Pre-Injectors:
LINAC II & PIA: 450 MeV
DESY II: 6 GeV, ε≈340 nm·rad

## Slide 6: Possible Layout of PETRA IV
Constraints for upgrade:
  Keep tunnel and experimental halls
  Keep beamline positions as far as possible
  Keep circumference (2304 m)
But: Most IDs are installed at canted sections
  5 mrad in von Laue Hall
  20 mrad in PXE, PXN
It likely that canting won’t be possible due to the emittance contribution of IDs in canted sections with
New experimental hall in the SW-W arc
Some beamlines have to move to the new hall

## Slide 7: Time Schedule of PETRA IV Project
Tight time schedule:
Project preparation phase 1/16 – 12/19
Conceptual Design Report 4/2018
Technical Design Report 12/2019

## Slide 8: Desired Parameters of PETRA IV
Very challenging design parameters!
Equal beam size at IDs → round beam
Goal: Investigate what are the limits to reach the desired parameters
Parameter | Value
Energy | 6 GeV (4.5 – 6 GeV)
Current | 200 mA (100 – 200 mA)
Number of bunches | ~ 1000
Emittance horz. | 10 pm·rad (10 – 30 pm·rad)
vert. | 10 pm·rad (10 – 30 pm·rad)
Bunch length | ~ 100 ps
Number of Beamlines | 30

## Slide 9: Lattices Investigated for PETRA Upgrade
An upgrade to convert PETRA III into a diffraction limited light source needs a reduction in emittance of two orders of magnitude
  New lattice is required
  Very strong sextupoles → severe reduction of dynamic aperture
  Exploit unique layout of PETRA with 8 long straight sections and 6 ID-less arcs for unconventional designs
Started to investigate two different lattice types
  Based on the ESRF-HMBA cell
  Based on 4D-phase space exchange and MBAs with non-interleaved sextupoles

## Slide 10: Lattice based on HMBA Cells
Lattice build from HMBA-cells of the ESRF-EBS
  Selected also at other facilities as a starting point for lattice design
  Scaling of the cell is necessary to replace the DBA cells & FODO-arcs of PETRA III
Arcs:
  Use 9 HMBAs cells to build a 45° arc (201.6 m)
  All 8 arcs in all octants are identical
Straight sections:
  FODO cells to connect arcs with matching triplets at both ends
  Altogether 4 long (108 m) and 4 short (64.8 m) straight sections
PETRA III DBA cell
Scaled H7BA cell

## Slide 11: H7BA Cell Scaling
ESRF-EBS
PETRA III
PETRA IV
5°
11.25°
L(ESRF-EBS) = 26.4 m
L(PETRA III) = 23 m
Scaling the H7BA cell to the P3 DBA cell:
  Length: 26.4 m → 23 m
  Bending angle: 11.25° → 5°
Result:
  Emittance: 134 pm rad → 11 pm rad
  Dispersion peak: 9 cm → 3.5 cm
  Quadrupoles & sextupoles stronger → DA, MA smaller
Scaled H7BA-cell
H7BA-cell of ESRF
~9 cm
~3.5 cm
0
5
10
15
20
25
0
5
10
15
20
25
Betafunctions [m]
-0.16
-0.14
-0.12
-0.10
-0.08
-0.06
-0.04
-0.02
0.00
0.02
0.04
0.06
0.08
Dispersion [m]
0
5
10
15
20
0
5
10
15
20
25
Betafunctions [m]
-0.07
-0.06
-0.05
-0.04
-0.03
-0.02
-0.01
0.00
0.01
0.02
0.03
Dispersion [m]

## Slide 12: HMBA Lattice : Arcs
9 H7BA cells, 207 m, 45°
~3.5 cm
~25 m
All 8 arcs have equal optics and phase advance → 72 HMBA cells
Two octants are mirror symmetric; super periodicity of lattice is 4
950
1000
1050
1100
1150
0
5
10
15
20
25
30
35
Betafunctions [m]
-0.07
-0.06
-0.05
-0.04
-0.03
-0.02
-0.01
0.00
0.01
0.02
0.03
Dispersion [m]

## Slide 13: HMBA-Lattice : Straight Sections
Layout of straight sections:
  FODO lattice with matching triplets at both ends
  Phase advance of 2·2π (long straight section) and 2π (short straight section) in both planes to keep symmetry
  RF cavities (500 MHz, 5 MV) in south
Short straight sections in SW, NW, NE, SE
Length 64.8 m
2 x FODO
Triplet
Δφx = Δφy = 2π
Long straight sections in N, S, E, W
Length 108 m
5 x FODO
Triplet
Δφx = Δφy = 2·2π
arc
arc
arc
arc
1120
1140
1160
1180
1200
1220
1240
0
5
10
15
20
25
30
35
Betafunctions [m]
-0.07
-0.06
-0.05
-0.04
-0.03
-0.02
-0.01
0.00
0.01
0.02
0.03
Dispersion [m]
2000
2050
2100
2150
0
5
10
15
20
25
30
35
Betafunctions [m]
-0.07
-0.06
-0.05
-0.04
-0.03
-0.02
-0.01
0.00
0.01
0.02
0.03
Dispersion [m]

## Slide 14: HMBA Lattice : DA and MA
Result for the full ring from HMBA cells:
Emittance of HMBA-based ring is 12 pm·rad at 6 GeV 
  No effects of IDs on emittance considered
  In addition a factor of two for round beam
Momentum acceptance is ok: 3-4% 
Dynamic acceptance is too small: 0.29 /1.2 mm·mrad 
  Cell not yet optimized (tune scans, MOGA, …)
Some quadrupoles too strong, g < 120 T/m 
  Stronger focusing & shorter cell length
Next steps:
Try a more relaxed H6BA (or H5BA) cell and include (vertical) damping wigglers to reduce emittance
Try a relaxed MBA cell design in 6 ID-less arcs
Optimization of the lattice (tune scans, MOGA, …)
Include errors
Not optimized
βx=21.9 m βy=20.9 m

## Slide 15: Touschek Lifetime
For very small emittances Touschek lifetime will rise again
A larger momentum acceptance shifts the lifetime minimum to higher emittances
From Piwinski’s formula: For  > 5 h in the range of 10-30 pm·rad a momentum acceptance of > 2% is needed
  Conditions: E = 6 GeV, round beam, N = 1010 particles in bunch <bx> = 4.8 m, <by> = 8.9 m, <Dx> = 1.3 cm , σs=1 cm, σp = 10-3 (scaled ESRF-HMBA-cell)
10 pm
20 pm
2.5%
2%
1.5%

## Slide 16: Phase Space Exchange Lattice: Twists
Lattice design to get a round beam:
Two x-y phase space exchange insertions (Twists) in long straight sections
Twist insertions couple (x,x’) ↔ (y,y’) phase space twice per turn
Positions of Twist insertions still allow off axis injection (injection oscillation in x-plane in ver. low gap chambers at undulators)
Horizontal natural emittance e0 is equally distributed in both planes: ey ≈ ex ≈ e0 /2 (exact if two Twists installed opposite of each other)
3 arc octants,
injection section,
undulator sections :
x = hor., y = vert.
3 arc octants:
y = hor., x = vert.
y ↔ x
x ↔ y
Idea of Lattice: R. Brinkmann
schematic

## Slide 17: Phase Space Exchange Lattice: Arcs
mx,y = 
SF
SF
PETRA has altogether 8 arcs:
  In two arcs a design with achromats is needed for the installation of undulators
  6 ID-less arcs can have a different design
Each of the six arcs consists of a ~200 m long MBA with a bending angle of 45°
Use non-interleaved sextupole pairs with 180° phase advance to cancel nonlinear kicks of sextupoles → large DA
Only SF-type cells in all arcs (because of two Twists)
Two SF families correct the sum of the chromaticities of the two half-rings 1 & 2:
Unit cell in arcs without undulators
bx ,by / m
Dx / m
0 = 44 pm·rad @ 6 GeV
(preliminary design)

## Slide 18: Test of Phase Exchange Lattice
Prove of principle of the phase exchange lattice
Eight straights with equal lengths (two with damping wigglers; one with 100 MHz RF)
Two Twist sections in E and W (9 skew quads)
Eight arcs with non-interleaved sextupoles Two SF sextupole families (N + S)
No Undulator arcs
Damping wigglers
Twist
Arc from unit cells

## Slide 19: Test-Lattice : DA and MA
Hor. Dynamic Acceptance ~4.5 mm·mrad for Dp/p=0 (ver. always larger)
Momentum Acceptance ± 2.4% (limited by higher order chromaticity)
Emittance: x ≈ y = 24 pm·rad @ 6 GeV (without DW)
Mesh: -3 mm < x0 < 3 mm (at β=1 m) and y0=0 mm
Red: δ<0, green δ>0
Tune footprint for ξx= ξy = 0

## Slide 20: Phase Space Exchange Lattice V1
Added two arcs with HMBA cells in Version 1 of Phase Space Exchange Lattice
HMBA cell has 13 pm·rad at 6 GeV (matched to )
Design of ID-less arc cells and Twist insertion is unchanged
Emittance of ring is 27/26 pm·rad (6 GeV, no DW, no IDs)
Almost round beam due to small contribution of the undulator cells to emittance compared to arc cells

## Slide 21: Chromaticity Correction and DA
Tried two chromaticity correction schemes:
With sextupoles in HMBA-arc on:
  Global DA limited by the cell-DA (~0.4 mm·mrad in hor. direction) and by the arc-DA in momentum
With sextupoles in HMBA arc off:
  Compensation of Chromaticity in ID-less arcs
  Asymmetry in mode distribution (3 vs. 5) → stronger sextupoles required → reduced MA
Mixing of interleaved/non-interleaved cell designs is not optimal
Next step: integrate a H6BA cell with non-interleaved sextupoles in lattice → damping wigglers needed
SF
SF
mx,y = 
NI-H6BA: 33 pm·rad
H7BA: 12 pm·rad
mx,y = 3/

## Slide 22: Conclusions and Outlook
Lattice studies how to convert PETRA III in a diffraction limited light source using MBAs have been started
Goal for parameters are very challenging: emittance of 10-30 pm·rad at 6 GeV for 200 mA in ~1000 bunches
Two different lattice types are currently being evaluated:
  A lattice based on ESRF-style H7BA-cells
  A lattice based on MBAs with non-interleaved sextupole pairs and incorporated x-y phase space exchange
Lattice studies are still in a very early stage
Next steps: Optimization of cell designs for both lattice types; include realistic errors in the simulations; collective effects; injection scheme, …