## Slide 1: Envelope tracking as a tool for low emittance ring design
M. Aiba and M. Ehrlichman
2nd LERD workshop
01.12.2016, Lund, Sweden

## Slide 2: Introduction
Computations for low emittance ring design (LERD)
  Linear optical functions (Beta and Dispersion)
    Basis of LERD – Quads and Bends configuration
  Radiation integrals
    → Emittance, Damping time, etc.
  Particle tracking
    → Nonlinear opt. – Dynamic aperture, life time, etc.
  Envelope (or sigma matrix) tracking
    → Emittance, Damping time, IBS, etc. for any coupled lattice
Implemented in SAD code from KEK
Not everybody is using this “tool”

## Slide 3: Sigma matrix
Sigma matrix represents the beam:
- Beam sizes (squared) = Diagonal elements
- Emittances = Eigen values
- Coupling terms = Off-diagonal elements

## Slide 4: Envelope tracking (1)
Transport sigma matrix element by element
Synchrotron radiation is included as Damping and Diffusion matrices
  Reference: K. Ohmi, K. Hirata, and K. Oide, “From the beam-envelope to synchrotron-radiation integrals”, Phys. Rev. E 49-1, p.751 (1994)
IBS can be included in the same manner
  Reference: K. Kubo, K. Oide, “Intrabeam Scattering in Electron Storage Rings”, PRST-AB 4, 124401 (2001)
    Generalization of the method in J.D. Bjorken, S.K. Mtingwa, “Intrabeam Scattering”, Part. Acc. Vol. 13, pp. 115-143 (1983)

## Slide 5: Envelope tracking (2)
SR and IBS effects are computed at each element
B=
1) At all elements
2-a) If the element is dipoles
Damping:
Transport & Diffusion:
2-b) If the element is not dipoles
Transport:
IBS:
3) Continue tracking until an equilibrium is reached
are computed
with IBS theory for given
sigma matrix elements
Damping matrix
(on-energy beam)
include gradient
and edge of bending
Diffusion matrix
IBS diffusion

## Slide 6: Rad. Int. vs Envelope tracking
Comparison for SLS2 lattice
 | Radiation integral | Envelope tracking
Natural emittance (pm) | 137 | 139
Energy spread (‰) | 1.03 | 1.03
Hor. Damping time (ms) | 4.54 | 4.48
Ver. Damping time (ms) | 8.07 | 7.96
Long. Damping time (ms) | 6.60 | 6.57
Note:
- Need to slice dipole to 1~2 cm length for good agreement
for Envelope tracking.
- Required slice length depends on optical function.

## Slide 7: Emittances with full coupling
Envelope tracking can handle any coupled lattice
Equilibrium emittances of Mobius rings (no IBS) are computed:
* M. Borland, Private communication (2015)
is confirmed *

## Slide 8: IBS simulation (1)
“Standard” simulation procedure
  Compute IBS growth rate for one turn
    IBS (diffusion) increases the momentum spread (<x’2>, <y’2>, <d2>)
  Add synchrotron radiation damping at the end of turn
    For the transverse planes:
    e=e0+deIBS+deSR
    deSR is computed for the equilibrium emittances and damping
    times
    Transverse equilibrium emittances are set “artificially”
    to mimic a coupled lattice
    For the longitudinal plane:
    d=d0+ddIBS+ddSR
    and the bunch is “forcibly” fit to the RF bucket
  Continue the tracking until deIBS+deSR~0 and ddIBS+ddSR ~0
  Faster simulation: e=e0+N(deIBS+deSR) (N~10-1000)
s
𝛿

## Slide 9: IBS simulation (2)
Result for:
  Zero current bunch length ~ 3mm
  Zero current vertical emittance = 5 pm (Artificially set!)
Standard → Env. tracking:
Horizontal emittances ↑
Vertical emittances →
Longitudinal emittance ↓

## Slide 10: IBS simulation (3)
Simulation for full-coupled lattice
 | Without IBS | IBS "Standard" simulation | Env. tracking with SR+IBS
Hor. Emittance (pm) | 88 | 165 | 135
Ver. Emittance (pm) | 88 | 88 | 134
Energy spread (‰) | 1.03 | 1.31 | 1.21
Bunch length (mm) | 1.24 | 1.58 | 1.45
Bunch current (mA) | 5 | 5 | 5
Short bunch length and increased bunch current to enhance IBS
Weak point of Standard simulation
(artificial introduction of coupling)
is more evident for full-coupled lattice

## Slide 11: Summary
Envelope tracking
  a good complement tool for LEDR
  can handle any coupled lattice
  including synchrotron radiation and IBS