## Slide 1
Nonlinear dynamics and Low emittance tuning for CLIC damping ring (DR) new design
H. Ghasem1,2
Y. PapaPhilippou2
1 School of Particles and Accelerators, IPM, Tehran, Iran
2 CERN, Geneva, Switzerland
2nd Workshop on Low Emittance Ring Lattice Design, MAXIV
1-2 December 2016
Special thanks to Javi Alabau-Gonzalvo and Eduardo Marin Lacoma

## Slide 2
Outline
CLIC overview
CLIC DR new design
  Longitudinal variable bend and superconducting wiggler
  Trapezium field profile dipole
  Optics and parameters
Nonlinear dynamics
  Chromaticity correction and tune sensitivity with energy
  Phase space and dynamic aperture
  Lost particles
  FMA
  Multipole error
  Acceptance
Vertical emittance tuning algorithm - to bring the vertical emittance to design value (εy<1 pm rad including IBS effect) under the misaligned lattice
  Effects of misalignments – Theory
  Distribution of correctors
  Tuning algorithm
  Tolerances
  Vertical emittance

## Slide 3
The goal: Colliding electrons and positrons head-on collision at energies up to several Tera-electron volts (TeV).
CLIC overview

## Slide 4
Technology: Using radiofrequency (RF) structures and a two-beam concept to produce accelerating fields as high as 100 MV per meter to reach a nominal total energy of 3 TeV, keeping the size and cost of the project within reach
CLIC overview

## Slide 5
The DRs’ layout has a racetrack shape and consists of two arcs and two long straight sections.
The arcs are composed of theoretical minimum emittance (TME) cell with longitudinally variable bends and the straight sections are based on FODO cell filled with high field super conducting damping wigglers.
Each arc/straight section includes of 42 TME/10 FODO cells and there are totally 90 dipoles and 40 superconducting wiggler magnets in the whole DR.
There are four matching sections grouped in two types to match the optics of straight section to the optics of arc section and vice versa.
General layout of CLIC damping ring (DR)

## Slide 6
The longitudinally variable dipole, whose magnetic field varies along their length, can provide lower horizontal emittances than a uniform dipole of the same bending angle.
For this propose, the maximum magnetic field of a variable bend should be applied at its center and decreases towards the two exit edges of the dipole.
Several longitudinal field profile of dipoles and corresponding DR parameters have been studied.
S. Papadopoulou, F. Antoniou and Y. Papaphilippou,
Emittance reduction with variable bending magnet strengths: Analytical optics considerations, preprint (2016).
Longitudinal variable bend
The results revealed that damping ring based on trapezium field profile dipole provides better conditions in view of beam emittance, number of dipole and ring circumference, etc. and therefore I mainly focus on DR based Trapezium dipole.
Defining λ and ρ as λ = L1/L2 and ρ = ρ1/ρ2 and assuming L as the half length of dipole ;

## Slide 7
Parameters | Highest field section | Lowest field section
Length (cm) | 4.1825 | 5.0550
Field (T) | 1.7666 | 0.8366
Radius (m) | 5.4000 | 11.4028
Def. angle (Deg.) | 0.4438 | 0.2540
K (m-2) | -1.1000 | -1.1000
Gradient (T/m) | -10.4937 | -10.4937
The dipole total length is set to L = 58 cm as the optimized value.
Each trapezium field profile dipole bends the beam 4 Degrees.
Trapezium dipole has small gradient for beam focusing.
The highest field section with length of about 4.2 cm provides magnetic field of 1.76 T.
Trapezium field profile dipole

## Slide 8
Parameters | Value
Energy (GeV) | 2.860
Circumference (m) | 359.440
Hor./Ver. tune | 45.2895/8.3133
Natural emittance (pm.rad) | 75.8924
Natural chromaticity | -128.789/-61.832
1st order mom. com. factor | 1.2478E-4
Energy spread | 1.2745E-3
Energy loss per turn (MeV) | 5.721
Damping time (ms/ms/ms) | 1.179/1.199/0.604
TME cell;
Length= 2.45 m
ψx/2π= 0.442
ψy/2π= 0.042
FODO cell;
Length= 5.969
ψx/2π= 0.238
ψy/2π= 0.096
Wiggler (l=2 m, B=3.5 T, λ=49 mm)
Dispersion suppressor;
Length= 8.56
ψx/2π= 0.851
ψy/2π= 0.709
Dispersion suppressor;
Length=8.57
ψx/2π= 0.851
ψy/2π=0.726
Optical functions and parameters

## Slide 9
Two families of sextupole magnets both with the same length of 15 cm in the TME cell are considered to correct the natural chromaticity of ring to +1.
Parameters | SD | SF
Length [cm] | 15 | 
Pole radius [mm] | 15 | 
Sextupole strength [m-2] | -362.6698 | 416.5494
B” (T/m-2) | -3459.7589 | 3973.7531
Pole tip field (T) [R=15 mm] | 0.3892 | 0.44705
Small variation of tune point up to ±0.3 % energy deviation reveals that present sextupole arrangement was good a starting point to perform nonlinear beam dynamics.
Chromaticity correction-Tune shift with energy

## Slide 10
ΔP/P=0
ΔP/P=0.3%
ΔP/P=-0.3%
DA: Physical transverse stable space for the particles after a given number of turns (2000 here)
The injected beam normalized emittance and energy spread;
For electron DR: εxn=10 μm and εyn=10 μm, δ=0.3%
For positron DR: εxn=65 μm and εyn=10 μm, δ=0.3%
Phase space & DA
Electron DR
Positron DR

## Slide 11
ΔP/P=0
ΔP/P=0.3%
ΔP/P=-0.3%
DA & lost particles
Electron DR
Positron DR

## Slide 12
Frequency Map Analysis
ΔP/P=0
ΔP/P=0.3%
ΔP/P=-0.3%

## Slide 13
 | Order | Multipole | Systematic | Random
Dipole, Bn/B1 @ 10 mm | 2 | Quadrupole | 1.00 *10-4 | 1.00*10-3
 | 3 | Sextupole | 1.50*10-4 | 1.00*10-3
 | 4 | 8-pole | 0.00 | 1.00*10-3
 | 5 | 10-pole | 5.00*10-5 | 1.00*10-3
 | 6 | 12-pole | 0.00 | 1.00*10-3
 | 7 | 14-pole | 5.00*10-4 | 1.00*10-3
 | 8 | 16-pole | 0.00 | 1.00*10-3
Quadrupole, Bn/B2 @ 10 mm | 3 | Sextupole | 0.00 | 1.00*10-3
 | 4 | 8-pole | 0.00 | 1.00*10-3
 | 5 | 10-pole | 0.00 | 1.00*10-3
 | 6 | 12-pole | 1.00*10-6 | 1.00*10-3
 | 7 | 14-pole | 0.00 | 1.00*10-3
 | 8 | 16-pole | 0.00 | 1.00*10-3
 | 9 | 18-pole | 0.00 | 1.00*10-3
 | 10 | 20-pole | 1.00*10-7 | 1.00*10-3
 | 11 | 22-pole | 0.00 | 1.00*10-3
 | 12 | 24-pole | 0.00 | 1.00*10-3
 | 13 | 26-pole | 0.00 | 1.00*10-3
 | 14 | 28-pole | 1.00*10-8 | 1.00*10-3
 | 15 | 30-pole | 0.00 | 1.00*10-3
 | 16 | 32-pole | 0.00 | 1.00*10-3
 | 17 | 34-pole | 0.00 | 1.00*10-3
 | 18 | 36-pole | 1.00*10-8 | 1.00*10-3
Sextupole, Bn/B3 @ 10 mm | 4 | 8-pole | 0.00 | 1.00*10-3
 | 5 | 10-pole | 0.00 | 1.00*10-3
 | 6 | 12-pole | 0.00 | 1.00*10-3
 | 7 | 14-pole | 0.00 | 1.00*10-3
 | 8 | 16-pole | 0.00 | 1.00*10-3
 | 9 | 18-pole | 1.00*10-6 | 1.00*10-3
 | 15 | 30-pole | 1.00*10-7 | 1.00*10-3
 | 21 | 42-pole | 1.00*10-6 | 1.00*10-3
 | 26 | 54-pole | 5.00*10-7 | 1.00*10-3
 | 33 | 66-pole | 1.00*10-7 | 1.00*10-3
 | 39 | 78-pole | 5.00*10-8 | 1.00*10-3
 | 45 | 90-pole | 1.00*10-8 | 1.00*10-3
DA & multipoles
Electron DR
Positron DR

## Slide 14
RF frequency, fRF: 2 GHz
Natural radiation loss per turn, U0: 5.7 MeV
Parasitic energy loss per turn, Up: 50 keV
Harmonic number, h: 2398
Harmonic efficiency coefficient, m: 0.8
RF voltage, VRF: 6.055 MV
Over voltage factor, q: 1.0493
RF acceptance, εRF: ±0.736 %
No essential requirement for the aperture for the DR vacuum system in view of acceptance.
10 mm residual vertical dispersion and 1.5% momentum deviation are assumed.
εi is assumed to be 10 times larger than the injected beam and the “i” indicates horizontal and vertical directions.
Acceptance
Electron DR
Positron DR

## Slide 15
In practice, the vertical emittance for a circular machine is dominated by two factors;
  residual vertical dispersion (This is caused by the coupling between longitudinal and vertical motion)
  betatron coupling (This is caused by the coupling between horizontal and vertical motion)
Magnet alignment errors are the dominant sources of vertical emittance in particular:
  tilts of the dipoles around the beam axis;
  vertical alignment errors of the quadrupoles;
  tilts of the quadrupoles around the beam axis;
  vertical alignment errors of the sextupoles.
In the rest, the impact of these errors on the vertical emittance shall be discuss.
Tuning algorithm to minimize the vertical emittance by correcting for these errors will be presented.
Vertical emittance

## Slide 16
Vertical emittance and tuning algorithm
Nominal lattice
Vertical steady state emittance
Feed expected misalignments
Correctors distribution
Orbit correction
Vertical dispersion and coupling correction
Vertical equilibrium emittance measurement

## Slide 17
=
Misalignments of magnets
Combined Dipole
Combined horizontal dipole
generated by Δx, θ
Skew quadrupole
generated by θ
Vertical dipole
generated by Δy, θ
Orth. quadrupole
generated by θ
Hor/ver dipole
generated by Δx/Δy
Quadrupole
=
Skew quadrupole
generated by θ
Sextupole
Orth. sextupole
generated by θ
Skew quadrupole
generated by Δy
Orth. quadrupole
generated by Δx
Skew sextupole
generated by θ
Ignoring Δxsinθ, Δysinθ
Ignoring Δxsinθ, Δysinθ
Ignoring Δxsinθ, Δysinθ,
ΔxΔy, Δx2, Δy2

## Slide 18
Correctors installed
242 vertical; (84 per arc, 8 per DS-I, 9 per DS-II, 20 per LSS)
262 horizontal; (84 per arc, 8 per DS-I, 9 per DS-II, 30 per LSS)
Correctors
Monitors installed
262 BPM; (84 per arc, 8 per DS-I, 9 per DS-II, 30 per LSS)
Skew quads
2 sextupole families in the arcs
Skew quads installed as windings in the sextupoles.

## Slide 19
The variation of the vertical orbit at the BPM position sj resulting from the corrector kick θi at si is expressed by;
Correction method – response matrix
Feed misalignment error
The self-consistent solution of vertical dispersion when a skew quad strength changes by Δ(kl) is
This is the response of dispersion function to a unit change in skew quad strength.
Feed misalignment error
This is the response of vertical orbit a unit change in vertical corrector strength.

## Slide 20
Accumulated histogram;
For 100 machine samples, the vertical emittance due to the dipole vertical displacement up to 100 μm is below than 0.5 pm rad.
For the case of 150 μm, vertical emittance is above 0.5 pm only for 5 machine samples.
For the case of Δy = 150 μm;
Dipole vertical offset

## Slide 21
Accumulated histogram;
Dipole roll up to 0.7 mrad is tolerable.
For the case of Δϕ = 500 μrad;
Dipole roll

## Slide 22
Accumulated histogram;
Vertical emittance is very sensitive to misalignment of quads.
Vertical emittance due to the quad vertical offset up to 20 μm is below than 1 pm rad for 99 machine samples.
To be in the goal vertical emittance region, vertical offset of the quads must be kept in ±15 μm.
For the case of Δy = 20 μm;
Quadrupole vertical offset

## Slide 23
Accumulated histogram;
For 100 machine samples, the vertical emittance up to 200 μrad quadrupole roll is below than 1 pm rad.
±100 μrad corresponding to the vertical emittance below than 0.5 pm for 100 machine samples can be achievable with the present day alignment techniques.
For the case of Δϕ = 150 μrad;
Quadrupole roll

## Slide 24
Accumulated histogram;
Vertical emittance is very sensitive to misalignment of sextupoles.
For 100 machine samples, vertical emittance due to the sextupole vertical offset up to 20 μm is below than 1 pm rad.
The vertical emittance will be kept in the goal region for 10 μm vertical offset of the sextupoles.
For the case of Δy = 25 μm;
Sextupole vertical offset

## Slide 25
Accumulated histogram;
Vertical emittance is not very sensitive to the roll of sextupole.
Up to 300 μrad, the vertical emittance is in the goal region for the 100 machine samples.
For the case of Δϕ = 250 μrad;
Sextupole roll

## Slide 26
Vertical emittance
For 95% of machine samples,
vertical emittance is below than 0.7 pm rad.
Error | Unit | Value
Dipole/quadrupole/sextupole/BPM vertical misalignment | μm | 35/20/20/50
Dipole/quadrupole/sextupole roll | μrad | 80/50/50
BPM roll | μrad | 50
BPM noise | nm | 200

## Slide 27
Closed orbit & vertical dispersion

## Slide 28
Corrector’s strength

## Slide 29
Coupling coefficients

## Slide 30
Shift of tune & chromaticity

## Slide 31
Thank you!

## Slide 32
Back up slides

## Slide 33
The IBS algorithm is based on the Bjorken and Mtingwa’s * formula.
Assumed parameters;
No. Particles:4E9
Bunch charge:0.72 nC
Vertical emittance: 0.73 pm
RF voltage=6.055 MV
Harmonic=2398
Bunch length=1.577 mm
Parameters | Without IBS | With IBS | Growth rate (%)
Natural emittance (pm.rad) | 73.752 | 89.847 | 21.823
Energy spread | 1.275E-3 | 1.303E-3 | 2.196
Bunch length (mm) | 1.577 | 1.612 | 2.194
* J.D. Bjorken, S.K. Mtingwa
Intrabeam Scattering, Part. Acc. Vol. 13, 1983, 115-143.
Calculated with ELEGANT
Intra beam scattering