## Slide 1: Summary of design studies for a possible upgrade of Diamond M. Apollonio – Diamond Light Source Ltd. Low Emittance Lattice Workshop, Lund, December 1st 2016 thanks and credits to: A. Alekou, T. Pulampong, R. Bartolini, R. P. Walker (DLS) S. Liuzzo, P. Raimondi, N. Carmignani (ESRF)
Notes: OK

## Slide 2
  Low Emittance
    From 2.7nm to <270pm
    Constraints on new machine
  Evolution of Diamond-II low emittance lattice
    Double Double Bend Achromat (DDBA)
    Double Triple Bend Achromat (DTBA)
  Where we stand
    Optimizations
    Open issues
  Summary
Outline
Notes: OK

## Slide 3
  Diamond II wish list
  Emittance: from 2.7 nm to <270pm
  Minimal changes to present machine
    Keep tunnel / beamline structure
    Leave straight sections as they are
    Re-use hardware wherever possible (RF, magnets, …)
  Keep I09-I13 optics (mini-beta sections)
  Maintain short pulse operations (low-alpha optics)
  Minimize dead-time
  Minimize technology risks
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
Notes: OK

## Slide 4
  Broadly speaking, emittance reduction is achievable with usual approach, i.e.
  Increase n. of dipoles
  Increase Jx with combined function dipoles
  MBA solutions with longitudinal gradient dipoles
  However, reducing emittance may not be the only target
  increase ratio of straight_sections / C
  This twofold request led to the Double DBA concept (DDBA)
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
Notes: OK

## Slide 5
  Double Double-Bend Achromat (DDBA)
  modification of present Diamond DBA cell
  central region “cleared” to host a new insertion device (VMX)
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
  A modified 4BA with a 10x emittance reduction factor and 2x n. of possible beamlines
  Baseline design for Diamond-II
  until the end of 2015
Notes: OK

## Slide 6
  at present one DDBA cell has been installed in Diamond and is being commissioned
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
Notes: OK

## Slide 7
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
DDBA cell installation (16/11/2016)
beam accumulation in the SR
(17/11/2016)
Beam current = 300mA
(24/11/2016)
Notes: OK

## Slide 8
  There were few reasons to go beyond the DDBA concept:
    a request from beamlines for a more aggressive scheme: 20x reduction in emittance
    Challenges in the optimization of Lifetime, Dynamic Aperture
  Point (1) led to a 6BA-like approach, where the 7BA ESRF cell (HMBA) was modified to create a central ID straight
  Collaboration with ESRF very fruitful in overcoming some design difficulties
  Emittance  140 pm
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
Notes: OK

## Slide 9
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
ESRF-HMBA
Sextupoles located at large hx dispersion bumps
Central DQ2 removed
Drift spaces kept equal
Magnet lengths shortened thanks to
reduced gradient (6GeV  3GeV)
DII-DTBA
~ (3p,p) phase advance
C2
ESRF - HMBA
E: 6 GeV
Cell lenghts: 26.4m
C: 844m (32 cells)
DII - DTBA
E: 3 GeV
Cell lenghts: 22.6m
C: 561m (24 cells)
Porting the ESRF-HMBA concept into Diamond SR:
by scaling magnet lengths while keeping the same
inter-distances
by shortening cells to fit Diamond length constraints
Parameters | DDBA | DTBA
No. of magnets(D/Q/S) Hor. Emittance Tune (H/V) Nat. chrom (H/V) Bunch length Energy spread αc Straight length (L/M/S) [m] | 4/5/10 270 pm.rad 51.21/17.31 -128/-93 2.17 mm 7.92e-04 9.96e-05 9.1/6.7/3.4 | 6/8/8 130 pm.rad 58.18/21.31 -77/-118 1.88 mm 6.82e-04 1.02e-04 8.0/5.2/3.0
Notes: OK

## Slide 10
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
There are indeed two kinds of cell, C1 and C2, used to reproduce the SP-6 structure of the present lattice (1long / 3 short straights):
-C1 C2 C2 C1
C1 is an asymmetric cell: +1.5m w.r.t. C2
Both C1/C2 cells need re-matching (see later)
ID_C
ID_B
2 x ID_A
2 x ID_A
2 x ID_A
ID_B
ID_B
ID_B
ID_C
long straight
short straight
new straight
DII-SuperPeriod
Notes: OK

## Slide 11
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
C1a/2
extra quad
D-II SuperPeriod
Notes: Q1: betax,y appear to be different from the values seen in the present VMX lattice. Is it supposed to be so? No “complaint” from BLs? CHECK WITH TP
Betax,y(I21) @ str5 = 10.0m / 5.3m Betax,y(DII-C1a)@str5 ~ 8.5m / ~2.5m
Betay @ str6 = 4.5m / 1.5m Betay(DII-C2) @str6 ~ 4m / ~2m

## Slide 12
Injection Cell
Adjust QF1-I to increase bx
Combat reduced DA@injection
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
SP-1 modified with INJ cell
Notes: OK

## Slide 13
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
DA@C2 independent from beta@injection
DA@Cinj grows with beta@injection
MA larger with no inj cell
courtesy of A. Alekou
no CINJ
no CINJ
no CINJ
Notes: ON

## Slide 14
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
Optimizing the lattice:
interplay between Linear & Non-linear dynamics
Linear optimization
  Matching technique
  Cancellation of non-linear driving terms
  Cell-length adaptation
Non-linear optimization
  MOGA
Notes: Quasi OK

## Slide 15
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
C2 matching technique imported from ESRF experience based on 5 main parameters (controlled by cell quads)
bx @ IDs
by,ay at central SF sextupoles
jx,y advance between sextupoles [3p/p]
jx,y advance in the cell
These parameters have been
kept fixed when changing cell length (HMBA  DTBA)
scanned when tuning quads during DTBA optimization (later)
C1 matching:
jx,y advance in the cell = C2 case (for symmetry)
axy @ LS = 0
hx’ @ LS = 0
(hx = 0 additional constraint for some C1 cases)
 | C1a | C1c
quads used for matching | 5 | 6
Matching params | fx=2.3833 fx=0.8458 ax = 0 / ay = 0 hx’= 0 | fx=2.3833 fx=0.8458 ax = 0 / ay = 0 hx’= 0 / hx= 0
hx @ long str. [mm] | -3.96 | 0.00
ID_C [m] | 3.586 | 3.732
Waist at ID_C | yes | no
Notes: ----- Meeting Notes (27/11/16 00:42) -----

## Slide 16
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
Cell optimization scan
Empirical finding (*) that some observed parameters (knobs) have effective impact on physically relevant quantities:
bx @ IDs  ex
by @ sext  ex, xx
ay @ sext  dQy/dAy
K4 @ oct  dQx/dAx
jy advance between sextupoles  dQx/dAy
Each parameter scanned individually while keeping others fixed
LINEAR KNOBS optimization
ex vs bx @ IDA
DA @ IDA
(*) P. Raimondi, ESRF
courtesy of A. Alekou
Notes: Confirm that each parameter is a function of quads: beta = beta(quads), alfa=alfa(quads), phi=phi(quads) ...

## Slide 17
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
LINEAR KNOBS optimization
Cell-2 MOGA optimization(*) on the whole set of parameters
(bx, by, ay, K4, jx,y)  (t,DA) [keep x=(2,2)]
Promising improvement, BUT still errors to be included
(*) 24xC2 ring
Ib = 300mA
Nb = 900
Bl = 1.71 mm
C = 1.0%
pick up solution for further optimization
courtesy of A. Alekou
With a DA of 11 mm and a lifetime of 3.2h the DTBA is a promising candidate for Diamond II.
Most of the design effort is concentrating on this lattice

## Slide 18
NON-LINEAR optimization
SP – sextupoles / octupoles
chromaticity control (2,2)
C2: SD1, SF1, SD2 / OF1
C1: SD3, SF2, SD4 / OF2
(t,DA) optimization
MOGA improvement in DA
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
courtesy of A. Alekou
Notes: SD2 is not used at all? What is it for?

## Slide 19
courtesy of A. Alekou
Injection Efficiency optimization  DTBA lattice with InjCELL
chromaticity control (2,2)
C2: SD1, SF1, SD2 / OF1
C1: SD3, SF2, SD4 / OF2
(t,DA) optimization
Cinj: SF3, SD5, SD6 / OF3
(t,IE) optimization
 IE~85%, t ~ 1.1hr
IE parameters
Npart = 1e3
Nturns = 512
ex = 150nm
InjGap = 6.8mm
C = 1%
Ib = 300mA
NON-LINEAR optimization
lattices
Low Emittance DDBA HMBA DTBA optimization conclusions
HHC cavities for bunch lengthening will be necessary
to increase Touschek lifetime
Notes: Injection Cell reduces the MA, hence the drop in LT. Higher Harmonic Cavities possible way of compensating for this effect

## Slide 20
lattices
Low Emittance DDBA HMBA DTBA open issues conclusions
Issues:
integration of present
features into new
lattice
I09 / I13 straight @ mini-b
I21 strong focussing section
Low alpha-optics
improve performance @ BL
mini-b straights critical, with low by and virtual focussing
present proposed solution under study for mini-b cases
250m
I13: coherence
imaging

## Slide 21
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
STR Q-Q: 4.88m straight section
mini-b
courtesy of T. Pulampong
Notes: Check better newer plots

## Slide 22
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
mini-b
courtesy of T. Pulampong
MA
DA
~-5.8 mm
courtesy of T. Pulampong
!
Notes: Check newest results with TP

## Slide 23
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
Initial consideration on layout, engineering
Integration, girders, beamline layout, etc.
courtesy of R. Bartolini

## Slide 24
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
Diamond is considering a development to reduce emittance by a factor 10x to 20x
Following the DDBA concept, and the expertise developed at ESRF the DTBA concept emerged, which should double the n. of beamlines
Initial studies suggest DTBA cells organized in 6-fold SP could fulfil the 20x emittance reduction
However optimization process is underway to ensure:
  Good LT/DA are achievable
  Non linearities can be controlled
  Present machine requirements are met (mini-b / low-a)

## Slide 25
Thanks for your attention