## Slide 1: Off-axis injection lattice design studies of HEPS storage ring
This work done by Physics group of HEPS
Reporter : Y. M. Peng
LERLD 2016 workshop
1-2 December 2016

## Slide 2: Outline
Introduction of HEPS present nominal design
Design goals of off-axis lattice
Design considerations
Dynamic analysis
Summary

## Slide 3: Introduction of HEPS current lattice
HEPS is a 6-GeV light source with emittance less than 0.1nm, proposed to be built in Huairou district , suburbs of Beijing ,China.
The current design is a 48-H7BA cells lattice with emittance 59.4pm.
Efficient dynamic aperture ( the particles is recognized lost when tune run across the integer & half integer resonance lines):~2.5mm in x and ~3.5mm in y.
DA is only sufficient for on-axis injection schemes.

## Slide 4: On–axis injection schemes
’ swap-out’ injection
Each injector shot replaces an existing stored bunch
DA only need accommodate the injected beam size
Requires full-charge injector
Old beam dumped or recycled
Complexity in beam dump or recycled ring
Longitudinal injection
  Can be achieved beam accumulation
  Requires large MA.
  Or a very challenging injection kicker (very narrow pulse width).
Swap-out, M. Borland, USR workshop, 2012
Swap-out, M. Borland, USR workshop, 2012
Long. Inj., M. Aiba, et al., PRST-AB,
MAX-IV
HEPS

## Slide 5: Off–axis Lattice goals
Emittance less than 100 pm at 6GeV with a circumference about 1.3km
6-m straight section for insertion devices
Vertical beta functions at IDs close to 3m in vertical
Horizontal beta functions at IDs not too large (<10m) to improve brightness
Sufficient injection aperture and a 10-m straight section for off-axis injection
typically ~10 mm for local-bump injection and ~5 mm for pulsed multipole injection
Sufficient MA for Lifetime at 200 mA

## Slide 6: Lattice design consider
To enlarge the DA, except optimizing the multipole sets, it seems necessary to increase the beta functions at the straight section.
3 parts of the design
Standard cell : H7BA , as same as the nominal design , designed with low beta functions for optimal matching of the electron and photon beam.
Injection cell: two cells neighboring are re-matched to make a high-beta section for injection.
Opposite cell (survey requirement): opposite to the high-beta straight section in the ring, with beta functions below 15 m for the convenience of installing RF cavities there

## Slide 7: Standard cell --Hybrid 7BA*
Phase advance of Δφx=3π and Δφy=π between corresponding sextupoles chosen to cancel geometrical sextupole kicks
Two octupoles were also placed in the dispersion bumps and used to reduce the detuning terms;
*: L. Farvacque et al., IPAC13, 79
Combined dipole
Longitudinal gradient dipole
Longitudinal gradient dipole
High gradient quadrupole
Dispersion bump
L=3m

## Slide 8: MOGA/PSO optimization(48-H7BA)
32 element parameters (all tunable magnet positions and strengths)
Constraints:
A reasonable maximum value of beta function along the ring, max(bx , by ) ≤ 30 m;
Reasonably low beta functions in ID section for high brightness, 1.5 m ≤ by < 4 m and 1.5 m ≤ bx < 15 m;
Stability of the optics, Tr(Mx,y) < 2, with Mx,y being the transfer matrix of the ring in the x or y plane;
Fractional tunes in (0, 0.5), which is favorable against the resistive wall instability;
Reasonable natural chromaticities, |ξx, ξy| ≤ 5.5 in one 7BA;
All drifts between adjacent magnets longer than 0.1 m;
One of the drifts neighboring the inner three dipoles should be longer than 0.35 m to accommodate a three-pole wiggler which is to be used as a hard X-ray source;
Reasonably low energy loss in each turn due to synchrotron radiation (U0 ≤ 2.2 MeV)

## Slide 9
Parameters | units | values
Circumference | m | 1295.7
Emittance | pm.rad | 60.2
Tune |  | 111.284/41.143
Natural chromaticity |  | -134.12/-137.15
Beta functions in SS | m | 7.20/3.07
Energy spread |  | 8.5827E-4
Main parameters of 48 normal cells

## Slide 10
Effective DA(H~2.4mm,V~3.7mm)
Ring acceptance projected in the (x, d) plane and the corresponding frequency map at the center of the 6-m straight section

## Slide 11: Injection cell
Add one family additional quadrupoles in each straight section.
Increase the length of long straight sections from 6m to 10m.
bx in straight section >90m, estimated value of DA in horizontal is more than 8.5mm
The straight sections have the same phase advance as the standard 6-m ones
Didn’t break the Phase advance of Δφx=3π and Δφy=π between corresponding sextupoles
The optical functions in dipole is same as the standard 6-m ones

## Slide 12: Opposite straight section
The total length is equal to the high-beta straight section
The horizontal phase advance has a 2p difference with the high-beta straight section

## Slide 13
Parameters | units | values
Circumference | m | 1317.3
Emittance | pm.rad | 60.2
Tune |  | 112.284/41.143
Natural chromaticity |  | -137.09/-140.02
Straight section | m | 6*46+10*2
Beta functions in 6 m-SS | m | 7.20/3.07
High beta in 10 m-SS | m | 90.86/5.99
Low beta in 10m-SS | m | 1.96/5.02
Energy spread |  | 8.5827E-4
Momentum compact factor |  | 3.14E-5
RF frequency | MHz | 499.8
Harmonic number |  | 2196
RF voltage | MV | 3.4
Bunch length | mm | 2.56
Main parameters of off-axis injection lattice

## Slide 14: Nonlinear analysis
  Nonlinear optimization is not done, just scaling the sextupole strengths to keep the corrected chromaticity unchanged, (+0.5, +0.5).
Effective dynamic aperture and the ring acceptance projected to (x, d) at the center of the high-beta straight section

## Slide 15: DA with error
20 seeds
1000 turns
Misalignment in girder:30μm
Misalignment between girders:100μm
Tilt :1E-4
Accuracy of BPM:0.1 μm
Integral field errors:
Quad: 2E-4
Dipole:1E-3
Sextupole:1E-3
Only correct the orbit and beta beating, not correct the dispersion and emittance y

## Slide 16: LMA and Touschek lifetime
 | t1/2 [h]
Bare Lattice | 0.65
Bare Lattice with IBS | 0.81
Bare Lattice with LC | 3.14
Bare Lattice with LC and IBS | 3.4
Bunch length with LC is about 12mm
In the calculation, the bare lattice is used, RF cavity and synchrotron radiation are turned on

## Slide 17: LMA
If the largest horizontal beta function reduced to 60 m. In this case, the DA is slightly smaller (scales as square root of beta function, ~7.4mm), but the effective MA at the dispersive region is increased to ~2%, and the Touschek lifetime for bare lattice with LC and IBS is about 7.5 hours.

## Slide 18: Summary
We have had a lattice with enough DA for off-axis injection, but the MA in dispersive region had a obvious decrease.
There is probably an ‘optimal’ value of the highest beta function to simultaneously obtain a large enough DA for off-axis injection and large enough LMA for a long enough Touschek lifetime.
We need more nonlinear optimization, maybe use local chromaticities correction in high-beta cell.

## Slide 19
Thank you for your attention!