## Slide 1: ALBA Status
Ferran Fernandez
On behalf of the Accelerator Division

## Slide 2: Outline
Introduction
Operation
Accelerator Developments
Other activities

## Slide 3: Introduction

## Slide 4
BOOSTER
100 MeV ->
3 GeV
LINAC
100 MeV
STORAGE RING
3 GeV
Parameter | Value
Energy | 3 GeV
Circumference | 268.8 m
Emittance | 4.5 nm·rad
Current | 250 mA
Rf frequency | 500 MHz
# cavities | 6
Long straights | 4 (8 m)
Medium straights | 12 (4 m)
Layout

## Slide 5
Bending: e- Diagnostics
BL04: MSPD
SCW31 – (8-50 keV)
HP/HR
Powder Diffraction
BL09: MISTRAL
Bending– (0.27-2.6 keV)
X ray Microscopy
BL11: NCD
IVU21– (6-13 keV)
Non Cristalline Diffraction
SAXS/WAXS
BL13: XALOC
IVU21 – (5-22 keV)
Macromolecular Cristallography
BL22: CLÆSS
MPW80– (2-63 keV)
Absorption &
Emission Spectroscopies
BL24: CIRCE
EU62– (0.1-2 keV)
Photoemission
spectroscopies
BL29: BOREAS
EU71– (0.08-3 keV)
REsonant Absorption
and Scattering
BL01: MIRAS
Bending – (0.4-100 µm)
IR Spectroscopy
BL20: LOREA
EUXX– (10-450 eV)
ARPES
In operation (8)
In construction (2)
BLXX: XAIRA
IVUXX (~5-25 keV)
Macromolecular Cristallography

## Slide 6
1st official user on 12 October
1st industrial signed on 17 October
New Beamlines - Miras

## Slide 7
Lorea: Angle-resolved Photoemission Spectroscopy
  The 9th BL -> procurement stage
  Schedule:
    Summer 2017 -ID, FE and vacuum chambers
    Fall 2017 -Lead hutch + infrastructure
    Beginning 2018 -Optics, end station, cabling,…
    Beginning 2019 -First user
Xaira: PX beamline with a beam spot in the micron range
  The 10th BL -> design stage
  Target: First user end 2020
ID vacuum chamber - Aug16
New Beamlines – Lorea & Xaira

## Slide 8
Chart: SUBMITTED AND GRANTED ACADEMIC PROPOSALS
| Submitted Proposals | Granted Proposals
2012 | 202 | 93
2013 | 186 | 89
2014 | 252 | 128
2015 | 337 | 187
2016 | 382 | 217
2017 (1st call) | 180 | 100
Beamtime proposals

## Slide 9: Operation
Top-up
Statistics
News
Improvements

## Slide 10
Operation – Top-up
24/7
8 Runs (4-5 weeks)
Top-up every 20min

## Slide 11
 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Accelerator operation [h] | 3280 | 4464 | 5250 | 5730 | 5744 | 5888
Scheduled user beam [h] | 2387 | 3540 | 3888 | 4320 | 4368 | 4632
Availability [%] | 76.7 | 83.8 | 96.8 | 97.3 | 97.7* | 
MTBF [h] | 21.0 | 25.0 | 33.7 | 51.4 | 59.8* | 
MTTR [h] | 1.0 | 0.8 | 1.1 | 1.4 | 1.4* | 
Chart: 
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Availability (%) | 77 | 84 | 96.8 | 97.3 | 97.7
Operation (hours) | 3280 | 4464 | 5250 | 5730 | 5744 | 5888
* Until 15 Nov
Operation - Statistics

## Slide 12
Chart: MTTR: 1.39 h
| 2012 | 2013 | 2014 | 2015 | RUN_01 | RUN_02 | RUN_03 | RUN_04 | RUN_05 | RUN_06 | RUN_07 | RUN_08
MTTR | 1 | 0.79 | 1.1 | 1.3636 | 0.8265 | 1.84 | 1.3033 | 0.91144 | 0.98562 | 3.2886 | 2.6433 | 0
cumulative results | 1 | 0.79 | 1.1 | 1.3636 | 0.83 | 1.08 | 1.13 | 1.06 | 1.0445 | 1.3 | 1.3649
Chart: MTBF: 59.8 h
| 2012 | 2013 | 2014 | 2015 | RUN_01 | RUN_02 | RUN_03 | RUN_04 | RUN_05 | RUN_06 | RUN_07 | RUN_08
MTBF | 20.75 | 24.95 | 33.7 | 51.381 | 43.9583 | 77.875 | 85.6429 | 38.9688 | 44.3077 | 66 | 199.8333 | 0
cumulative results | 20.75 | 24.95 | 33.7 | 51.381 | 44 | 52.5 | 55.3 | 50.3 | 58.6296 | 51.9 | 59.7698
Operation - Statistics

## Slide 13
BL Beamlines PSS
CT Controls
DI Diagnostics
EPS EPS interlock
ID Insertion Devices
INF Infrastructure
LI Linac
MML High Level Software (MML)
OE Human error
OI Orbit Interlock
OT Others
PM Pulsed magnets
PS Power Supplies
PSS PSS (except BLs)
RF Radio Frequency
VC Vacuum
WI Water interlocks
# events Down time [h]
During 2015, 63 events (87.4 h) with no beam for BLs
35 x Beam lost due to hardware failure
25 x FE closed (mainly for reinjection)
3 x beam killed to prevent failures (2xMIRAS + 1xPSS)
Operation – Statistics

## Slide 14
Accelerators - WEEK 35
            Installation of LOREA Al vacuum chamber and opening of RF cavities –> conditioning needed
            Problems with: RF, M1 re-centering, BO_KIEXT, BO_BEND01/02, water failure.
            Almost no accelerator tests were done
            Poor conditioning, therefore, low lifetime
            And then, UPS failure … Beam for users started 8h late
Operation - Startup

## Slide 15
Operation News – Miras Mirror
120mA

## Slide 16
sx
sy
BbB: ON OFF ON OFF ON OFF
Tests with low chromaticity
The Horizontal BbB feedback is in operation since 11th October 2016
Operation News – Bunch-by-bunch
Diamond BbB software

## Slide 17
1 BO RF plant  1 IOT
6 SR RF plants  12 IOTs
S06A
S06B
S10A
S10B
S14A
S14B
BO
5x L3 – IOTs
6x TH794 – IOTs
2x TH795 - IOTs
Spares:
2x TH794 - IOTs
1x TH795 – IOTs
ALBA SR is operating now with 12 IOTs
increasing slowly the current,
always ensuring reliability
Operation News – RF amplifiers

## Slide 18
Voltage in cavity S06 was limited due to arcs
Absorber has been replaced on 16th Nov
So far no arcs at “nominal” voltage
Operation News – RF cavity absorber

## Slide 19
Motivation: | The failure of Main Booster power supplies is responsible for the 70% of Beam time loss due to power supplies.
Identification of the failure cause: | The transition from decay mode to top-up mode increased the stress on the power semiconductors(IGBT). This stress is mainly due to the Thermal and Power cycling of power semiconductors. Another area to improve is to acquire the capacity to modify the control/regulation parts and to add more diagnostic to the power supplies.
Top up mode/ 1yr
Decay mode / 1 yr
R. Petrocelli, Electronics Group
Operation improvement – BO PC

## Slide 20
Current actions: | Increase the maintenance of power modules, replacement of power semiconductors once a year. Balancing the stress in different modules. Reducing the number of cycles by reducing the warming up of power supplies during each injection. (working on it)
Next step Actions: | Increase the number of spare modules. To use this additional modules as a test bench for a solution. Call for Tender in March 2017.
Further actions: | Refurbishment of all power supplies modules with a proven solution ( starting 2018). Improvements in control/regulation and diagnostics (starting June 2018)
R. Petrocelli, Electronics Group
Operation improvement – BO PC

## Slide 21: Accelerator Developments
Single Bunch Bucket Selection
Beamsize using interferometry
Bunch-by-Bunch Transverse Size
“Speckle” tests
… and others with no time to cover

## Slide 22
Single Bunch Bucket Selection
  Precise measurement filling pattern
  Top Up SBBS algorithm  Precise filling patterns
  (Single Bunch Bucket Selection)

## Slide 23: Beam size reconstriction using visible interferometry
Rotaring the interferometry slits
to obtain the full beam size
Coupling scan tests
L. Torino et al.
PRST-AB paper

## Slide 24: Bunch by bunch interferometry transverse beam size measurement using Fast Gated Camera
Beam size acquisition synchronised wih the bunch position
Observation of induced “bunch train” instability
MB
SB
MB
SB

## Slide 25: “Speckle” Collaboration

## Slide 26: Other Activities
International Collaborations
Magnetic Lab
RF Lab

## Slide 27: International Collaborations
CLIC-CERN
     WP1: Damping Ring Stripline Kicker test
     WP2: Collective Effects
ILSF
   Associate partner: 1% Budget & Beamtime
   PhD Collective Effects
CERN – HTS-BS-FCC
 Agreement to be signed soon
INFN - ELI-NP project
     WP1: Magnetic simulations
     WP2: BPM measurements
H2020 - ARIES – ADA
 Start date May 2017
H2020 - FCC - EuroCirCol
     WP4: Cryogenic Beam Vacuum System
     WP3: Beam Instrumentation & Diagnostics
     WP4: 1.5 GHz RF System

## Slide 28: Collaborations/Contracts
Magnetic Lab
  Elytt/LEHIPA permanent magnets quads
  CIEMAT cyclotron magnet (new magnetic bench)
  ThomX magnets
  Elytt/CLARA (STFC) dipoles
  CIEMAT – LIPAC magnets
  …
RF lab
  Test and Conditioning cyclotron cavity for CIEMAT
  Digital LLRF for DIAMOND
  …
CIEMAT Cyclotron cavity
at ALBA RF lab
ALBA magnetic bench at CIEMAT
Measureing the Cyclotron magnet

## Slide 29
Division Head
F. PEREZ
Operations
M. PONT
Operators
F.FERNANDEZ
M. ALVAREZ
O. SERRES
D. YEPEZ
E. MORALES
RF & Linac
RF
A. SALOM
B. BRAVO
J. OCAMPO
Linac
R. MUÑOZ
D. LANAIA
IDs
J. CAMPMANY
Magn Lab
J. MARCOS
V. MASSANA
Beam Physics
U. IRISO
Beam Dynamics
G. BENEDETTI
T. GÜNZEL
Z. MARTÍ
M. CARLÀ
CLIC
Diagnostics
A. OLMOS
A. NOSYCH
L. TORINO
ELI – NP
J.C GIRALDO
M. SOS
N. AYALA
R. FOS
MINECO
Z. HAZAMI
PhD
P. SOLANS
L. GARCIA MINECO
J.M. ALVAREZ
CLIC
WP4
CLIC
X. RODRIGUEZ CLIC
Accelerator Division
Thanks, to all Alba staff