## Slide 1: SLS-2 Upgrade of the Swiss Light Source
Andreas Streun on behalf of SLS-2 project team PSI Villigen, Switzerland
The SLS
   layout  achievements  upgrade summary
Low emittance lattice concept
   TME cell dilemma  longitudinal gradient bends and anti-bends
Period-12 7-BA lattice
   parameters  non-linear optimization  period 12 vs. period 3  source point shifts  straight sections  brightness
Design Progress
   instabilities  orbit & optics  vacuum  injection  superbend
Outlook
2nd workshop on low emittance ring design
Dec. 1-2, 2016, Lund, Sweden

## Slide 2: 1. The SLS
4 days
1 mA
90 keV pulsed (3 Hz) thermionic electron gun
Synchrotron (“booster”) 100 MeV  2.4 [2.7] GeV within 146 ms (~160’000 turns)
100 MeV pulsed linac
2.4 GeV storage ring ex = 5.0..6.8 nm, ey = 1..10 pm 400±1 mA beam current top-up operation
shielding walls
transfer lines
Current vs. time
Electron beam cross section in comparison to human hair

## Slide 3: SLS beam lines

## Slide 4: SLS major achievements
Reliability
  >5000 hrs user beam time per year
  97.5% availability (2005-2015 average)
    2016 (< Nov. 15): availability 99.2%, mean time between failures: 11 days
Top-up operation since 2001
  constant beam current 400-402 mA over many days
Photon beam stability < 1 mm rms (at frontends)
  ‏fast orbit feedback system ( < 100 Hz )‏
  undulator feed forward tables, beam based alignment, dynamic girder realignment , photon BPM integration etc...
Ultra-low vertical emittance: 0.9 ± 0.4 pm
  model based and model independent optics correction
  high resolution beam size monitor developments
150 fs FWHM hard X-ray source FEMTO
  laser-modulator-radiator insertion and beam line
Emittance 5 nm at 2.4 GeV  no longer state of the art
  SLS flagship applications (CXDI, Ptycho, RIXS etc.) not competitive in future?

## Slide 5: Need for a new lattice concept
Upgrade task: factor >30 lower emittance
SLS challenge: small circumference
Scaling of new ring designs to SLS upgrade:
Approximate emittance scaling ex  (Energy)2 / (Circumference)3
SLS E = 2.4 GeV C = 288 m
MAX IV E = 3 GeV C = 528 m ex = 328 pm  1290 pm
SIRIUS E = 3 GeV C = 518 m ex = 240 pm  950 pm
ESRF-EBS E = 6 GeV C = 844 m ex = 147 pm  590 pm
ALS-U E = 2 GeV C = 200 m ex = 106 pm  50 pm different concept: on-axis swap-out with additional accumulator ring
SLS-2: New lattice cell concept ex  150 pm

## Slide 6: Upgrade summary: storage ring old  new
Lattice type: 12TBA  127-BA
  longitudinal gradient bend / anti-bend cell
Emittance: 5 nm  150 pm(incl. IBS)
Circumference: 288 m  290.4 m
Periodicity: 3  12
Straight sections: 311 m, 37 m, 64 m  125½ m
3 Superbends: 2.9 T  6.0 T
maintained:
  2.4 GeV beam energy, 400 mA current
  off-axis top-up injection

## Slide 7: Upgrade summary: impact
Building: 400 m circumference
  ring tunnel: modification on 325 m length
18 Beam lines
  1 shutdown (laser beam slicing)
  3 major, 7 medium, 4 minor, 3 no modifications
  6 spaces for new beam lines
Booster synchrotron: 270 m circumference
  emittances 10/2 nm at 2.4 GeV  “SLS-2 ready” 
  booster-to-ring transferline adaptation
Storage ring RF-system:
  500 MHz, 4  ELETTRA cavity 
  3rd harmonic passive s.c. twin cavity  keep/active/new?
+ new

## Slide 8: 2. SLS-2 low emittance lattice concept
New LGB/AB cell based on
  longitudinal gradient bend (LGB) to minimize emittance
  anti-bends (AB) to provide optics matching for LGB
get low emittance with moderate optics.
  not possible with traditional TME cell !
Further emittance reduction:
increase of damping (radiation loss)
increase of horizontal damping partition (Jx)
A. Streun & A. Wrulich, Compact low emittance light sources based on longitudinal gradient bending magnets, NIM A770 (2015) 98–112
A. Streun, The anti-bend cell for ultralow emittance storage ring lattices, NIM A737 (2014) 148–154

## Slide 9
Traditional “theoretical minimum emittance” (TME)
  base cell for multi-bend achromat lattices
  minimum emittance (TME) conditions
Deviations from TME conditions
Ellipse equations for emittance
Cell phase advance
 Real cells: m < 180°  F ~ 3...6
The dilemma of the TME-cell
bx h
homogeneous bend,
length L , curvature h = 1/r
quad
quad
S. C. Leeman & A. Streun, PR ST AB 14, 030701 (2011)
d
b


## Slide 10: 1st step The longitudinal gradient bend (LGB)
h(s) = B(s)/(p/e)
Dispersion’s betatron amplitude
Orbit curvature
Longitudinal field variation h(s) to compensate H (s) variation
Curvature is source of dispersion:
Optimization of curvature h(s) :
  approx. hyperbolic field variation (for symmetric bend, dispersion suppressor is different)
  Result for ½ symmetric bend  ( L = 0.8 m, F = 8°, 2.4 GeV )
Trend: h0   , b0  0 , h0  0
homogeneous bend
optimized profile
hyperbola fit


## Slide 11: LGB optimization with optics constraints
Optimization of field profile By(s) for fixed b0, h0
  Emittance (F) vs. b0, h0 normalized to parameters for the “theoretical minimum emittance” of a homogenous bend.
F = 1
F = 2
F = 2
F = 3
F = 3
F = 1
LGB requires small (~0) dispersion at centre, but tolerates large beta function !
F  0.3
b
b
d
d
usual operating region for TME cells
135°
180°
225°
phase advance in TME cell
operating region for LGB cells
how to suppress dispersion?
Homogeneous Bending Magnet
Longitudinal Gradient Bend

## Slide 12: 2nd step The anti-bend (AB) [or reverse/inverse bend]
General problem of dispersion matching:
  dispersion production in dipoles  “defocusing”: h’’ > 0
Quadrupoles in conventional (TME) cell:
  over-focusing of beta function bx  high phase advance & chromaticity 
  insufficient focusing of dispersion h  compromise on emittance 
LGB needs h0  0  but tolerates moderate bx
 to do: disentangle h and bx
use anti-bend (AB) angle q < 0  kick Dh’ = q < 0
AB out of phase (60-80°) with LGB:  Dh’ < 0 at AB  Dh < 0 at LGB 

## Slide 13: Momentum compaction
Anti-bend  negative momentum compaction factor
small
large
negative
< 0
AB history
1980’s/90’s: proposed for isochronous rings and to increase damping - but 
PAC 1989

## Slide 14: in a nutshell  the way to minimum emittance
Increase of radiation loss  I2
LGB I2 increase for h =h(s)
AB S|bend angles| > 2p
Damping
Increase of horizontal damping partition number Jx = 1 - I4/I2
traditional (combined function): k < 0 where h > 0, h > 0
AB k > 0 where h < 0, h > 0
Damping partitioning
LGB Minimization of I5
h  0 where h  max.
AB dispersion matching:
h  0 at LGB center.
hd
h’d
x’
x
Quantum excitation
Radiation integrals

## Slide 15: SLS-2 LGB/AB-cell
bx by
Dispersion h
for q = 0.78°
for q = 0°
dipole field
quad field
total |field|
}R = 13 mm
AB TGB LGB TGB AB
5° angle, 2.48 m length
Tunes nx/y = 0.40 / 0.08
LGB angle = 4.38° longitudinal gradient bend
TGB angle = 0.31°+q transverse gradient bend (i.e combined function bend)
AB angle = q anti-bend (half quadrupole geometry)
AB-angle q 0.78° 0°
Emitt. [pm] 135 535
Damp. Jx 1.80 1.15
E- loss [keV] 7.9 5.8
MCF a [104] 2.1 +4.8
sextupoles

## Slide 16: 3. SLS-2 period-12 7-BA lattice
Arc layout (30°)
Optical functions
rms beam size  20 m  5 m in straight centers
bx by h
sx sy hse

## Slide 17: Lattice parameters
Name | SLS*) | SLS-2#)
Emittance at 2.4 GeV [pm] | 5022 | 138  150)
Lattice type | TBA | 7BA
Circumference [m] | 288.0 | 290.4
Total absolute bending angle | 360° | 585°
Working point Qx/y | 20.42 / 8.74 | 37.17 / 10.31
Natural chromaticities Cx/y | -67.0 / -19.8 | -66.4 / -40.3
Optics strain1) | 7.9 | 7.0
Momentum compaction factor [10-4 ] | 6.56 | -1.37
Radiated Power [kW] 2) | 205 | 232
rms energy spread [10-3 ] | 0.86 | 1.05  1.08)
rms bunch length [mm] | 3.73 | 2.60  8.5)
damping times x/y/E [ms] | 9.0 / 9.0 / 4.5 | 4.6 / 8.0 / 6.5
product of horiz. and vert. normalized chromaticities C/Q
assuming 400 mA stored current, bare lattice without IDs
*) SLS lattice before FEMTO installation (<2005)
#) SLS-2 with 3 superbends
) including intra-beam scattering for 1 mA bunch current (400 mA in 400 of 484 buckets; 500 MHz), 10 pm vertical emittance, 1.4 MV RF voltage, 3rd harmonic cavity for 3 bunch length.

## Slide 18: Problems with previous period-3 lattice
maintain undulator source points
  straight sections: 6  short, 3  medium, 3  split long
  no modification of (undulator) beam lines and building
  287.25 m circumference  harmonic “478¾”  479  -260 kHz
non-linear dynamics
  good beam lifetime and injection efficiency for zero chromaticity
  bad for large non-zero chromaticity
    may be required for suppression of beam instabilities
switch to period-12 geometry
  superior non-linear performance
  simpler structure, standardization
  managable modifications for beam lines and building

## Slide 19: Non-linear optimization
Variables
4 chromatic sextupole families
3 harmonic sextupole families
4 octupole families
constraint on chromaticity: -2 variables
8 variables
quadrupoles via matching knobs
Computing
64 XEON cores, typically 45 hrs
Quadrupole
Sextupole
Octupole
Longitudinal Gradient Bend
Combined Function Bend
Anti-Bend
BPM
Vertical corrector
Horizontal corrector
Method: MOGA
Objectives: dynamic acceptances at Dp/p = 0, +3, -3 %
Constraints: orbit, matrix trace, chromatic footprint, magnet strengths
 M. Ehrlichman, Genetic algorithm for chromaticity correction in diffraction limited storage rings, PR AB 19, 044001 (2016)

## Slide 20: Tune footprints period 3 and 12
chromaticities -5 for CBI-suppression ( < 0 because a < 0 ! )
chromatic and amplitude dependent tunes after MOGA
previous period-3 lattice and new period-12 lattice
Michael Ehrlichman

## Slide 21: Dynamic apertures period 3 and 12
Michael Ehrlichman
chromaticities -5: horizontal dynamic aperture vs. momentum
period-3: lifetime 0.5 h period-12: lifetime 3.9 h
( chroma 0  4.4 h ) ( chroma 0  5.3 h )
lifetime calculation parameters: 1.4 MV RF voltage for 5% RF energy acceptance, no 3rd harmonic cavity, 10 pm vertical emittance, 6D-tracking (Bmad)
2 MV  7% acceptance  lifetime 14.6 h (?)

## Slide 22: Momentum acceptance and ½-integer crossing
Touschek particle may survive crossing non-systematic ½-integer
if resonance is narrow
  optics correction: beta beat 1-2 % rms
if crossing is fast
  high local chromaticity at resonance
  high synchrotron tune
G.-M. Wang et al., IPAC-2016, THOBA01  measurements
Y. Jiao & Z. Duan, NIM A 841 (2017) 97-103  simulations
SLS-2 period-12
chroma -5
6D momentum
acceptance

## Slide 23: Source point shifts
Lattice Circumference | SLS now f6cwo 288.00 m | SLS2-period 3 dc01a 287.25 m | SLS2-period 12 db12c 290.40 m
Harmonic number | 480 = 2222235 | 479 = 479 (-260 kHz) | 484 = 221111
3  L-straight L DR DS | 11760 | 2 x 5161 0 0 [ 3030* ] | 5384 1771 0
3  M-straight L DR DS | 7000 | 5028 0 0 | 5384 -8 0
6  S-straight L DR DS | 4000 | 2897 0 0 | 5384 65 1782
3  Superbend DR arc 2,6,10 DS |  | -225 -1 | -178 -205
radial and longitudinal shifts [mm] relative to SLS-now (without Femto)
* due to splitting the L-straights
L-straight
S-straight
M-straight
Superbend
2/6/10S  longer
4/8/12S  shorter

## Slide 24: 5L straight: period-12 lattice and existing SLS girders
Lothar Schulz
Tunnel & ceiling modification at 3 long straights.
Beam lines affected have to be refurbished anyway.

## Slide 25: Straight sections

## Slide 26: Brightness
Brightness comparison per sector for the existing undulators
(SRW calculation)     SLS now
 SLS-2 period-12
- - - SLS-2 period-3
 A. Saa Hernandez, Synchrotron radiation from insertion devices at SLS-2, Internal report SLS2-Note-03-2016-10-18
Up to factor 40 higher brightness compared to SLS now.
Angela Saa Hernandez

## Slide 27: 4. Design Progress
Work well in progress, and delayed or postponed
Beam instabilities: confidence in 400 mA beam current?
  Longitudinal single and multi-bunch instabilities
  Transverse single and multi-bunch instabilities
Lattice refinement
  Girder layout, orbit and optics correction
Vacuum system
  Concept design: copper [plated] chamber
Injection schemes
  single multipole / longitudinal on-axis / anti-septum bump
Magnets
  Superbend design
  Design of normal conducting magnets and undulators
RF systems, feedback systems, diagnostics, engineering integration

## Slide 28: Single bunch longitudinal: microwave instability
~3 mA
~13 mA
Haisheng Xu
Design current 1 mA in train,
up to 5 mA in single bunch (“cam shaft”)

## Slide 29: Multi-bunch longitudinal: cavity HOMs
Stable Windows
HOMs of ELETTRA-type 500 MHz cavity used in SLS
Haisheng Xu
 HOM free windows can be found with SLS-2 conditions too (negative momentum compaction, weaker longitudinal radiation damping)

## Slide 30: Orbit and optics correction
Orbit correction: 150  BPM / CH / CV
  Orbit distortion acceptable after simulated beam based alignment.
  Error settings: 50 m girders absolute, 20 m girder joints, 20 m elements, 10 m BBA resolution, 20 bit/2 mrad corrector resolution.
  residual orbit: 40 nm rms corrector kicks: 200 (40) rad max (rms)
Optics distortion suppressed through LOCO-style optics corrections
Horizontal and vertical emittances at SLS-2 are not smaller than vertical emittance at SLS today (1..10 pm).
“SLS-2 ready” BPM electronics for SLS: 2..3  better resolution and feedback frequency. upgrade scheduled for 2015/16  delayed.
Masamitsu Aiba & Michael Böge

## Slide 31: Vacuum system
Existing SLS-girders
Super-LGB cryostat
Absorbers and pumping ports
High field bends (2 T n.c., 6 T s.c.)  antechambers.
No NEG coating.
Full copper or copper-coated stainless steel (at correctors).
Discrete pumps, e.g. NEXTorr® on CF63 flanges.
Maximum local pressure < 3 pbar after 1000 Ah of beam.
Discrete crotch absorbers, e.g. GlitCop®.
Distributed absorbers on the inner side of the anti-bend chambers.
100 l/s NEXTorr® and sputter ion pumps.
Lothar Schulz

## Slide 32: Anti-septum injection scheme
DLSR : miniaturization of components.  injection elements too!  electrostatic razor blade, pulsed anti-septum, etc.
Kicker
Septum
Anti-septum
Kicker-2
(Anti-septum)
0.5 m, -13.8 mrad
Kicker-3
0.4m 10 mrad
Kicker-1
0.15 m 3.8 mrad
Septum
(from SLS)
0.8 m, 5°,
70 ms full sine
Anti-septum wall thickness can be as thin as 1 mm:
- Short pulse (6 s, half sine)
- Stray field comes after the injection bunch passes!
Bump height = -12 mm
Anti-septum wall = 1 mm
Injection point -15...-16 mm
(separation = 3...4 mm)
Dynamic aperture  5 mm
Christopher Gough Masamitsu Aiba

## Slide 33: Longitudinal gradient super-bend
Hard X-rays & low emittance
Requirements
  hyperbolic field shape
  warm bore
  removable from beam pipe
Challenges:
  restricted space
  thin superinsulation
Concept design done
  CDR chapter written 
 Prototype fabrication
  technical design 2017
  cost estimate 400 kCHF
  company selection
Super-LGB brightness for 0.5 mrad fan opening angle and full vertical acceptance
 2.9 T at SLS(1)   5.4 T at SLS-2
- - ESRF-2 0.86 T 2-pole wiggler

## Slide 34: Superbend magnetic design
Requirements:
Necessity to evacuate the synchrotron radiation: split racetracks + solenoids.
Maximum longitudinal magnet length about 400 mm.
B-field profile full width half maximum (FWHM): 40-70 mm.
B-field peak: ≥6 T.
B-field integral (along the beam path): 0.61 T m.
Inner coils
to produce the
B-field peak
ARMCOR (better V-permendur) to enhance the field and reduce the stray field
Outer coils
to guarantee
the required
field integral
Ciro Calzolaio
Stephane Sanfilippo
Alexander Anghel
Sergei Sidorov

## Slide 35: Superbend components and parameters
LN2 vessel
LHe vessel
ARMCOR
(or V-permendur)yoke
G10/Steel Support
Pre-cooling pipe
HTS current leads
316 L yoke reinforcement
4 K
thermal connection
50 K
thermal connection
Gifford-McMahon
(or pulse tube) cryocooler
Cryostat
inner wall
 | Outer coils | Inner coils
Conductor type: | Nb-Ti | Nb3Sn (RRP)
Insulation: | Formvar | S-glass
Ic @ 4.2 K (A) | 752 @ 5T | 810 @ 12T
Magnetic energy (kJ) (1 coil) | 3.8 | 16.6
Inductance (mH) (1 coil) | 50 | 210
Current per turn (A) | 400 | 400
N. turns (1 coil) | 200 | 1485
Extraction Voltage (V) (tdamp=0.4s) | 340 | 140
Horizontal aperture (mm) |  | 53
Peak field at conductor (T) | 2.8 | 11.3
Peak temperature (K) | 4.2 | 4.3
To guarantee 8-10 hours autonomy in case of cryocooler failure.
Ciro Calzolaio
Stephane Sanfilippo
Alexander Anghel
Sergei Sidorov

## Slide 36: 5. Outlook: SLS-2 roadmap
CDR originally planned for end 2016, delayed...
rest of 2016: project plan
  define project group: responsible staff persons.
  establish (i.e. update/extend) plan: tasks & milestones.
winter 2017: set priorities to address pending critical tasks
  n.c. magnet designs.
  mechanical integration.
  complete beam instabilities study.
  tolerance studies (magnets, alignment).
  cost estimate for building modifications.
spring 2017
  review meeting ?
  proposals for 2MCHF project budget (2017-2020)
    prototypes: super bend ? injection kicker ?
summer/fall 2017: CDR editing
may affect lattice layout!
}
}
confidence in design

## Slide 37: SLS-2 accelerator project “cloud”
Beam Dynamics:
Masamitsu Aiba, Michael Böge, Michael Ehrlichman, Ángela Saá Hernández, Andreas Streun
Instabilities & impedances, and RF-systems:
Haisheng Xu, Lukas Stingelin, Micha Dehler, Paolo Craievich
Magnets:
Ciro Calzolaio, Stephane Sanphilippo, Alexander Anghel, Sergei Sidorov, Philippe Lerch, Marco Negrazus, Vjeran Vrankovic
Pulsed magnets:
Christopher Gough
Vacuum system:
Lothar Schulz, Andreas Müller, Adriano Zandonella
General concept and project organisation:
Albin Wrulich, Lenny Rivkin, Terry Garvey, Uwe Barth
THE END
Open position: post-doctoral fellow
SLS-2 design issues based on R&D at the existing SLS storage ring
Start between May 1 and Aug.1, 2017; limited to 2 years.
Application deadline Dec. 20, 2016
Info: https://www.psi.ch/pa/stellenangebote/1391
Contact: andreas.streun@psi.ch