## Slide 1: HDR Handling at EMBL-HH Status Report
Marina Nikolova

## Slide 2: Overview
Introduction
Software Set-up
  Data Acquisition
  Data Transfer Management
  Data Visualization
Infrastructure Organization
Outlook

## Slide 3: Introduction
EMBL: 3 beamlines at Petra III on the DESY campus
A pool of detectors:
  2 Pilatus 6Ms, Pilatus 2M, Pilatus1M, Eiger 4M
  Eiger 16M delivery expected end of April
TINE control system for device communication
Shutdown: January – April

## Slide 4: System Overview: Control and Data Flow
GUI
MxCuBE
Image Tracker
Adxv
Collection
Server
Grimsel
PPU
Server
Pilatus
Eiger

## Slide 5: Collection Server
TINE server
Communicates with and schedules devices involved in collection sequence:
  Detector
  Diffractometer
  Detector shield
  Energy
  Transmission
  Resolution
Pilatus or Eiger based on configuration

## Slide 6: Data Transfer Management Software
PPU TINE Server – an engine for remote script execution
  Allows execution of queued command sequences on PPUs
Pilatus
  Per user restart of DECTRIS’ furka/grimsel on (GUI) client request
  Verification of process status and data transfer DCU => PPU
Eiger
  Data download DCU => PPU on collection server request
  Parallel command-line CURL downloads via 10Gb/s connection
  Built-in download verification and multiple retries on failure
  CURL file DELETE request during collection on successful download
  Maximum download rate: 370 Eiger 4M frames/sec

## Slide 7: System for Real-Time Data Visualization
Image Tracker
  TINE Server
  Learns of files transferred (DCU => PPU) via communication with data transfer software – grimsel (Pilatus) / ppu-server (Eiger)
  Decision which frame to display next made based on a set of rules
  Command to display frame sent to adxv viewer via socket
ADXV
  New socket commands for hdf5 slab control
  -o_direct flag for fast I/O over nfs
  Fix for data type issue – yellow lines along space between modules
  Fix for crashes on opening big hdf5s

## Slide 8: Infrastructure Organization
Infiniband Storage 40 Gb/s
P13
DCU
P13
PPU
P14
DCU
P14
PPU
P13
MW
P13
UI
P14
UI
P14
MW
Processing
Processing
Processing

## Slide 9: Eiger Streaming Client
Tioga: “where it forks”/”swift current”, zmq
Tested without beam only
No dropped messages
2 10 Gb/s connections DCU  PPU
Consistent rate of ~510 frame writes/sec at 750Hz
Writes to /ramdisk of PPU
Subsequent collection blocked in arm until stream is finished
Pull Message
Bitshuffle lz4 Decompress
Write cbf
Parse out configuration (once)
all PPU CPU threads

## Slide 10: Outlook
Tioga tests with beam
Writes to storage – BGFS 7.5 GB/s
Connection to Dozor?
Connection to Image Tracker
Add pixel mask
Flatfield Correction?

## Slide 11: Acknowledgements
Gleb Bourenkov
Andrew Arvai
Stefan Fiedler
Thank you