## Slide 1
Harmonic RF project for ESRF-EBS
Lee Carver, Alessandro D’Elia, Jörn Jacob, Vincent Serrière, Simon White
HarmonLIP Workshop
MAX IV / Lund, 10-12 October 2022
Part of this work has been performed within the frame of the WP2 collaboration among ESRF, HZB, KEK, PSI & SOLEIL

## Slide 2: ESRF 1992: First 3rd generation synchrotron light source
200 MeV Linac
6 GeV Booster
6 GeV Storage Ring
200 mA
Existing Storage Ring
1992: commissioning
1994: external users
since then:
many upgrades
brilliance increase by about a factor 1000
Up to 100 keV X-rays
2020 New Extremely Brilliant Source: EBS
First 4th generation high energy light source
further brilliance increase by a factor 40
Substantial gain in coherence
Circ = 844 m

## Slide 3: EBS RF system Layout
EBS Storage Ring
NEW Teststand: in new adjacent building
KLYS 2
Cell 7
KLYS 1
Cell 5
75 kW
tower
75 kW
tower
75 kW
tower
75 kW
tower
75 kW
tower
75 kW
tower
Cell 25
-7 dB
-7 dB
Space for 4th harmonic RF system
Symmetric 3dB splitting using existing magic T’s
352 MHz 1.1 MW klystron
  ELTA/AREVA
  based on SOLEIL design

## Slide 4: Gradual implementation of 10 SSA (each 110 kW RF, max 250 kW AC)
Cell 7
KLYS 1
Cell 5
3 existing 150 kW SSAs / ELTA
KLYS 2
Space for 4th harmonic RF system
2023
2023
2024
2024
2025
2026
2026
Dec.
Keep Klystron 2 if still spare klystrons left as a unique high power RF source for the teststand
01
02
03
04
05
06
07
08
09
10
13
12
11
2026
2026
Dec.
2025
Cell 25
Klystron 1 dismounted in Autumn 2026 to free space for last 2 SSAs for cavities 04 and 05
SAT for each SSA connected to RF power teststand, switching between:
cavity in teststand and
load with variable mismatch (EH tuner)
 RF Teststand
10 new 110 kW SSAs
by JEMA France

## Slide 5: Lifetime in EBS
Threshold ~1.4mA
For all modes: Hor. Emit. z = 135 pm | Multibunch 7/8 filling | 16-bunches | 4-bunches
Total current | 200 mA | 92 mA | 40 mA
Current per bunch | 0.23 mA | 5.75 mA | 10 mA
Bunch length (calc.) | 13 ps | 31 ps | 37 ps
Vert. Emit. z set at | 10 pm | 20 pm | 20 pm
Touschek Lifetime | 33 h | 3.5 h | 2.5 h
computed, not measured
Measured MWI factor 2 lower than GdfidL computation
[S. White, N. Carmignani et al.]

## Slide 6: 4th harmonic RF system for bunch lengthening
Harmonic RF system at 1.41 GHz
    Bunch lengthening by a factor 2.5 to 3
    1st Priority for high I / bunch (16b and 4 x 10 mA)
    Reduced Touschek scattering, IBS and microwave instability:
      Increased lifetime  less frequent injections, reduced loss rate and radiation load
      Improved overall stability
      Room for smaller In-Vacuum ID gaps
      alleviate possible impact from future lattice developments like mini-beta straights
      Reduced emittance and energy blow up
    Reduced heat-load and stress of critical chambers, like ceramic chambers or In-Vacuum IDs
      Today maximum 35 mA in 16 bunch and 20 mA in 4 bunch operation until installation of new ceramic Kicker chambers
    2nd step: for multibunch operation
    Intrinsically less Touschek scattering, very low IBS, no MWI
    7/8 filling  strong transient beam loading (TBL) almost impossible to avoid
      Phase transients partly spoil bunch lengthening
      Minimize R/Q of harmonic cavities  E020 mode cavity
RF t
V [MV]
Vc = 6.0 MV
Vh,opt = 1.27 MV
Uo = 3.1 MV
Vtot
Principle: 4th harmonic RF system for bunch lengthening
E020 mode cavity initially proposed by Naoto Yamamoto / KEK

## Slide 7: 4th harmonic 2-cell E020 mode cavity – in house development
Active NC cavity design well advanced:
    2 coupled and 2 uncoupled cells considered
    Freq = 1.409 GHz
    R/Q = 44.5 ohm/cell
    Q0 = 30500
    Smart HOM & LOM dampers almost not affecting Q0 of E020 mode
    Elaborate water cooling
    Aperture coupler: coupling  = 1
    Vacuum ports on HOM dampers also preserving Q0
H-Field
454 mm
Ferrite LOM (E010 mode) & HOM absorber
[Alex D’Elia, Vincent Serrière]

## Slide 8: ACTIVE harmonic system - Power requirements
Thresholds for LCBI
HOM impedances
Main RF Voltage | Harmonic RF Voltage | 3 x 2 Harm Cav cells | 4 x 2 Harm Cav cells
6.5 MV | 1.49 MV | 46 kW | 26 kW
6.0 MV (nominal) | 1.35 MV | 38 kW | 22 kW
Optimum harmonic cavity tuning: Load angle = 0
(exactly as for main RF)

## Slide 9: Simulation with Ferrite instead of PML revealed new challenge
Replacing PML with real ferrites in the 3D model:
revealed small azimuthal modulation of fields of TM020 / -mode of coupled cells
coupling to higher order waveguide TE mode in coaxial HOM/LOM damper reaching ferrite ring
Reduction of Q by a factor 2 !
2 investigated possibilities to mitigate this problem:
H-Field penetration in the original structure
Remarks:
Additional choke to stop TE propagation
Initial RF performances recovered
Power density at the ferrite after optimization ~10W/cm2 (15W/cm2 is the limit given by the manufacturer: being checked on teststand);
Cavity slightly longer (by ~80mm in total).
Possibility 1
Ferrite Loads
Additional choke
Remarks:
1 additional HOM damper per cell to stay within LCBI threshold
Q factor ~5% lower because of the HOM dampers
Power density at the ferrite ~15W/cm2 (no optimizations done yet);
Review of mechanical integration of the disk needed
Cavity length does not change
Possibility 2
Ferrite Loads
Coupling lots moved towards cav’ axis

## Slide 10: Cell 25 with 3 main RF and 3 harmonic RF cavities
3 harmonic cavities designed to fit in remaining space of cell 25

## Slide 11: Status
Status and objectives:
    Challenging design of 4th harmonic cavity goes on:  Vincent Serrière’s presentation of latest findings
    Launch procurement of cavity and 1.4 GHz SSA hopfully early 2023, including prototype phases
    Why not 3rd harmonic at 1.057 GHz ?
      Existing 1.3…1.4 GHz SSAs was the main reason to go to 1.4 GHz fro an active system, now also high power transistors around 1 GHz
      As suggested by Patrick Marchand: we could now also envisage a 3HC system
      We would need 1.6 to 1.8 MV at 1057.11 MHz for 5.5 to 6.0 MV at 352.37 MHz,
      Cavities expected to have R/Q = 44 Ohm, Qo  40000
    Collaborations :
      Particle tracking simulations under way in a collaboration of ESRF RF and Beam Dynamics groups:  Lee Carvers’s presentation
      International exchange and bench marking  WP2 collaboration ESRF, HZB, KEK, PSI & SOLEIL, HarmonLIP
      Planned collaboration with ESRF Detector & Electronics group for the development of a fast digital RF feedback system built with ESRF FPGA controllers
    Remarks on Active vs Passive and Robinson DC  J. Jacob’s dedicated presentation
    Implementation on EBS possibly in about 3 years

## Slide 12: Many thanks for your attention