## Slide 1: Review of Simulation Tools for Harmonic Cavity Systems
Alexis Gamelin
HarmonLIP
Lund, 11-12 October 2022
Part of this work has been performed within the frame of the WP2 collaboration among ESRF, HZB, KEK, PSI and SOLEIL

## Slide 2: Warning …
If your favorite code/theory/method is not mentioned, sorry about it but it is difficult to be exhaustive ...
Please tell me about it after the talk!
the examples come from my personal (i.e. limited) experience.
I am the (main) developer of mbtrack2 so many examples are from/about mbtrack or mbtrack2.
This talk is rather partial as:

## Slide 3: Overview
Analytical methods
  Bunch profile
  Beam stability
Tracking codes
  Codes
  Physics principles
  Benchmark

## Slide 4: Bunch profile calculation
Aim: compute the equilibrium bunch profile for a given set of parameters.
There are now many analytic and semi-analytic methods to do this for active/passive harmonic cavities for an arbitrary beam filling pattern with/without additional impedance:

## Slide 5: Bunch profile calculation
Example: simple method for passive cavities and uniform beam filling (M. Venturini).
It is possible to compute the bunch profile from the total voltage of the RF system by solving a system similar to the Haïssinski equation[1]:
Define a scaled potential which depends on the bunch profile via and :
The bunch profile is then given by
FT of the bunch profile taken at
System of equation to solve numerically to find , and
For a given and , you get , and which allows you to compute the bunch profile. Finding a solution does not say anything about its stability. But if no solution exists, the beam can not be stable.

## Slide 6: Bunch profile calculation
Comments regarding more complete methods:
To consider non-uniform filling, the computation is mostly similar but it needs to take into consideration a form factor amplitude and phase for each bunch (so also additional equations for each bunch).
To consider active cavities, the total cavity voltage needs to be set a sum of the beam loading voltage and generator voltage.
Unfortunately, there are too few open-source implementation of these algorithms available on the web (that I know of …):
Elegant “haissinski” sub-program which includes passive harmonic cavities with additional impedance in uniform filling (L. Emery, M. Borland): https://ops.aps.anl.gov/manuals/elegant_latest/elegant.html
Mbtrack2 “BeamLoadingEquilibrium” class which includes any number of combination of active or passive cavities in uniform filling (A. Gamelin): https://gitlab.synchrotron-soleil.fr/PA/collective-effects/mbtrack2/-/blob/stable/mbtrack2/utilities/beamloading.py
“BunchLengthening” which includes passive harmonic cavities, BBR wake and arbitrary filling pattern (T. He): https://github.com/hetianlong-afk/BunchLengthening

## Slide 7: Bunch profile calculation
Example: benchmark against measurements and tracking code.

## Slide 8: Beam stability
Coupled bunch mode number
Number of bunches
Coupled-bunch mode instability (HOM, AC Robinson, …)
Aim: estimate beam stability for a given instability type
Usual formula
Clinchor (L. Emery): https://ops.aps.anl.gov/manuals/clinchor_V2.0/clinchor.html
Semi-analytic method based on normal mode analysis to estimate the growth rate of coupled bunch instabilities of an arbitrary filling pattern (gaps, charge variation, …)

## Slide 9: Beam stability
/ Periodic Transient Beam Loading (PTBL) instability
Aim: estimate beam stability for a given instability type
Numerical solution of the linearized Vlasov equation
Semi-analytic methods involving bunch profile calculations
Simplified expressions
M. Venturini
T. He
Quite complex and limited to uniform filling.
An open implementation is available on a sub-branch of mbtrack2 but the convergence can be quite difficult …
Using bunch profile calculations, it is often possible to estimate the PTBL instability threshold when the Haïssinski solver no longer gives continuous solution (several different solutions are found) or no convergence at all.
PTBL
stable
(A. Gamelin LER’2020)

## Slide 10: Beam stability
with higher order (synchrotron/azimuthal) modes and fast mode coupling instability
Aim: estimate beam stability for a given instability type
And a few others …
The theory assumes a purely quartic rf potential, it describes the Robinson () instabilities from dipole and quadrupole modes and the mode coupling.
The theory seems quite powerful but is mathematically complex … An open implementation of it would be very nice.

## Slide 11: Overview
Analytical methods
  Bunch profile
  Beam stability
Tracking codes
  Codes
  Physics principles
  Benchmark

## Slide 12: Multi-bunch tracking codes including beam loading
Code | Language | // | Source & Distribution | RF FB | BxB FB | Single bunch effects | Beam loading implementation
mbtrack - SOLEIL/KEK - Max IV | C | CPU | Semi-open (closed git accessible on demand) https://gitlab.com/soleil_ap/mbtrack https://bitbucket.org/fcullinan/mbtrack/src/master/ | Advance / ? | No / Yes | TD (broad band resonator) | Phasor
mbtrack2 | Python | CPU | Open https://gitlab.synchrotron-soleil.fr/PA/collective-effects/mbtrack2 | Basic | Yes | TD (wake function) | Phasor
elegant | C | CPU | Open https://ops.aps.anl.gov/manuals/elegant_latest/elegant.html | Advance | Yes | FD & TD | Phasor
BlonD | Python | CPU | Open https://blond.web.cern.ch/ | Advance | No | FD & TD | Multi-turn wake
STABLE | Matlab | GPU | Close | Basic | No | TD | Phasor
SPACE | C (?) | CPU | Close |  |  |  | 
Not mentioned in this table but also worth mentioning:
PyHeadTail (multi-bunch existing but not in the stable distribution version)
CETASIM (beam loading module in progress)
PyAT (beam loading module in progress)
Others I forgot …

## Slide 13: Beam loading using the phasor method in mbtrack
Introduction to the beam loading calculations in tracking codes using the phasor method.
Basic longitudinal equation of motion to go from turn (i-1) to turn i (one turn map) :
Usual way to include RF systems in macro-particle tracking code, what I call “ideal cavity” (no beam loading), is just a sum of n cosine (or sine) like:
But this approach can not simulate instabilities generated by the RF system or the transient beam loading …
Initial paper considering passive cavities for mbtrack:
Extension for active cavities for mbtrack/mbtrack2:
Synchrotron radiation damping and quantum excitation:

## Slide 14: Beam loading using the phasor method in mbtrack
Introduction to the beam loading calculations in tracking codes using the phasor method.
To simulate beam loading, the field in the cavity, expressed through the cavity phasor should be decomposed in two components, the generator phasor and the beam induced phasor :
The generator phasor is expressed in term of the generator voltage and phase :
The beam induced voltage is built up by the successive passages of the different particles inside the cavity. When a charged particle goes through the RF cavity, it induces a voltage :
with the cavity loss factor
The field induced by the different particles crossing the cavity between time t and time t+∆t is added to the beam voltage phasor already present in the cavity at time t:
with the cavity filling time and the phase slippage factor:
So by sorting the bunch macro-particles into bins, one can compute the beam loading phasor evolution during the passage of a bunch.
As a particle see only half of its wake, the energy change felt by the particle due to the RF system is given by:

## Slide 15: Beam loading using the phasor method in mbtrack
Phasor initialization
To speed-up calculation, it is often needed to initialize the beam phasor to its equilibrium value. It can be done either by tracking a “frozen” beam distribution or more efficiently by using approximate or exact formulas.
The formula for the exact phasor evolution of a “frozen” beam distribution over a turn of duration is given by (mbtrack2):
Comment about the multi-turn wake vs phasor implementation
The phasor formalism has the advantage that you do not need to keep the history of beam (previous beam distributions) to compute the voltage at the present turn.
This is especially important for superconducting cavities for which the filling time order of magnitude is seconds (so potentially ~100 000 turns).
The multi-turn wake implementation is not limited to resonators (and might be a bit more robust in some cases).
with
Bin number
Bunch number
Distance between bunch j and and (j+1)
Distance between two bins in bunch j
MP charge in bin k of bunch j

## Slide 16: Beam loading using the phasor method in mbtrack
Simulation set-up
How to set-up the different parameters (detuning, generator voltage and phase) to get the total “cavity” voltage and phase that you want in your active cavity ?
Set the tuning angle/detuning, can be set to optimal detuning (minimum generator power) or arbitrary:
Compute the generator power:
Compute the generator voltage and phase at resonance:
Set the generator voltage and phase:
Assuming uniform filling at beam current , but gives good enough results in most cases:

## Slide 17: Benchmark: mbtrack (N. Yamamoto)
*M. Pedrozzi, et al., SRF03 (2003) p. 91
189 ps
Phase
Length
Experimental result
“mbtrack” result
DC Robinson
mbtrack has been widely benchmarked against theory and (a bit) against experiment
Transient beam loading
AC Robinson & HOM

## Slide 18: Benchmark: mbtrack2 vs elegant
mbtrack2
elegant
Bunch n°0
Bunch n°100
Bunch n°200
Bunch n°300
Bunch n°400
Benchmark of mbtrack2 vs elegant with SOLEIL II parameters
RMS bunch length
Center of mass
SOLEIL II parameters
500 mA beam with 10 empty buckets
Using “ideal” main cavity (because I am elegant beginner …)
SC passive 4th harmonic cavity

## Slide 19: Benchmark: ALS-U with l=1 instability
Benchmark the l=1 instability / PTBL using the parameters from M. Venturini paper
mbtrack2:
Tuning angle for tracking
Only harmonic cavity w/ beam loading as no parameters for main cavity (ideal cavity)

## Slide 20: Benchmark: ALS-U with l=1 instability
Benchmark the l=1 instability / PTBL using the parameters from M. Venturini paper
mbtrack2:
Tuning angle for tracking
Turn = 4e4
Turn = 4e4
HC voltage & phase
Only harmonic cavity w/ beam loading as no parameters for main cavity (ideal cavity)

## Slide 21: Benchmark: ALS-U with l=1 instability
Comment: about noise on the filling pattern …
Using SOLEIL-II parameters (SC passive HC, ), adding some noise on the filling pattern can suppress this instability (but also reduce the achievable bunch lengthening).
I wanted to show this for the ALS-U case ( ) but I found out that the instability was still there … So be careful about this.
Add a lot of noise …

## Slide 22: Conclusions
In many cases, you need both to solve a problem!
Please, next time you write a nice piece of code, think of your colleagues and make it open-source!
Analytical methods & theory:
Many recent improvement on theory, analytic or semi-analytic methods, the field is very active!
Lack of good open-source implementation of these, in my view it is a big loss for the community …
Tracking codes:
State of the art tracking codes are now able to simulate multi and single bunch effects at the same time together with RF and bunch by bunch feedback.
Many successful benchmark against theory and other codes.
Probably need more benchmark against experimental data.

## Slide 23
Thank you for your attention!

## Slide 24: mbtrack2 examples & tutorials
Jupyter notebook available on google colab (on a web browser, nothing to install):
mbtrack2 base features:
https://colab.research.google.com/github/GamelinAl/mbtrack2_examples/blob/main/mbtrack2_demo.ipynb
dealing with RF cavities and longitudinal beam dynamics:
    https://colab.research.google.com/github/GamelinAl/mbtrack2_examples/blob/main/mbtrack2_cavity_resonator.ipynb