## Slide 1
Passive vs Active Systems, DC Robinson, DLLRF
Jörn Jacob
HarmonLIP Workshop
MAX IV / Lund, 10-12 October 2022
Part of this work has been performed within the frame of the WP2 collaboration among ESRF, HZB, KEK, PSI & SOLEIL

## Slide 2: Harmonic RF for bunch lengthening
Vacc() = Vc sin(s + ) + Vh sin(nh + n)
Optimum Working point (1st & 2nd derivatives = 0):
s =  - arcsin[ n2/(n2-1) U0/Vc ]
Vh,opt = sqrt[ Vc2/n2 - U02/(n2-1) ]
 h,opt = (1/n) arcsin[- U0 / (Vh,opt (n2-1) ]
For instance 4th harmonic RF for the ESRF:
  U0 = 2.52 MeV / turn (without ID = worst case)
  Vc = 6.0 MV
  s = 153.38 deg
  Vh,opt = 1.35 MV
  n h,opt = -7.14 deg
Principle: 4th harmonic RF system for bunch lengthening
 [rad]
V [MV]

## Slide 3: Passive NC / SC harmonic caviTY
Passive NC harmonic cavity :
    MAXIV, Solaris: 3 x 100 MHz
    ALS: 3 x 500 MHz
    BESSY: 3 x 500 MHz
  Pros:
    Simple, most economic solution
    Vh driven by the beam
    Only fres tuning to obtain desired Vh = f(Ibeam)
    Vh phase follows beam phase
    no phase tuning required
    no DC Robinson problem
  Cons:
    Low total impedance  only for high current operation
    Low Q  Vh,opt achievable if enough total current, but not h,opt :
    i.e.: cancelation of 1st derivative possible, but not 2nd derivative
    nevertheless, significant bunch lengthening achievable
    High total R/Q  Strong phase transients  R/Q
Passive SC harmonic cavity :
    SLS, Elettra: 3 x 500 MHz
    APS: 4 x 352.2 MHz, under development
    SOLEIL II: possibly
  Pros:
    Almost purely inductive,
    h = 0 close to h,opt !
    No beam power loading
    Vh,opt easily achievable down to low beam current
    Only fres tuning to obtain desired Vh = f(Ibeam)
    Vh phase follows beam phase
    no DC Robinson problem
    Note: APS project foresees power coupler to slightly load the SC cavity and achieve also h = h,opt
    Low R/Q ,  minimize phase transients
  Cons:
    Operation of SC-RF technology, Cryoplant
    Operation requires more financial and manpower resources than NC cavities
    Larger risk of down time

## Slide 4: ACTIVE NC Harmonic cavity
Active NC harmonic cavity :
    ALBA, BESSY, DESY project: 3 x 500 MHz scaling of E010 EU cavity in test at BESSY
    KEK: development of 3 x 500 MHz E020 cavity
    ESRF: development of 4 x 352.37 MHz E020 cavity
  Pros:
    Any Vh and h can easily be set for any current
    Allows bunch lengthening for high and low current / few bunch filling
    Still reasonable number of cavities
    E020 cavities: similar R/Q as SC cavities
    Real alternative to SC cavities
  Cons:
    Lacking operational experience
    DC Robinson stability needs to be addressed
    Requires high power RF amplifiers

## Slide 5: General stability
Different configurations are being evaluated by the HarmonLIP community w.r.t. stability:
    By beam tracking simulations
    When possible: by experiments on existing systems
    See other presentations
Coming slides  some considerations on:
    Robinson DC for active harmonic RF systems
    Possible active control

## Slide 6: 4th harmonic 2-cell E020 mode cavity – ESRF in house development
Active NC cavity design well advanced:
    2 coupled and 2 uncoupled cells considered
    Freq = 1.409 GHz
    R/Q = 44.5 ohm/cell
    Q0 = 30500
    Smart HOM & LOM dampers almost not affecting Q0 of E020 mode
    Elaborate water cooling
    Aperture coupler: coupling  = 1
    Vacuum ports on HOM dampers also preserving Q0
H-Field
454 mm
Ferrite LOM (E010 mode) & HOM absorber
[E020 proposed by Naoto Yamamoto, KEK
ESRF design by Alex D’Elia, Vincent Serrière]

## Slide 7: ACTIVE harmonic system - Power requirements
Thresholds for LCBI
HOM impedances
Main RF Voltage | Harmonic RF Voltage | 3 x 2 Harm Cav cells | 4 x 2 Harm Cav cells
6.5 MV | 1.49 MV | 46 kW | 26 kW
6.0 MV (nominal) | 1.35 MV | 38 kW | 22 kW
Optimum harmonic cavity tuning: Load angle = 0
(exactly as for main RF)

## Slide 8: Beam loading diagram with harmonic cavity for bunch lengthening
Vacc() = Vc sin(s + ) + Vh sin(nh + n)
Optimum Working point (1st & 2nd derivatives = 0):
s =  - arcsin[ n2/(n2-1) U0/Vc ]
Vh,opt = sqrt[ Vc2/n2 - U02/(n2-1) ]
 h,opt = (1/n) arcsin[- U0 / (Vh,opt (n2-1) ]
Optimum tuning (min power)  load angle = 0:
 such that Vgr // Vc
h such that Vghr // Vh
Beware, in the vector diagram:
Main RF turns at  = t
Harmonic RF at n = nt
-
-
h
h
Ibeam
Vbr
Vb
Vgr
Vg
Vghr
Vgh
Vh
VC
gh = /2 – n h
-nh
 harm = n gh
Vbh
Vbhr
s

n

h

## Slide 9: Robinson DC (2nd type) – Integration of synchrotron equation
Assumptions:
RF loops (Amp, Phi, tuning | slower than | Synchrotron motion | slower than | Cavity Bandwidths (main & HC)
B  1 Hz | << | fs  1 kHz … | << | Above  40 kHz

  Tuning angles, generator amplitudes and phases are constant at the scale of the synchrotron motion
  The beam induced voltages in the cavities follow the beam phase
    fs = frf x sqrt [  K’ / (2 h E0/e) ], (K’<0  DC Robinson instability)
    K’ = -Vc cos s - nVh cos(nh) + Vb sin  + nVbh sin h (Eq. 1)
> 0
Main RF, giving fs0
< 0
Harm. RF, for cancelling fs
< 0
Main RF
beam loading
(Robinson term)
> 0
Harm. RF,
beam loading
(Stabilizing effect)

## Slide 10
Coming examples already shown
at
ESLS RF meeting at SOLEIL in November 2018
Computed for 3rd harmonic RF system
(and not for actual 4th harmonic project)

## Slide 11: Robinson DC (2nd type) – Integration of synchrotron equation
Numerical integration of synchrotron equation:
  Uniform filling (no transients)
  Starting with beam phase offset by +1 or -1 deg
  Tracking Vb, Vbh and beam turn by turn
  Checking convergence (neglecting synchrotron oscillation damping)
  No linearization !
Vh = Vh,opt = 1.89 MV
nh = nh,opt = -12.2 deg
5 cavities, h = 1
 stable
Eq. 1
← Numerical integration

## Slide 12: Robinson DC (2nd type) – Integration of synchrotron equation
Vh = Vh,opt = 1.89 MV
nh = nh,opt = -12.2 deg
5 cavities, h = 2
 Unstable for Ibeam > 0
Eq. 1
Start with
beam = +1 deg
Start with
beam = -1 deg
Only for negative beam phases: stabilization through non-linearity of voltage waveform
Equilibrium for  100 mA

## Slide 13: Robinson DC (2nd type) – Integration of synchrotron equation
Vh = 1.80 MV ( Vh,opt )
nh = nh,opt = -12.2 deg
5 cavities, h = 2
 Unstable for Ibeam > 150 mA
Eq. 1
Start with
beam = +1 deg
Start with
beam = -1 deg
Threshold at  150 mA confirmed by numerical integration

## Slide 14: Robinson DC (2nd type) – Integration of synchrotron equation
Vh = 1.50 MV ( Vh,opt )
nh = nh,opt = -12.2 deg
5 cavities, h = 5
 Unstable for Ibeam > 130 mA
Eq. 1
Start with
beam = +1 deg
Threshold at  130 mA confirmed by numerical integration
For active system, Integration of synchrotron equation indicates:
Robinson stable if Harmonic RF beam loading > Main RF beam loading
  Sufficient harmonic cavity impedance,
  Sufficient number of harmonic cavities
  Upper limit for coupling h

## Slide 15: Direct RF Feedback
Analog RF feedback on MAIN RF system:
  Gain G
  Impedance for coherent in phase longitudinal beam motion reduced by factor 1/G
  Reduction of Robinson term in Eq. 1 by a factor 1/G
    fs = frf x sqrt [  K’ / (2 h E0/e) ], (K’<0  DC Robinson instability)
    K’ = -Vc cos s - nVh cos(nh) + Vb sin  / G + nVbh sin h (Eq. 1)
> 0
Main RF, giving fs0
< 0
Harm. RF, for cancelling fs
< 0
Main RF
beam loading
(Robinson term)
> 0
Harm. RF,
beam loading
(Stabilizing effect)

## Slide 16: DLLRF system for FAST Digital RF Feedback
  To stabilize main RF, one can compute the optimum correction for a fast RF feedback:
        =
    where , ), ( = Load angle, mostly zero)
  Alternative: simulate behaviour of a passive cavity
   Feedback harmonic voltage phase to lock on beam phase
  Results of synchrotron equation integration need to be cross-checked with particle tracking simulations
  The two RF feedback approaches need to be included in the simulations and checked

## Slide 17: Many thanks for your attention