## Slide 1: The VSR Demo Project
Helmholtz Zentrum Berlin
Adolfo Velez Saiz
12.10.2022
HarmonLIP
MAXIV, Lund

## Slide 2
The SR BESSY II is a 1.7 GeV synchrotron radiation source operating for 20 years in Berlin
BESSY II emits extremely brilliant photon pulses ranging from the long wave terahertz region to hard X rays
Pioneer in offering low α operation with a comunity of user performing dynamic measurements in „functional materials“
Nevertheless BESSY II has passed ist halve life and needs to be renewed to be competitive among other light sources
BESSY III
The context

## Slide 3
New generation light sources move in the direction of minimizing beam emmitance
Complete new ring
New magnet/vacumm system
Long dark time (1 year ESRF)
Very expensive (100sM€)
Long pulses needed
BUT ...
Short pulse experiments (1ps) represent one of the strong fields at HZB (low-Alpha, femtoslicing)
Such a pitty to lose the stablished community!
DLSR by multi-bend achromats (MBA)
Lifetime problems

## Slide 4
The VSR Concept
Limited pulse length in storage ring
Hardware (RF cavities)
At high current beam becomes unstable
  For ps pulses, flux is reduced by nearly 100
BESSY II @ present
1
10
10−4
10−3
10−2
10−1
1
10
0.1
Bunch current (mA)
RMS bunch length (ps)
Low alpha
User optics
Low alpha optics
Ith roughly proportional to V´rf σ2
100 × more voltage gradient
User optics
  Supply short pulses down to 1.5 ps
    100× more bunch current
  Low α permits few 100 fs
  Could we configure BESSY VSR so 1.5 ps and 15 ps bunches can be supplied simultaneously for maximum flexibility and flux?!!
Machine optics

## Slide 5
Long and short bunches simultaneously
Voltage / MV
Time [ ns ]
BESSY VSR
Long Bunch
Short Bunch

## Slide 6
High gradient SRF cavities + High Current
20 MV/m in continuous wave (CW)
High current, 300 mA
  Particulate free vacuum in a “dirty”machine
  Transparent “parking” of cavities
  Higher-order modes in SRF systems in relation to beam spectrum
  Very strong damping of HOMs
  Sufficiently strong bunch-by-bunch feedback to suppress instabilities
Coupled-bunch instabilities
Trans. beam loading & Robinson instabilities
  RF and tuning control for the cavities
  Choice of BW and available RF power
  Changing bunch profile along bunch train
Technical realization
  Integration in a single straight (4.2m)
  Cryogenic installation
  Required infrastructure for system development and tests
BESSY VSR, a great challenge

## Slide 7
Challenges
High current (300mA)
CW operation
High gradients (20MV/m)
Few cavity systems with high HOM damping capabilities
+
Very demanding impedance budget (Z
Short straight = 4m (low β), compact cavities, damping integrated
Not State of the Art
New methods and components to be developed
BESSY VSR Demo
Validate the technology by SRF R&D
2 x 1.5 GHZ cryomodule to be commissioned in bERLinPro/SEALab
Several components commissioned with beam in BESSY II (CSB, beam-pipe absorbers …)
Cavities, couplers, etc, commissioned in SUPRALAB
Module ready for BEAM at BESSY/SEALab
VSR Demo for BESSY VSR,a preparatory phase

## Slide 8
Collimating Shielded bellow. Disipates synchroton light impacting on surface avoiding module quenching by losses. Novel component!
High current highly damped SRF cavities, novel component! Tailore bunch length by applying high field gradients. In the mean time disipate unwanted high order power by means of HOM loaded waveguides
High order mode waveguides/loads. Unwanted power is transported through waveguide arms to cooled ceramics for disipation. Transition from 2K (cavity) to room temperature. Challenging design.
Blade tuner. Streches the cavity to control the operation frequency. Critical component for operation. Operational forces must be optimized so no damage is induced in the cavities.
High power couplers.
Throw RF power into the cavities to maintain volgae and ensure control. Challenging component. Connects cavity vacuum to the outside. Failure could imply contamination
Beam vacuum:
Needs to be ultra-clean.
Any dust particulate could cause
Malfunction and
Quenching
(operation down)
X 10 Units
X 2 Units
X 2 Units
X 2 Units
1 Unit
VSR Demo

## Slide 9
Damping HOM modes
Beam dynamics calculations on VSR show extreme HOM damping level required to avoid coupled bunch instabilities (CBI‘s)
  5e4 Ω, longitudinal modes
  1e7 Ω/m, transverse modes
A few cavity/damping concepts available are able to cope both with high current and high gradient
VSR requires a very compact cavity system (4.2 max. module length)
Very High HOM power expected (1.5KW per cavity)
  2e5 Ω, longitudinal
  2e7 Ω/m, transverse
The state of the art at this point was not mature enough to fulfill the VSR impedance requirements
JLAB High current CW cavity
Ib =100 mA
V=20 MV
Eacc=20MV/m
Waveguide damping seem a good starting point
  Waveguides can transport high power levels
  Reduce the risk of dust contamination (loads far from the cavity)
  „In principle„ easy to design (well defined cut-off frequencies)
Which cavity

## Slide 10
Enlarged beam-tubes (as used by bERLinPro)
  5e4 Ω, long. modes
  1e7 Ω/m, trans. modes
Beam pipe cut off is reduced (2.4 GHz to 1.7GHz)
Modified WG aspect ratio
f = 2.755 GHz TM Dipole
A.Velez et al. WEPMA013
IPAC15
A.Velez et al. MOPP071, LINAC‘14
Standard WG to extended WG
H>W/2 (50mm  60mm)
Coupling to waveguides is enhanced (also propagation through beam pipes)
Some mode bands such as TE011 are not affected
Propagation in WG is defined by orientation of H
Same cavity modes result into ortogonal orientations Inside WGs
Impedance Budget (R/Q*Q)
Optimizing the cavity, impedance budget

## Slide 11
Impedance on multicell cavities
A price is to be paid when increasing total gradient ufortunately …

## Slide 12
8
Monopole Band
 | Frequency [GHz] | R/Q [Ω] | Qext | Mode Type
1 | 1.49866 | 386 | 5.00∙107 | π
2 | 1.49134 | 0.41 | 2.98∙107 | 2π/3
3 | 1.47424 | 0.09 | 4.74∙107 | π/2
4 | 1.45785 | 0.05 | 1.60∙108 | 2π
Optimizing the cavity
Impedance budget below threshold!!

## Slide 13
= /(c 2 Qloaded) ,
Bunch 4mm
Bunch 9mm
Pole-fitting gives quantitative estimate on the resonances of the system (Mode type undefined)
For the fundamental mode Qext=5e7 should be used, because the wake length 20m is too short to extract such high Qext
The search for best fit is done manually, it depends on frequency range & filter settings in the algorithm
Pole fitting is a fast estimate of the resonances in the system (low resolution)
Eigenmode analyses is required (High resolution).
At high frequencies >4GHz is very time consuming
& requires huge hardware resources
Developing numerical methods

## Slide 14
Spectrally Weighted with “Baseline” pattern
During cavity design additional to standard parameters (peak fields, field flatness …), HOM spectrum should be controlled to avoid any resonances with circulating beam harmonics
Both cavities are not hitting any of beam resonances that are multiple of 250MHz
Wakefield Simulations (CST)
To minimize HOM power Cavity resonant eigenfrequencies must avoid beam harmonics!!!
More than 1KW per cavity!
HOM Damping

## Slide 15
Wakefield Simulations (CST)
To minimize HOM power Cavity resonant eigenfrequencies must avoid beam harmonics!!!
More than 4KW in total!
Spectrally Weighted with “Baseline” pattern
HOM Damping

## Slide 16
Tuning unwanted HOMs
Cavities must be designed so that dangerous HOM modes lay far apart from synchrotron harmonics to avoid beam loss
Standard technique is limited to a few GHz due to eigenmode limitations

## Slide 17
60-80K
5K
2K
Water-cooled HOM loads (room temperature 300K)
Specifications: 460W per load
Design, fabrication and tests @ JLab
Risk of a local quench: Superconducting region transitions above Tc (9.2K)
and superconductivity is lost
Damping unwanted HOMs

## Slide 18
High current highly damped SRF cavities, novel component! Tailore bunch length by applying high field gradients. In the mean time disipate unwanted high order power by means of HOM loaded waveguides
High order mode waveguides/loads. Unwanted power is transported through waveguide arms to cooled ceramics for disipation. Transition from 2K (cavity) to room temperature. Challenging design.
X 10 Units
X 2 Units
VSR Demo

## Slide 19
Since we are working in a synchroton we expect Synchrotron Light
89 W !!!
Courtesy of H.W.Glock
Collateral damage, synchrotron light

## Slide 20
Collimating Shielded bellow. Disipates synchroton light impacting on surface avoiding module quenching by losses. Novel component!
1 Unit
VSR Demo

## Slide 21
Impedance issues? Is the beam stable?
Particulates? Are we going to Quench?
Of course the community (specially SRF) was concerned …
Collimating shielded bellow (CSB)

## Slide 22
Collimated Shielded Bellow (CSB) as critical component to BESSY VSR successfully commissioned with beam at BESSY II (350mA)
First Fundamental Power Coupler prototypes fabricated at Research Instruments (RI)
SRF cavity fabrication in full swing at RI
SRF Cryomodule fabrication running
CSB Installed in BESSY T2 Straight
Close view on CSB
Impedance computed for beam excited CSB
Beam Tests

## Slide 23: Prototyping and testing
Single cell 1.5 GHz
5-cell cold model 1.5 GHz
VSR Blade tuners
4-cell VSR 1.5 GHz
4-cell VSR 1.5 GHz
16KW FPC VSR 1.5 GHz
ALL to be TESTED @ SUPRALAB HZB
VSR 1.5 GHz FPC

## Slide 24
Testing infrastructure

## Slide 25
Technical Infrastructure building
BESSY II
High-bay
building
view north-west
LN2
storage
SeaLab (former bERLinPro)
Testing infrastructure

## Slide 26
Thank you for your kind attention
Tack för din vänliga uppmärksamhet
Muchas gracias por su atencion