## Slide 2: Control system deployment and monitoring
ESS-MAX IV collaboration workshop
PRESENTED BY Anders Lindh Olsson

## Slide 3
Controls Ecosystem

## Slide 4: Controls Ecosystem
Purpose
Provide support for building, operating, and maintaining the control system at the European Spallation Source ERIC

## Slide 5: Controls Ecosystem
Architecture
  Client-server
    Microservices behind API gateway
  Web interface
    Singular for all services
  REST API with protected endpoints
    Authentication and authorisation
  Use of tools with high degree of maintainability
    Preference for open-source libraries

## Slide 6: Controls Ecosystem
Integrations
  Ping† (access management)
  GitLab (devops platform)
  AWX (ansible task engine)
  CSEntry/Netbox (network and device configuration)
  Prometheus (monitoring system and time-series database)
  ChannelFinder (EPICS record directory service)
  Grafana Loki (log aggregation)
  ENOVIA† (“CHESS”; product lifecycle manager)
  † not yet integrated

## Slide 7: Controls Ecosystem
Indirect integrations
Through the previously listed integrations, we can also access information about
  IOC configuration
  Dependencies (e.g. ESS’ EPICS environment – e3 – packages)
  (Record) data archival
  Autosave save-sets (recovery of set values upon reboot)
  Artifactory (binary storage)
  Conserver (attach to IOC consoles)
  And more

## Slide 8
Deployment

## Slide 9: Deployment
”Thin” control system processes
In EPICS, our control system is built up out of Input-Output Controllers (IOC)
At ESS, our IOC processes are run in containers and as system daemons
  Same binary everywhere (softIocPVA)
  Functionality comes from EPICS modules, which essentially act as plugins
We try to split our IOCs if there are no hard dependencies to simplify maintenance
  Smaller units to update, separate log streams and metrics, etc.
Our IOCs are basically defined by small text files (10s of rows)

## Slide 10: Deployment
IOC-hosts, IOC types, and IOC deployment
We can then run any number of IOCs on a given host (which will be virtual unless there are non-ethernet hardware dependencies)
  We try to divide IOCs between so-called IOC-hosts according to location or domain
Since we have high multiplicity for some systems, we have generic IOC types that then are instantiated; for example, a timing receiver has a common definition which is instantiated over a 100 times
Ansible is the solution used for host configuration, and is consequently also used to deploy IOCs onto hosts

## Slide 11
Monitoring

## Slide 12: Monitoring
Health
Monitoring software looking for certain metrics
  For host machines
    CPU, memory, etc.
  For software controllers
    CPU, memory, etc.
    Whether it has been modified locally, if there are local files, etc.
Log streams
  IOC log

## Slide 13: Monitoring
Auditing
We also log all remote actions
  Session log (who did what locally)
  Write log (who did what remotely)
All IOCs are version controlled, and all previous deployments and remote start/stop actions are logged

## Slide 14: Monitoring
Metadata and relationships
The ecosystem is still under development, but we have plans to also be able to display relationships
  To other IOCs
  To systems and subsystems
as well as to simplify access of related metadata
  Documentation (requirements, manuals, operational details)
  Hardware details

## Slide 15: DEMO

## Slide 16: WORKSHOP

## Slide 17: Workshop
Instructions
We will divide into four separate groups, one per topic
For each group, please assign one person to take notes
This same person will at the end of the session present on the group’s findings
Schedule:
  09.30 Start of workshop
  10.30 COFFEE BREAK
  10.40 Continuation of workshop
  11.30 Group presentations
  12.00 LUNCH

## Slide 18: Workshop
Topics
  What would an “ideal” deployment and monitoring system do for us? What are the three most important characteristics/features?
  Describe a scenario where comprehensive monitoring of control system can prevent loss of beam time. What are the capabilities that allows us to keep the machine running when it would otherwise have stopped?
  What does this group consider to be “industry best practises” regarding deployment of controls systems? What about monitoring?
  What monitoring, alarm, and notification capabilities should be available to be reactive when it comes to issues in the control system?