## Slide 2: Automatic Fault Identification and Recording in the CERN accelerator complex
Michi Hostettler, Anti asko, Jean-Charles dumont, Lukas Felsberger, Jack Heron, Piotr skowronski, Matteo Solfaroli, Eric Veyrunes

## Slide 3: Outline
introduction: down the accelerator chain
automatic fault detection & recording
diagnostics & fault identification
statistics, consolidation & maintenance
conclusions

## Slide 4
introduction down the CERN accelerator chain
1

## Slide 5: the CERN accelerator complex
it is a supply chain!

## Slide 6: the CERN accelerator complex
it is a supply chain!

## Slide 7: the CERN accelerator complex
it is a supply chain!
equipment fault

## Slide 8: the CERN accelerator complex
it is a supply chain!
equipment fault

## Slide 9: down the accelerator complex
the larger the machine, the higher the stakes
longer cycle times = longer downtime after a fault
higher beam energy = higher damage potential
PSB
1.2s
2 GeV
PS
1.2 - 3.6s
26 GeV
SPS
10 - 20s
450 GeV
LHC
2 - 24h
6800 GeV

## Slide 10: down the accelerator complex
the larger the machine, the higher the stakes
equipment in fault
recovery
fault
production
turn-around

## Slide 11
fault detection & recording
2

## Slide 12: fault detection
what has failed, and what impact it has on the beam?
failure of a critical system ➜ beam interlock
    Beam Interlock System (BIS): hardware interlock fast (μs), connected to the most critical systems
    Software Interlock System (SIS): software interlock slow (s), monitoring more but less critical conditions
failure of an “optional” system ➜ beam degradation
    monitoring is important!
    different alarm systems in the CERN accelerator complex
      LASER: individual systems actively raising alarms
      Big Sister: SIS like surveillance system to detect non-critical problems – raises alarms instead of generating interlocks
      LHC Announcer: audible warnings, speech synthesis
“orbit corrector fault on beam 2”

## Slide 13: fault recording
keeping track
CERN Accelerator Fault Tracking tool (AFT)
    what failed? when?
    what downtime did it cause?
fault recording mostly automated
    automatic fault recording logic in every accelerator
      detect a fault is present (no beam, or degraded beam)
      identify the system or equipment in fault
      open a fault in AFT
      detect the end of fault ➜ close the fault in AFT
    ➜ improve data quality (no faults missed!)
    weekly working group: review of recorded faults
LHC 2023: 66% of all faults recorded automatically in AFT

## Slide 14: fault recording
keeping track

## Slide 15: fault tracking through the complex
“no beam from injectors”
AFR operational
AFR possible long-term
AFR passive
No AFT
PSB
ISOLDE
PS
East Area
AD
ELENA
N_TOF
SPS
North Area
Awake
HiRadMat
Linac4
LHC
upstream faults block downstream machines
    need to identify root cause for fault recording!
    automatic fault recording instances expose status
    downstream machines link faults upstream
      find the first machine in the chain with a fault
experimental areas: “passive” fault recording
    fully dependent on next upstream machine
    e.g. East Area from PS, North Area from SPS

## Slide 16: fault tracking through the complex
“no beam from injectors”
special case: LHC
    very long cycle!
    once beams are in, independent from injector complex (for > 10 h if all goes well)
    keep (even degraded) beams if injector complex is down
    record fault only if beam is requested and a fault is present in the injector complex
      LHC beams only produced on request
      request not made if a known fault is present in injectors
      ➜ ”best-effort” detection: LHC at pre-injection and no local fault
Comments (30-May-2024 12:23:46)
**Stable beams**
We will try to keep this fill as long
as possible

## Slide 17
fault identification & diagnostics
3

## Slide 18: fault identification
post-mortem diagnostics
interlock(s) triggered ➜ why?
    initial interlock may be transient
    more interlocks may appear as a consequence
    need to understand the first trigger and why it fired
re-try and watch the event sequence online?
    commonly done in injector complex – not always easy!
    LHC: too costly due to > 2h cycle time
LHC: post-mortem system
    sequence of interlocks triggered
    circular buffers of key systems data, frozen at trigger

## Slide 19: putting it all together
from detection to identification to recording
Automatic Fault Recording
Accelerator Fault Tracking (AFT) database
Post Mortem System
BIS (Beam Interlock System)
SIS (Software Interlock System)
Equipment
Equipment
Equipment
Automatic Fault Recording of upstream injectors

## Slide 20: system dependencies
the obvious fault may not be the root cause
TOTEM (movable devices close to the beam) interlock!
… but why ATLAS_AFP (similar system) triggered as well?
TOTEM interlock

## Slide 21: system dependencies
the obvious fault may not be the root cause
TOTEM/AFP interlocks depend on the beam size (β*)
TOTEM interlock
that explains the interlock of both TOTEM and AFP: but why did β* jump to 0 for one second?
β* = 30cm – as expected
β* = 0 ???
β* publication

## Slide 22: system dependencies
the obvious fault may not be the root cause
TOTEM interlock
β* is reconstructed from magnet currents by SIS and distributed through the timing system
β* publication
ERROR BetaStarValueConditionExtImpl => No data for : RPHSA.RR53.RQ7.L5B1_DATA ERROR BetaStarValueConditionExtImpl => Error - b* computation not valid or data out of range IR5
SIS lost subscriptions for magnet currents from power converters, connection drop: network issue?
lost current subscriptions

## Slide 23: system dependencies
the obvious fault may not be the root cause
TOTEM interlock
β* publication
lost current subscriptions
[…]
We believe that that the switch port 33 is the root cause, in the coming hours we will patch the outlet 3319/05 on a different switch port.
[…]
faulty network switch port
after further investigation: problem traced to a faulty network switch port

## Slide 24
statistics, consolidation & maintenance
4

## Slide 25: fault statistics
availability by facility
Facility | ’16-‘18 Overall [%] | ’21/’22 Overall [%] | ’23 Overall [%] | ‘24 up to June [%]
LINAC2 | 98.5 |  |  | 
LINAC4 |  | 96.7/97.1 | 98.0 | 95.7
PSB | 95.3 | 94.4/95.1 | 96.1 | 94.4
PS | 87.6 | 88.6/88.7 | 91.6 | 90.6
SPS | 82.4 | 74.5/73.3 | 86.4 | 85.9
LHC | 80.8 | 63.9 * | 57.7 * | 73
cumulative availability
* dominated by a few long, major events
general availability steady - improving
    ‘21/’22: re-commissioning after long shutdown (‘19-’21)
    LHC ‘22/’23: dominated by single “black swan” events
      2024 looks good so far!
downstream fault propagation clearly visible
    faults in early machines affect the entire complex!
    high (>95%) availability of early machines is key
    these are not new machines!
      PS from 1959, PSB from 1972
      maintenance and consolidation is crucial to keep availability

## Slide 26: impact on LHC luminosity yield
availability matters!
Chart: Integrated Luminosity in ATLAS/CMS [fb-1]
100 fb-1: 2024 target
60% availability
70% availability
80% availability

## Slide 27: fault statistics
availability by system
fault statistics by system possible thanks to rigorous tracking in AFT
fault time attributed to the root cause, not the consequences
    e.g. magnet quench ➜ loss of cryogenics: fault time assigned to magnets

## Slide 28: fault-tracking culture
statistics are there to help, not to blame
fault statistics by facility / system are not to blame!
    understand why some systems fail more often than others
      intrinsic complexity?
      ageing? maintenance?
      need for consolidation?
    emphasize what can be improved for the future
      … not what went wrong in the past
fault tracking data: foundation for future developments
    e.g. automated analyses, predictive maintenance
    reliable automatic recording important for data quality
Availability

## Slide 29
conclusions
5

## Slide 30: conclusions & outlook
CERN accelerator complex: a beam production chain
    each machine depends on its injectors
    faults early in the chain can bring the complex down
faults detected & recorded automatically
    fault detection: ensure machines are protected
    fault recording: identify the root cause (equipment, upstream machine, ..) and record fault
    important diagnostics: what failed in which sequence (post-mortem system)
    focus on getting the majority of faults recorded correctly: there is always an unexpected case!
outcome: reliable fault statistics by root cause and system
    crucial input for consolidation efforts!
    foundation for future developments: preventive maintenance, fault prediction, …

## Slide 31
spare slides
42

## Slide 32: 2023 in context
Fault duration:
long faults: dominant for run 3
faults < 1 day: stable ~16%
thanks to the continuous effort of the equipment groups!