## Slide 1: Minimizing Fault Troubleshooting Time by Linking Equipment Protection Faults to Part Replacement
Charles Peters
25 June 2024

## Slide 2: The SNS Produces Short High Power Beam Pulses for Neutron Production
Injection
Linac
Ring
To Target
Current (mA)
Linac Beam Pulse
Pulse length (msec)
Current (A)
Pulse length (nsec)
Nick Evans
PARAMETERS
33 kW per pulse
60 Hz repetition rate
2.0 MW beam power
5000 production hours
H- to 1.3 GeV
1.6x1014
protons

## Slide 3: Sponsor Deliverables are Beam Availability and Operating Hours
High beam power makes Beam Reliability difficult
  A lot of sensitive interlocks to the Machine Protection System (MPS) to prevent damage from beam loss
Focus on Beam Availability to maximum operating hours
  Redundancy and spares
  Predictive and preventive maintenance
  Keep beam trips short
*FY18, 22, 23 operating hours reduced due to extended maintenance outages for upgrade installation

## Slide 4: Downtimes > 1 day Dictate Beam Availability
Errant beam, magnet ps
SCL RF cavity trips
DTL/CCL RF cavity trips
Requires tech expert or repair (call-in)

## Slide 5
Most trips >1 day come from single point failures with limited access for maintenance and repair
Clear investment should be made to minimize the probability of target failures

## Slide 6: Minimize Recovery Time for Shorter Trips
Errant beam, magnet ps
SCL RF cavity trips
DTL/CCL RF cavity trips
Requires tech expert or repair (call-in)

## Slide 7: Benefits of Linking First Fault to Action Taken
Goal is to link a downtime to a solution instantly
  Operators know the history without searching
    Average time to repair
    Probability of
      Needing an expert
      Part replacement
      Which part to replace
System | First Fault | Trips in last year | Trips in last month | Trips in last week | Trips in last day | Max downtime (hours) | Average downtime (hours) | Min downtime (hours) | Action code (operator reset) | Action code (expert reset) | Action code (expert repair) | Highest mode part replacement
SCL_HPRF_XMTR27_fault | FF: Cathode 3 Over Current | 25 | 5 | 2 | 1 | 8 | 0.5 | 0.4 | 92% | 7% | 1% | CPI Klystron Model XYZ
Date | System | First Fault | Downtime (hours) | Action code | Part replaced
15 June 2024 034535 | SCL_HPRF_XMTR27_fault | FF: Cathode 3 Over Current | 0.48 | Operator Reset | No
1 June 2024 130516 | SCL_HPRF_XMTR27_fault | FF: Cathode 3 Over Current | 0.42 | Operator Reset | No
22 May 2024 092150 | SCL_HPRF_XMTR27_fault | FF: Cathode 3 Over Current | 0.45 | Operator Reset | No
Last 3 trips

## Slide 8: Tools Used to Track System Reliability and Availability
EPICS – Experimental Physics and Industrial Control System
  The accelerator control system is the data feed for Asset Performance Management (APM) software
E-log – Electronic logbook
  How accelerator operations tracks changes to just about anything!!
  Minimal standardization
Need standardization!
OAS – Operations Administration System
  How accelerator operations tracks system downtime
  Some standardization
EAM – Enterprise Asset Management
  Computerized Maintenance Management System (CMMS) technical personnel document preventive and corrective maintenance on systems, positions, and assets
  Some standardization
System
Subsystem
Downtime
Fault Code

## Slide 9: Machine Protection System (MPS) EPICS PVs Build the EAM System Hierarchy
MPS EPICS Process Variables (PVs) are nicely named to help provide a way to define the EAM System and Position hierarchy
Beam control system
MPS
RF Cavities (124)
Klystrons (38)
Klystron power supplies (18)
Magnets (432)
Vacuum (46)
Diagnostics (435)
Misc (51)
DTL_LLRF:HPM1
…
DTL_HPRF:XMTR1
…
DTL_HPRF:MOD1
…
DTL_MAG:PS_DCH01
…
DTL_VAC:SGV01
…
DTL_DIAG:BLM130
…
TGT_MPS:PLC1
…
The PV breakdown also makes first fault logic simple
Example for RF
  Cavity, Klystron, Klystron power supply, Diagnostic, Vacuum = Klystron
  Cavity, Klystron power supply, Diagnostic, Vacuum = Klystron Power Supply
  Cavity, Diagnostic = Cavity

## Slide 10: Equipment First Fault EPICS PVs Build the EAM Failure Codes
Failure code creation is easy with systems with first fault software
Complication comes from each MPS equipment breakdown not having first fault software
RF Cavities (124)
Klystrons (38)
Klystron power supplies (18)
Magnets (432)
Vacuum (46)
Diagnostics (435)
Misc (51)
Klystron First Fault
EAM
Highest trip frequency systems have no first fault software
Working on it!

## Slide 11: Fault Response Currently 11 Steps (5.5 manual)
EPICS Production State PV
Monitor MPS EPICS PVs
Monitor Beam Power on Target
Recover Equipment
Recover Beam
Log Downtime
Close Work Order
Beam Power on Target = 0 kW
Log Signals and Create Work Order
Scan MPS EPICS PVs and Determine Cause
Determine Equipment First Fault
Automated Steps
Operator Manual Steps
RECOVER
RESPOND
MONITOR
Expert Manual Steps

## Slide 12: Future Fault Response 14 Steps (5.5 manual)
EPICS Production State PV
Monitor MPS EPICS PVs
Monitor Equipment First Fault EPICS PVs
Monitor Beam Power on Target
Recover Equipment
Recover Beam
Log Downtime
Enter Action Code (Operator Reset Expert Reset Expert Repair)
Add Parts to Work Order
Close Work Order
Beam Power on Target = 0 kW
Determine Equipment First Fault
Log Signals and Create Work Order
Scan MPS EPICS PVs and Determine Cause
RECOVER
RESPOND
MONITOR
Automated Steps
Operator Manual Steps
Expert Manual Steps
👍
👍
👍
👍
👍
👍
👍
👍
👍
👍
👍
👍
👎
👎
Notes: Library of standard work orders based on system equipment first fault

## Slide 13: Making Progress with Asset Management Upgrade Project in FY22
Goals are to utilize Enterprise Asset Management (EAM) to:
  Record labor and parts cost to maintain systems required for neutron production
  Track parts inventory
  Provide trend data to become more predictive
Help with budget planning
Free up engineer/tech time
Determine where to focus resources
Take data to understand needs
Adapt the software to meet needs
Add ability to record labor time
Add parts into the system by group
Establish and utilize centralized maintenance inventory
Step 1
Step 2
FY22-FY23
FY21
FY24 and beyond
Utilize data to improve maintenance processes
Continue to adapt software to meet needs and continue to utilize centralized inventory
Step 3

## Slide 14: Bottlenecks on Keeping Inventory Current
Experts don’t want to do inventory (it’s not fun)
  Just order more when preventive maintenance is due or when they use the last part
Experts don’t want to move parts to central inventory
  Worried they won’t get their parts back promptly so they continue to hoard in their shops
  Perception central inventory doesn’t have the space
A spreadsheet is way easier than dealing with the EAM application for maintaining inventory
Vertical Lift Module

## Slide 15: Current and Future Plans
Write the first fault software for RF cavities and magnets
Continue to build trust with technicians and mechanics
  Go into the field to experience their issues and fix them
  Work with central inventory and willing groups to develop processes for keeping EAM inventories updated
Simplify the interface to EAM
  Moving toward an SNS homegrown version of CERN EAM Light (SNS EAM Lighter Than Light)
    Let individual group planners easily update their inventory
      Updates are screened before being pushed to EAM
    Simplify part additions to work orders
      Using the as-built application there are too many button clicks to swap a part
      Focus on barcode scanners
        Previous attempts were slowed by IT requirements
LAST THING IS TO BE PATIENT!

## Slide 16
THANK YOU
QUESTIONS?

## Slide 17
Front End Systems Group
Baoxi Han
Electrical Power Conversion Group
Yugang Tan
RF Systems Group
John Moss
Controls Integration Group
Klemen Vodopivec
CF and Vacuum Group
Derrick Williams
Cryogenics and Target Group
Aaron Coleman
Electrical Support Group
Ben Cagley
Accelerator Operations Group
Geoff Milanovich
Integration and Planning Group
Charles Peters
Protection Systems Group
Kelly Mahoney
Target Systems Group
Jeffrey Saunders
Cooling Systems Group
Ben Goddard
Target Operations Group
John Denison
Mechanical Support Group
Doug Engle
Vacuum Systems Group
Jeremy Price
Research Accelerator Division
Fulvia Pilat, Director
Accelerator Systems Section
Sang-ho Kim
Beam Instrumentation Group
Sasha Aleksandrov
Accelerator Physics Group
Nick Evans
Mechanical Engineering Group
Charlotte Barbier
Superconducting Linac Group
Matt Howell
Accelerator Science and Technology Section
Sarah Cousineau
Control Systems Section
Karen White
Operations, Integration, and Maintenance Section
Glen Johns
Target and Mechanical Systems Section
Mike Dayton

## Slide 18
Availability and reliability statistics at ISIS and at other high-power proton accelerators
J.W.G. Thomason, S.A. Fisher, D.J. Adams, M.G. Glover, J. Ranner, D.J.S. Findlay ∗ ISIS, Rutherford Appleton Laboratory, Chilton, Oxon. OX11 0QH, UK
Nuclear Inst. and Methods in Physics Research, A 1053 (2023) 168338
120 kW
160 kW
1 MW capable
80 kW
1.3 MW
1.4 MW
Notes: This plot was put together by personnel from the ISIS neutron source in the UK. It shows the number of beam trips per day on the y-axis (log scale) binned by length of trip on the x-axis for various accelerator driven sources from around the world. They show a power law fit to the data for estimating beam trips per day by length of trip.
Pretty clear that the focus for the different types of accelerators is on trips lasting more than a minute (availability and I’ll show why), but here at SNS we do focus on even shorter length trips because we understand these short trips can be indications of potential longer failures in the future.