## Slide 2: Towards safe and reliable Neural Network controllers
CERN Industrial Control Systems group (BE-ICS)
Borja Fernández Adiego (CERN BE-ICS) Borja.Fernandez.Adiego@cern.ch
Ignacio D. Lopez-Miguel (TU Wien university)
Xaver Eugen Fink (CERN BE-ICS)
Thanapong Sommart (Osaka University)
Enrique Blanco Viñuela (CERN BE-ICS)

## Slide 3: Context
CERN
Cryogenics plants
Cooling and ventilation systems
Images from cds.cern.ch
Superconducting magnet test benches
LHC
(Large Hadron Collider)
Access and protection systems

## Slide 4: Context
Machine learning at CERN
Images from cds.cern.ch
Robotics
Data analysis of the physics experiments
Particle accelerators Operation and beam optimization
Industrial controls

## Slide 5: Context
Machine learning at CERN
Images from cds.cern.ch
Robotics
Particle accelerators Operation and beam optimization
Industrial controls
P. Arpaia, et al. “Machine learning for beam dynamics studies at the CERN Large Hadron Collider.” Nuclear Instruments and Methods in Physics Research Volume 985, 1 January 2021, 164652
Ghawash, Faiq, et al. "Approximate Model Predictive Control of Switched Affine Systems using Multitask Learning with Safety and Stability Guarantees. 62nd IEEE Conference on Decision and Control (CDC), December 2023"
Kain, Verena, et al. “Sample-efficient reinforcement learning for CERN accelerator control.” Physical Review Accelerators and Beams 23.12 (2020): 124801

## Slide 6: Motivation
Can we trust Neural Networks for critical applications?
And Neural Network controllers?
Neural network improves efficiency/cost
Difficult to predict the behavior in all situations
Accelerator downtime
Equipment damage
Environmental pollution
Reputation loss
Personnel safety
Financial loss
In general, software failures in controls can have significant negative consequences

## Slide 7: Roadmap
Why neural-network based controllers
Formal verification of neural-network based controllers
  Formal methods introduction
  Standards and state of the art for verification of NNs
Case study at CERN (our first steps)
Conclusions and future

## Slide 8
Why NN-based controllers?
… instead of “traditional” controllers

## Slide 9: Why NN-based controllers?
Many applications
Tasks hard to specify
Autonomous driving
Computationally fast
Matrix multiplication
Versatile
Non-linearities
No need to linearize
Only data needed
No physical modelling required
Collect data
Pisarov, Jelena & Mester, Gyula. (2020). The Future of Autonomous Vehicles. FME Transactions. 49. 29-35. 10.5937/fme2101029P.
Several rule exceptions
Rare but critical events
Changes in the environment
NN (controller)
System/
Plant

## Slide 10: Challenges NN-based controllers?
A few challenges to solve
Data as specification:
Does the data accurately represent the intended behavior in all scenarios?
How to demonstrate coverage?
Which KIPs/metrics can be used?
…
Model uncertainty and explainability:
Lack of generalization and robustness (residual errors) due to insufficient training data
Prediction uncertainty
…
From Keynote Talk at the NASA Formal Methods Symposium by Professor Simon Burton
https://conf.researchr.org/home/nfm-2024#program
“Safety under uncertainty: Automotive standards for AI safety and research perspectives”

## Slide 11: Standards for NNs?
What about AI for critical applications?
ISO/IEC 24029-2:2023: Artificial intelligence (AI) - Assessment of the robustness of neural networks - Part 2: Methodology for the use of formal methods
Extensions to Functional Safety standards. ISO 26262 and ISO 21448 with ISO PAS 8800: Road vehicles – Safety and Artificial intelligence https://www.iso.org/standard/83303.html (in progress)
(?) Aerospace industry is also pushing to extend standards like DO-178C (Software Considerations in Airborne Systems and Equipment Certification) to assess AI reliability by using formal methods (See NFM 2024 program https://conf.researchr.org/home/nfm-2024#program)
Functional safety standards like IEC 61508 recommend the use of formal methods
Formal methods and NNs

## Slide 12
Formal Methods
How to produce reliable software?
Ariane-5 satellite rocket accident
(June 1996)
US$370 million
Software bug
https://www.youtube.com/watch?v=5tJPXYA0Nec
Therac-25 Radiation Overdosing
(1985-1987)
6 cases of overdoses (3 of them died)
Software bug
https://www.youtube.com/watch?v=41Gv-zzICIQ

## Slide 13: Formal methods
… and formal verification (e.g. model checking)
Techniques based on mathematics and formal logic (precise semantics)
Petri nets, automata, …
init
l1
l2
l3
in>10
out1  False
out1  True
in≤10
out2  True
out2  False
l0
in  IntNonDet()
Graphical languages
Petri net
Automata
MACHINE
Switch
SETS
STATE = {closed, open}
VARIABLES
state
INVARIANT
state : STATE
INITIALISATION
state := open
OPERATIONS
toggle =
IF state = open
THEN
state := closed
ELSE
state := open
END ;
END
B-method, VDM, TLA+,…
Textual languages
B-method
Mathematical languages
Temporal logic, propositional logic, Z notation,…
Temporal
logic
Propositional
logic
Model of the system
Model checking
(a formal verification technique)
Formalization of the specification properties
Model checking

## Slide 14: Formal Verification
Formal verification vs Testing
If “Input1”, “Input2”, “Input3” and “Input4” are BOOL, then we need to check 24 = 16 combinations
If they are INT (16-bit), then 216*4 ≈ 1.8*1019 combinations
for large systems (many variables), such requirements cannot (practically) be checked by using testing techniques
Peer reviews and testing can (normally) catch most of the “problems” (e.g. code bugs), but not the corner cases
Input2
Input3
Input4
Output1
Output2
Controller
software
Functionality requirement
If Input1 is False, then Output1 is False
Safety requirement
If Output1 is False, then Output2 is True
Solution: Model checking
Sensors
Actuators
Input1
Model of control software (e.g., automata)
Formalize the requirement (e.g., temporal logic)
Explore all combinations in the model to find a violation of the requirements
Model Checking lectures (RWTH Aachen university) https://www.youtube.com/watch?v=Y5Hg4MvUXc4&list=PLwabKnOFhE38C0o6z_bhlF_uOUlblDTjh

## Slide 15: Formal methods and verification
in industry
15
Formal specification
Formal verification
Using TLA+ to create a clear and concise specification, leading to a subsequent code reduction https://cacm.acm.org/magazines/2015/4/184701-how-amazon-web-services-uses-formal-methods/fulltext
Verification of neural-network-based control systems in non-towered airports to avoid collisions at landing
https://www.researchgate.net/publication/356096882_Formal_Analysis_of_Neural_Network-Based_Systems_in_the_Aircraft_Domain
Integration of their static analyser INFER into their software development process https://www.inf.ed.ac.uk/teaching/courses/sp/2019/lecs/distefano-scaling-2019.pdf
NASA AMES Robust Software Engineering group
https://www.nasa.gov/isd-robust-software-engineering
Use of the model checker SPIN to verify the model of a software
http://spinroot.com/gerard/pdf/spin04.pdf
Use of the formal specification language VDM to specify industrial applications https://www.researchgate.net/publication/2879682_The_IFAD_VDM-SL_toolbox
Formal Verification of Critical Aerospace Software https://hal.archives-ouvertes.fr/hal-01184099/document
Correctness, Modelling and Performance of Aerospace Systems
http://www.compass-toolset.org
And many more …

## Slide 16: Formal verification at CERN
… of PLC programs (PLCverif tool)
16
PLCverif

## Slide 17: Formal verification
… of PLC programs at CERN (PLCverif tool)
17
https://gitlab.com/plcverif-oss/
PLCverif

## Slide 18
Formal verification of Neural Networks
Any tool available?
https://sites.google.com/view/vnn2023

## Slide 19: Formal verification of NNs
State of the art (not exhaustive)
Tool | method
alpha-beta CROWN | linear bound propagation and the branch and bound method for adversarial search
nnenum | zonotopes for over-approximation and geometric path enumeration for efficiently splitting ReLU networks
VeriNet | symbolic interval propagation and a branch-and-bound-based method
T. Sommart summer internship report at CERN https://cds.cern.ch/record/2867415
Check VNN competition (since 2020) https://sites.google.com/view/vnn2023
Many research initiatives (for example check NASA Formal Methods 2024 symposium)

## Slide 20: Formal verification of NNs
Which properties should we verify?
Monotonicity
Safety
Robustness
Input
Output
Safe region
Image
Noise
↑ Temperature → ↑ Fan speed
Is it possible that a given situation ever occurs?
Is there a combination of inputs that leads to a given output?
Explainability
Dangerous curve to the right
+ noise
Children crossing
Reachability
Time
System’s output
Input
Output
Stability
Time
System’s output

## Slide 21: Formal verification of NNs
General approach (user perspective)
(declare-const X_0 Real)
(declare-const X_1 Real)
(declare-const X_2 Real)
(declare-const Y_0 Real)
(declare-const Y_1 Real)
(declare-const Y_2 Real)
(assert (>= X_0 20.0))
(assert (<= X_0 25.0))
(assert (>= X_1 23))
(assert (<= X_1 27))
(assert (>= X_2 8.0))
(assert (<= X_2 21.0))
(assert (>= Y_2 Y_0))
(assert (>= Y_2 Y_1))
NN Model
(*ONNX Format)
Result
(SAT / UNSAT)
Specification
(VNNLIB Format)
NN Verifier
e.g. nnenum

Property OK

Property failed
Trace leading to the violation
* Open Neural Network exchange
NN model
Specification
(list of properties)

## Slide 22: Formal verification of NNs at CERN
Where are we?
Previous experience in formal methods applied to PLC programs (since ~ 2013)
Case study in 2023: Verification of NN controller for LHC Cooling Tower
Evaluation of existing NN-verification tools by summer student in 2023
Ignacio D. Lopez-Miguel et al. “Verification of Neural Networks Meets PLC Code: An LHC Cooling Tower Control System at CERN”.
In EANN 2023: Engineering Applications of Neural Networks conference https://link.springer.com/chapter/10.1007/978-3-031-34204-2_35
Thanapong Sommart report. “Formal Verification of Neural Networks”. https://cds.cern.ch/record/2867415
~ 20 publications related to this project + PLCverif tool

## Slide 23
CERN case study
LHC cooling towers

## Slide 24: CERN case study
LHC cooling towers control
Induced draft cooling towers (IDCTs)
Provide cold water for different LHC subsystems (e.g. cryogenics, chillers, air handling units, etc.)
Control actions:
  Mode selection:
    Ventilation
    Showering
    Bypass
  Fan speed
Control objective:
  Keep outlet water temperature within strict limits
  Utilize minimum amount of energy
NN fan
NN mode
common
classification
regression
IDCT
NN
Model predictive controller (MPC)
Ghawash, F., Hovd, M., Schofield, B.: Model predictive control of induced draft
cooling towers in a large scale cooling plant. IFAC-PapersOnLine 55(7), 161–167
(2022) https://www.sciencedirect.com/science/article/pii/S2405896322008394
Neural Network controller
The idea was replacing the MPC by a NN
But the NN is NOT DEPLOYED YET!!

## Slide 25: CERN case study
NN on a PLC
Why NN on PLCs?
Widely used in the process industry
Hardware robustness
Communication capabilities
Modularity
Simple to be programmed
NN on PLC code (structured control language)
Siemens S7-1200
Neural network will be implemented in a PLC (Programmable Logic Controller)

## Slide 26: CERN case study
LHC cooling towers control
Feedforward NN with ReLU and SoftMax activation functions
Developed and trained with Python Keras
Automatically translated to S7-1200 Siemens PLC Structured Control Language (SCL)
Initial non-conventional NN architecture
Input set
Output set
Regression
problem
Classification
problem
Hidden layers
ReLU
ReLU
ReLU
ReLU
ReLU
ReLU
Softmax
+bias
+bias
+bias
+bias
ReLU
+bias
+bias
+bias

## Slide 27: CERN case study
How to verify these properties?
Different methods were applied and compared:
nnenum: an open-source NN verification tool for ReLU NNs from Stony Brook University https://github.com/stanleybak/nnenum
Z3: an open-source theorem prover from Microsoft Research https://github.com/Z3Prover/z3
PLCverif: an open-source formal verification tool for PLC programs from CERN https://gitlab.com/plcverif-oss
Testing: traditional testing techniques
NN design
PLC source code
Executable
Ignacio D. Lopez-Miguel et al. “Verification of Neural Networks Meets PLC Code: An LHC Cooling Tower Control System at CERN”. In EANN 2023: Engineering Applications of Neural Networks conference https://link.springer.com/chapter/10.1007/978-3-031-34204-2_35

## Slide 28: CERN case study
Some properties to be verified
Operational modes reachability
Ventilation
Showering
Bypass
Input1
Input2
Input3
Do these inputs exist?
They help to better understanding the NN
Temperature
Monotonicity
Fan speed
Do exist such that ?
They represent problems
Find an example that satisfies where
a set of such that
Inputs (temperatures)
Range of the inputs:
Property to verify:
(declare-const X_0 Real)
(declare-const X_1 Real)
(declare-const X_2 Real)
(declare-const Y_0 Real)
(declare-const Y_1 Real)
(declare-const Y_2 Real)
(assert (>= X_0 20.0))
(assert (<= X_0 25.0))
(assert (>= X_1 23))
(assert (<= X_1 27))
(assert (>= X_2 8.0))
(assert (<= X_2 21.0))
(assert (>= Y_0 Y_1))
(assert (>= Y_0 Y_2))
Outputs (op. modes)
Property encoding (vnnlib)

## Slide 29
Conclusions and future
Formal methods and formal verification

## Slide 30: Conclusions and future
Formal verification of NN-based controllers
Formal methods and verification are now widely used in critical industries for software (recommended by standards)
Formal verification of NNs is a (relatively) new research trend
  There are still many challenges to overcome
  However, the existence of tools, guidelines from IEC and ISO, and critical industries are pushing towards the goal of designing “Safe Neural Networks controllers“
In general, it is mportant to verify NN-based controllers to:
  guarantee properties such as robustness, stability, safety, etc.
  have a better understanding of the behaviour of the NN
Our plans – PhD in formal verification of NNs (starting Sept. 2024):
  How to specify complex properties?
  Verification capabilities and performance
  Repair/train/explain when finding a violation
  Robust neural network training

## Slide 31: Conclusions and future
Not only formal verification for NN controllers
NN design
Source code
Executable
Runtime monitoring
Testing
NN design verification
NN-based controllers
Code synthesis
Formal verification (model checking)
Compositional verification
Counterexample analysis