## Slide 1: ESP32 microcontrollers
Sofia Bukreeva,
research engineer

## Slide 2: Primary goal
To have some solution for various tasks which are not reasonable to implement with PLC, PandaBox, Electrometer, etc.
Flexible
Scalable
Easy-to-use
2

## Slide 3: What we have: ESP32-POE-ISO board
Made by Olimex company.
Easy to start
Small and cheap
Power over Ethernet
General serial interfaces like SPI, I2C, UART
12 GPIOs (+4 input only)
Bluetooth/Wi-Fi
USB-UART for flashing the firmware/communicating/powering
3

## Slide 4
ESP32-D0WD-V3
SoC
ESP32-WROOM-32E Module
ESP32-POE-ISO
Board
What is ESP32:
4

## Slide 5
*No Flash/PSRAM
ESP32 module
What is ESP32:
ESP32 SoC
5

## Slide 6
Wireless connectivity (Wi-Fi, Bluetooth)
32-bit dual-core Xtensa LX6, 240 MHz
Ethernet MAC, CAN-compatible controller (TWAI)
UART, SPI, I2C, I2S, 12-bit ADC, 8-bit DAC…
520 KB SRAM, 448 KB ROM
28 GPIOs (but only 26 in ESP32 module) and +6 reserved for Flash
Low price 1-2 Euro per chip
What is ESP32:
6

## Slide 7
Open-source ESP-IDF
Espressif IDE
Supported by Arduino IDE
Extensions for VS Code, Eclipse
What is ESP32:
IoT Development Framework
7

## Slide 8
Minimum longevity commitment for ESP32 is
15 years starting from 2016.
Xtensa 32-bit LX7 dual/single-core, up to 240 MHz
RISC-V 32-bit single-core, up to 160 MHz
What is ESP32:
8

## Slide 9: Current situation
~10 ESP32-POE-ISO boards are spread at the facility within a couple of months.
Used at beamlines for reading sensors and simple logic implementation.
9

## Slide 10: Two ways of designing
New task
Specific ESP32 firmware
Specific Tango Device
New task
Generic ESP32 firmware
Generic Tango Device
10

## Slide 11: Main points
Settings can be sent with JSON messages over MQTT
Protocol - to be implemented on ESP32 and Tango Device
ESP32 firmware upgrade via OTA
FreeRTOS (for using two cores, at least)
To standardize the approach in the end.
11

## Slide 12: Considerations (ESP32-POE-ISO)
Might need more GPIO and level shifters
Might need external power
No JTAG on the board
Might need to make our own board
Or find similar on the market
Might need to change microcontroller at all
12

## Slide 13: Plan
13
To make a plan…
Choose IDE
Choose module or board
Test software features which are available
Start developing protocol

## Slide 15: Links
ESP32-POE-ISO board
ESP32-POE-ISO - Open Source Hardware Board (olimex.com)
ESP32 datasheet
esp32_datasheet_en.pdf (espressif.com)
ESP32 technical manual
esp32_technical_reference_manual_en.pdf (espressif.com)
ESP32-WROOM-32E datasheet
esp32-wroom-32e_esp32-wroom-32ue_datasheet_en.pdf (espressif.com)