## Slide 1: MAX IV linear accelerator
Workshop on Full Energy Linacs – March 2026
Erik Mansten
Introduction

## Slide 2: Full energy?
LINAC

## Slide 3: MAX IV presentations
LINAC
Injection – Sara Thorin
State Machine – Filip Persson
RF Systems – Dionis Kumbaro
Timing – Oliver Grimm
Cooling – Piotr Dziurdzia

## Slide 4: MAX IV news - 2016
 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Linac building |  |  |  |  |  |  |  | 
Linac installation |  |  |  |  |  |  |  | 
Linac commissioning |  |  |  |  |  |  |  | 
Linac operation |  |  |  |  |  |  |  | 
Notes: 2017 and on
RF upgrade
SXL
Reliable injection into R1 and R3
SPF operation

## Slide 5: The MAX IV facility
LINAC

## Slide 6: MAX IV linac overview
Thermionic RF gun
Photo cathode RF gun
BC1 @ 260 MeV
Extraction 1.5 GeV
Photo cathode RF gun
Extraction 3 GeV
Full energy injection and top up
Injection | 
Energy | 1.5 GeV/ 3GeV
Repetition rate | 10 Hz
Charge | 0.3 nC/shot
Emittance | 5 mm mrad
Energy spread | <0.25 %
BC2 @ 3 GeV

## Slide 7: MAX IV linac overview
Thermionic RF gun
Photo cathode RF gun
BC1 @ 260 MeV
Extraction 1.5 GeV
High brightness driver for the Short Pulse Facility
 | Design | Currently
Energy | 3GeV | 3 GeV
Repetition rate | 100 Hz | 10 Hz
Charge | 100 pC | 75-150 pC
Bunch length (FWHM) | 100 fs | 300 fs – 30 fs
Emittance | 1 mm mrad | 2 mm mrad
Energy spread | <0.4% | 0.15-0.07%
Extraction 3 GeV
SPF
Full energy injection and top
BC2 @ 3 GeV
Injection | 
Energy | 1.5 GeV/ 3GeV
Repetition rate | 10 Hz
Charge | 0.3 nC/shot
Emittance | 5 mm mrad
Energy spread | <0.25 %

## Slide 8: Compression, linearization and stability
Photo cathode RF gun
BC1 @ 260 MeV
BC2 @ 3 GeV
SPF
t
E
φ
Δt
ΔE
E0
Δt
ΔE
E0
Notes: As an introduction I will briefly discuss two options for bunch compression and linearization.
In this cartoon the yeallow field represents integrated energy gain as a function of phase or time.
The black pat of the curve shows the electron bunch energy bofore compression.
Through the bunch compresors the linear momentum compaction R56 makes the til catch up with the head resulting in a shorter bunch.
Without linearization the curvature of the filed remains.

## Slide 9: Compression and linearization
t
E
φ
Δt
ΔE
E0
Δt
ΔE
E0
t
E
φ
Δt
ΔE
E0
Δt
ΔE
E0
Chicane type bunch compression
R56<0
Pre crest acceleration
T566>0
Linearize with harmonic cavity
Harmonic non-linearized tuning
Arc type bunch compressor
R56>0
Post crest acceleration
T566>0
Magnetic linearization
Magnetic non-linear tuning
Notes: There are two main types of bunch compressors chicane like and arc like.
Chicane like compressors have a negative R56 and operate with acceleration phases pre crest.
A harmonic cavity is needed to linearize.
Arc like compressors have a positive R56 and operate at post crest phases.
I will later show you that this gives some advantages for stability.
Linearization in arcs can be done by magnetic tuning of the quadratic momentum compaction T566.

## Slide 10: Linearization scan – Longitudinal phase space
E
E
E
-0.1
0.1
0
t [ps]
0.4
0.2
-0.2
-0.4
0
ΔE/E [%]
-0.1
0.1
0
t [ps]
0.4
0.2
-0.2
-0.4
0
ΔE/E [%]
-0.1
0.1
0
t [ps]
0.4
0.2
-0.2
-0.4
0
ΔE/E [%]

## Slide 11: Shortest bunch measured
3.4 fs
Notes: To access the temporal reolution we combine a measured beam profile with RF off with a scan where we change the phase between the deflecting field and the electron beam and measure how the centroid moves as a function of phase.
The blue dots in the scatter plot is the raw data and the red line is a linear fit.
The slope of the fit connects time and position on the screen.
Plugging the numbers into the formula for temporal resolution we end up with 3 fs.

## Slide 12: Energy and timing jitter
Photo cathode RF gun
BC1 @ 260 MeV
BC2 @ 3 GeV
SPF
t
E
t0
ΔE
E0
Δt
E0
>>
Notes: The momentum compaction of bunch compressors connects energy and timing jitter.
In this example with positive R56 an energy increase delays the electron bunch.
Low arrival time jitter thus require low energy jitter.
For jitter studies we only have to include the linear momentum compaction, since higher order terms are insignificant.

## Slide 13: Energy jitter sources
Master oscillator
Experimental laser
Gun laser
Low-level RF
Synchronization
  Gun laser timing
RF distribution and amplification
  RF amplitude
  RF phase
Klystron
  Modulator HV
    RF amplitude
    RF phase
Amp
Klystron
Linac structure

## Slide 14: Energy jitter sources
Master oscillator
Experimental laser
Gun laser
Low-level RF
Synchronization
  Gun laser timing
RF distribution and amplification
  RF amplitude
  RF phase
Klystron
  Modulator HV
    RF amplitude
    RF phase
Amp
Klystron
Linac structure

## Slide 15: Klystron working principle
U0
Notes: Hot filament electron gun
HV, usually provided by a modulator
The input RF generates an energy modulation, which in the drift tube turns into a density modulation.
The density modulated beam radiates efficiently in the output cavity.

## Slide 16: Supression of amplitude jitter
U0
Pout [MW]
Pin [W]
600
400
200
0
0
20
40
60
Pin
Pout
Amplitude and phase changes in a correlated manner!
Notes: The output power as a function of input power has a saturation plateau.
Operating the klystrons in saturation is a very good to filter away amplitude variations on the input power.
The output power or amplitude also depends on the accelerating voltage.
Higher voltage, more power.
The time of flight also depend on the same accelerating voltage.
Higher voltage, shorter time of flight and reduced phase. – note that amplitude and phase change in a correlated manner.

## Slide 17: HV induced energy jitter
Photo cathode RF gun
BC1 @ 260 MeV
BC2 @ 3 GeV
SPF
θcrest
ΔE
Amplitude and phase changes in a correlated manner!
Notes: In this illustration energy gain is plotted for three HV settings, nominal setting in yellow.

## Slide 18: HV induced timing jitter - chicane
Photo cathode RF gun
BC1 @ 260 MeV
BC2 @ 3 GeV
SPF
θchicane
ΔE
E0
Δt

## Slide 19: HV induced timing jitter – arc like BC
Photo cathode RF gun
BC1 @ 260 MeV
BC2 @ 3 GeV
SPF
θmagic
E0
E0

## Slide 20: MAX IV single optical oscillator synchronization system
Rohde Schwarz SMA100A
Linac LLRF
Fiber amplifier
Coherent amplifier
Experimental laser
KM Labs amplifier
RF generation
Fiber distribution
400m stabilized fiber link to the experimental laser.
Spec broadening
KM Labs amplifier
Fiber amplifier
2ω
Compression
Spec broadening
Fiber amplifier
2ω
Compression
Spec broadening
Fiber amplifier
2ω
Compression
Gun laser lab
Femtomax
Low noise fiber oscillator
Notes: This schematic overview shows the single optical oscillator systems that we have started constructing.
Low noise Erbium laser oscillator

## Slide 21: Energy stability results
BC1_BPL01 BC2_BPL01
Optical MO – low noise fiber oscillator
New RF reference from Quantic Wenzel
Lower absolute phase noise fiber oscillator
Direct RF conversion @1550nm
Finding and eiminating other phase noise sources
Low jitter RF conversion
BC1
1.3e-4 energy jitter
7 fs – 14 fs time jitter (after BC1)
BC2
5e-5 energy jitter
5.8 fs - 17 fs (after BC2)
0
40
20
80
60
100
Time [s]
RF oscillator
BC1
7e-4 energy jitter
38 fs - 74 fs time jitter (after BC1)
BC2
2e-4 energy jitter
26 fs - 84 fs (after BC2)
Chart: ΔE/E
Chart: ΔE/E
ΔE/E
Notes: In the plots you see X position data for two BPMs at the dispersive maxima in BC1 and BC2.
BC1 in blue and BC2 in redish.
Already by eye the improvement is quite striking.
A factor of 5 worse oscillator jitter performance gives a factor 2 better accelerator stability

## Slide 22: Conclusion - MAX IV linac
Multi-purpose accelerator
Magnetic linearization
Short bunches
High energy stability

## Slide 23: Additional slides

## Slide 24: MAX IV linac
39 warm s-band linac structures + SLED
18 units
3 GHz
5.3 m/linac
20 MV/m gradient
3 + 0.6 GeV
18 modulators + klystrons
37 MW peak power
4.5 ms
100 Hz
Thermionic gun: 8 MW 10 Hz RF unit
Notes: Sits in two different tunnels

## Slide 25: Thermionic gun
RF gun
BaO cathode
Exported to SOLARIS and Canadian light source
270 degree energy filter
In operation at MAX-lab
Design parameters of the MAX IV thermionic pre-injector | 
Beam kinetic energy | 2–2.5 MeV
Bunch frequency before chopper, fgun | 2.9985 GHz
Bunch train frequency, fring | 99.931±0.5 MHz
Number of bunches per bunch train | 3
Number of bunch trains per LINAC shot | 1 or 10
LINAC shot repetition frequency | 10 Hz
Total injected charge per top-up injection | 9.0 nC

## Slide 26: Thermionic gun
RF gun
BaO cathode
Exported to SOLARIS and Canadian light source
270 degree energy filter
In operation at MAX-lab
Design parameters of the MAX IV thermionic pre-injector | 
Beam kinetic energy | 2–2.5 MeV
Bunch frequency before chopper, fgun | 2.9985 GHz
Bunch train frequency, fring | 99.931±0.5 MHz
Number of bunches per bunch train | 3
Number of bunch trains per LINAC shot | 1 or 10
LINAC shot repetition frequency | 10 Hz
Total injected charge per top-up injection | 9.0 nC
3 GHz
Up to 10 micro bunches
100 MHz
10 Hz
+ Chopper system*
* D. Olsson et al, A chopper system for the MAX IV thermionic pre-injector, Nuclear Instruments and Methods in Physics Research, Volume 759, 21 September 2014, Pages 29–35

## Slide 27: Thermionic gun + chopper
Energy
filtering
Strip line
Aperture
500 MHz

## Slide 28: Thermionic gun commissioning
Energy
filtering
Strip line
Aperture
500 MHz
Commissioning parameters | 
Charge | 0.75 nC/shot
Rep rate | 2 Hz
Chopper f | 500 MHz

## Slide 29: Thermionic gun commissioning
No aperture
With aperture
Energy
filtering
Strip line
Aperture
500 MHz

## Slide 30: Thermionic gun commissioning
No aperture
With aperture
Energy
filtering
Strip line
Aperture
500 MHz

## Slide 31: Thermionic gun commissioning
No aperture
With aperture
Energy
filtering
Strip line
Aperture
500 MHz

## Slide 32: Commissioning
Beam energy
280 MeV
L1B
Thermionic RF gun
Photo cathode RF gun
L1A
L0
BC1 (@260 MeV)
Maximum dispersion