## Slide 1
The Statemachine
Filip Persson, Asst. Head of Operations
Full energy linacs workshop

## Slide 2: Overview
Filip persson, operations
R3
Photo gun
R1
Thermionic gun
SPF
BC 1
BC 2
Topup every 10 minutes

## Slide 3: Two layers
Filip persson, operations
Statemachine Tango device
Statemachine Widget (Taurus based GUI)
Started by Johan Sjögren (former operator), Current framework developed by Andreas Johansson (former operator)

## Slide 4: States
Filip persson, operations
Each state has rules on how to enter the state
The state loop is the brain of the Tango device server.
It checks at each tick (500 ms) if current state should be exited and a new state entered.
A two loop hierarchy
Active user?
(requested ring injection/stop injection)
Active state? (topup)

## Slide 5: States
Filip persson, operations
3 GeV ring injection
1.5 GeV ring injection
SPF delivery
Linac trimming
Standby
5 states with the following hierarchy (looped in order)
Example:
R3 topup activated
Scheduled injection = true, and
Clock exceeds time of injection, and
Current below min limit, and
IDs within allowed limits
Scheduled injection = false, and
Current below min limit, and
IDs within allowed limits
OR
Conditions

## Slide 6: Bensikin software
filip persson, operations
Software handling linac settings
We’re using the underlying tango snapshot handler to load or save snapshots

## Slide 7: The injection loop
filip persson, operations
Starting python thread running at injection frequency
Reads ring current
Evaluates exit conditions (e.g. goal current reached)
Change targeted ring bucket by changing timestamp in the ring event generator using formula or filling pattern feedback
Timestamp for the triggering of the injection kicker is changed by same amount to keep fixed offset
Evaluates additional exit conditions
Additional exit conditions:
topup_max_failed_shots (40) is reached (no ring capture)
topup_max_duration is reached

## Slide 8: Statemachine control
filip persson, operations

## Slide 9: State log output
filip persson, operations
Logging important output or error messages

## Slide 10: Alarm state
filip persson, operations
Failing state transition or ending up in mixed state
Often due to failing equipment or communication issues with the equipment
Fail to set snapshot (linac settings)
Fail to enable injection trigger
Fail to control current of horizontal corrector used for deflecting thermionic electrons
Fail to open/close laser shutter controlling photo gun electrons

## Slide 11: Special modes of operation
filip persson, operations
Photo gun injection
Single bunch injection Timing and DC chopper values set)
Reduced charge mode Used if a very uniform filling pattern is desired. Vertical corrector after the gun is used to only let through 1/4 of the charge
Filling pattern control A vector of bucket weights (0 or 1) is set and the Statemachine only loops through allowed buckets. Best used together with single bunch injection.

## Slide 12: Filling pattern feedback
filip persson, operations
Effect on bucket weights
Bucket weight attribute
Filling pattern example

## Slide 13
Questions?