## Slide 1: Virtual Diagnostics and Bayesian Optimization in the MAX IV Linac
NSLS II-MAX IV workshop
5-6 Oct. 2026
Johan Lundquist

## Slide 2: Outline
The MAX IV Linac and the Transverse Deflecting Structure System
Machine Learning Fundamentals
Virtual Diagnostic for Longitudinal Phase Space Predictions
Bayesian Optimization of LPS Distributions
MAX Applications

## Slide 3
MAX IV – Linear Accelerator
Acceleration
40 S-band normal conducting RF structures. 265 MeV at first bunch compressor, 3 GeV at the second.
Bunch Compressors
Arc-like bunch compressors allow for tunable, non-linear compression.
MAX IV Linac
Full energy linac delivering to two rings and one short pulse facility (SPF).
SPF: FemtoMAX and TDS
Bunch length is critical, but separate branches makes online measurements very difficult, implement Virtual Diagnostic.
370 m
1.5 GeV
3 GeV
TDS
FemtoMAX
SPF
Notes: Cut here? Not so much general MAX IV
Refer to FemtoMax as experimental beamline

## Slide 4
Transverse Deflecting Structure
Measured
Longitudinal Phase Space
MAX IV TDS line includes two 3 m deflecting structures.
3 separate branches with multiple YAG screens for varied dispersion and streak
Notes: Maybe, mention IBIC23?

## Slide 5
Machine Learning – The Perceptron
Trainable Weights
Sets the relative importance of different inputs
Loss
Optimizer, ADAM
Ground truth
y
Prediction

## Slide 6
Machine Learning – The Multi-Layer Perceptron

## Slide 7: LPS Virtual Diagnostic – Experimental Setup
Photocathode gun
Thermionic gun
Accelerating
Structures
L01
Bunch Compressor 1
1.5 GeV
extraction
L2A L19A
3 GeV
extraction
L19A L19B
SP03
SP02
SP01
Main Drive Line
L02-19
L2B
Bunch Compressor 2
High Energy TDS
Dump
Dipole
Sextupole
Quadrupole
Magnets
To FemtoMAX
Non-destructive Beam Information
Scanned RF Parameters + Beam Position Monitors + Current Tranformers + etc…
Scanning RF phases before BC1 and BC2
This provides similar range of LPS shapes to what is used in beamline delivery
Destructive Measurement
TDS images for output
Virtual Diagnostic
9000 images collected, ~6 hour beamtime
  HDF5 set with 9000x650x650 images + 108 input params

## Slide 8: VD - Network Structure and Training
Dense Net + CNN trained with ADAM and MAE
  Used scheduled learning rate and checkpoints for early stopping
  Post-processing: Align beam distributions using cross-correlation
Large image size layer
  Extends training time
  Required for full LPS images
  Could be smaller -> lower resolution
Networks trained on LUNARC HPC Cluster
  Training time on Nvidia A100 ~10 minutes
  Training time on Laptop CPU ~1-2 hours
100 Dense Nodes
Batch Normalization
100 Dense Nodes
422 500 Dense Nodes
4*4x4 Convolutional Kernels
1*5x5 Convolutional Kernels
Input Vector

## Slide 9
MAX IV – LPS Predictions
Median
Worst
Best
10% of data set reserved for testing
R2: Mean = 95.5%, Median = 96.1%

## Slide 10
SwissFEL
FERMI
Multi-Facility Virtual Diagnostic for Longitudinal Phase Space Predictions
J. Lundquist, J. Björklund Svensson, P. Dijkstal, E. Mansten, G. Penco, S. Werin and F. Curbis, Scientific Reports Vol. 16, 12021 (2026)

## Slide 11
Multi-Facility Virtual Diagnostic – Final Results
 | MAX IV | FERMI | SwissFEL - Athos | SwissFEL - Aramis
Median | 96.1% | 96.4% | 94.3% | 99.1%
Mean | 95.5% | 96.3% | 88.7% | 98.9%
 | MAX IV | FERMI | SwissFEL - Athos | SwissFEL - Aramis
Median | 96.1% | 96.4% | 94.3% | 99.1%
Mean | 95.5% | 96.3% | 88.7% | 98.9%
Median Images
Performance on 10% of each full dataset

## Slide 12
Beam Parameter Approach - Results
MAX IV
FERMI
SwissFEL - Athos
SwissFEL - Aramis
250 Dense Nodes
Batch Normalization
250 Dense Nodes
Input Vector
Beam Parameters

## Slide 13: Bayesian Optimization of Longitudinal Phase Space in the MAX IV Linac

## Slide 14
Bayesian Optimization
Optimization of accelerator parameters can be costly and inefficient
Implement machine learning methods to alleviate
Bayesian Optimization works through a posterior model of the environment, which can return both values and uncertainty estimates
This can allow the optimizer to “learn” the response of the environment and optimize with few queries compared to other, traditional gradient optimizations

## Slide 15
LPS Optimization with XOpt
Jitter and the inherent complexity of the system makes LPS queries at MAX IV difficult
Implemented Bayesian optimization routines for key parameters ()
Optimizing on RF settings in the rest of the linac, affecting the compression and energy spread of the final bunches in the SPF
Implemented using the Xopt framwork, easily applied to other tasks of facilities

## Slide 16
Constructed a VD based on the MAX IV TDS system,
then performed Bayesian optimization on bunch length and energy spread using the XOpt framework.
In theory, allows for continual optimization or feedback on the LPS.
LPS Optimization with XOpt and Virtual Diagnostic

## Slide 17: MAX Applications

## Slide 18
ML-MOGA – Speeding up design of MAX
MOGA can require many queries of expensive, detailed simulations for convergence
Implement surrogate model of the tracking simulations (NN Lookup) which, once trained, is a cheaper, faster alternative to simulation
From Leeman slides ~40x speed up of MOGA optimizations
Implemented early on in lattice iterations for MAX IV-U

## Slide 19
Machine Learning for
ID Orbit Correction
IPAC’25
• Beam orbit distortions by Insertion Devices currently corrected with measured feed-
forward tables → Very time consuming
• Tables might be invalidated over time, or with different machine parameters
(e.g. long-term drift, machine upgrades)
• New modes of ID operation can require several hundreds of measurement
points e.g. universal mode
• Prototyping of ML models that effectively replace
measured feed-forward tables

## Slide 20
Machine Learning for
ID Orbit Correction
IPAC’25
•Loss function focused on minimizing orbit distortions
• Trained using archived data –> Will need to adapt the procedure for MAX
• Reinforcement Learning
• Recurrent Neural Network built with tensorflow and integrated into the control system (Tango)
• Without this or a similar solution, major beamtime commitment will be needed for remeasuring the FF tables!

## Slide 21
Virtual Diagnostics are relatively easy to implement and methodology can be generalized between facilities.
Plenty of work left to make them more general, outside supervised datasets and limited systems.
Combinations of ML techniques (like BO+VD) shows promise for automating difficult procedures, including applications for ring design and control.
ML-MOGA and Recurrent Machine Learning is assisting in lattice design and online control for ID compensation.
Conclusions

## Slide 22: Complementary Material

## Slide 23: Non-Destructive Passive Streaker Calibration using Machine Learning

## Slide 24
L | 1 m
w | 40 mm
b | 250 μm
g | ≤28 mm
p | 500 μm
δ | 250 μm
Passive Streaker Calibration using ML - Concept
P. Dijkstal, A. Malyzhenkov, P. Craievich, E. Ferrari, R. Ganter, S. Reiche, T. Schietinger, P. Juranić, and E. Prat, Self-synchronized and cost-effective time-resolved measurements at X-ray free-electron lasers with femtosecond resolution, Phys. Rev. Res. 4, 013017 (2022).

## Slide 25
Passive Streaker Calibration using ML - Concept
PS Signal implicitly difficult to calibrate, due to non-linear, trajectory-dependent streak.
We can use the upstream TDS to calibrate using the actual bunch profile, using their cumulative charge distributions.
BUT this is a destructive and time-consuming procedure, we’ve implemented a VD based calibration.

## Slide 26
Passive Streaker Calibration using ML - Setup
1D CNN U-NET
250 000 Trainable param.
Parameter Scans
2D Scan of phases before the two Bunch Compressors
DAQ first from C-Band TDS, then from PS
U-Net with Profiles in, Profiles out
1685 Profiles, 300 Length
256
128
64
Notes: Indicate that the waterfall is sorted by r2 somehow?

## Slide 27
Results, RMS Bunch Lengths and Time calibration factors
U-Net VD could provide an improvement in repdoduced profiles.
Similar performance when comparing reconstructed bunch lengths and measured using TDS.
Clear improvement over non-ML technique when looking at generated time calibration curves
  Compared using the linear component of the calibration curve in the core of the beam (0.3<G<0.9)

## Slide 28: FEL Power Profile Predictions with Image-Based Machine Learning at FLASH

## Slide 29
Utilize VD to predict corresponding Non-lasing LPS, for use in reconstructing FEL Pulse Profile
Uses BCM, BAM and charge signals
FLASH 2 Beamtime – 7/1-2026

## Slide 30
Data and VD Performance
Jitter Data, 6000 Non-lasing training shots
3150 test shots, Lasing
Non-Lasing
Lasing

## Slide 31
Power profile reconstructions using VD predictions and Non-VD choice of maximum similarity.
Taking the shift in COM, applying time calibration and charge normalization.
Techniques perform similarly well.
Final Performance and Comparison with Non-ML Technique