## Slide 1: Survey and Alignment Strategy for MAX 4U
NSLS II-MAX IV workshop
5-6 Oct. 2026
Keyu Zhou

## Slide 2: Outline
Survey and Alignment Work at MAX IV
What Does MAX 4U Mean to Alignment?
Survey and Alignment Strategy for MAX 4U
Conclusion

## Slide 3: Outline
OCT. 2026
Keyu Zhou
27 July 2023
Survey and Alignment Work at MAX IV
Alignment needs at accelerators and beamlines
Survey and alignment networks at MAX IV
Alignment strategy at MAX IV
What Does MAX 4U Mean to Alignment?
Survey and Alignment Strategy for MAX 4U
Conclusion
Nsls ii-max iv wORKSHOP

## Slide 4
NanoMAX beamline
1.5 Gev Ring and 3 Gev Ring magnets alignment
Linac element alignment
Beamline alignment:
Insertion device alignment
Front End alignment
Optics alignment
End station alignment
…
CoSAXS optical hutch alignment
Linac and SPF magnets alignment
Accelerators alignment:
Gun alignment
Linac element alignment
Transfer lines alignment
…
Alignment needs at MAX IV

## Slide 5
Wall nest:
Mounted on the wall with
expansion bolts
Floor nest:
Glued to the floor
Horizontal distance ~6 m
Nests on both of sides of wall and floor
Two different height of wall nests to have better
differential distribution of vertical angle observations
Local network, no connection to outside geodetic networks
Alignment network at MAX IV

## Slide 6
Network 1: Linac tunnel +SPF area+TR1+TR3
Network 2: 3 GeV ring tunnel + 3 GeV ring beamline area
Network 3: 1.5 GeV ring + 1.5 GeV ring beamline area
Alignment network at MAX IV
Three independent networks
MAX IV Facility (CAD)

## Slide 7
Alignment network at MAX IV
Limitation of free adjustment solution:
No Absolute external reference at MAX IV, the network remains floating in space
Blindness to gravity and earth’s curvature for large scale network
Stack-up error, especially with poor geometric diversity
We have a weak estimation of waviness
Corrector-magnets can handle the waviness
Boundary conditions introduced
Roughness:
High spatial frequency error
Waviness:
Low spatial frequency error
Errors=
+

## Slide 8
3 GeV ring magnets alignment
Magnet cell in 3 GeV ring: integrated unit containing consecutive magnet elements in a common solid iron block
UC4 magnet cell
Upper yoke
Lower yoke
Magnets
Intra magnet cell alignment: Guaranteed by mechanical manufacturing tolerance
Magnet half yoke with very tight manufacturing tolerance

## Slide 9
3 GeV ring magnets alignment
Inter magnet cell alignment:
Fiducialization is done by manufacturer
Cell to cell alignment is done with standard MAX IV alignment sets
5 Fiducial nests on each magnet cell
Standard MAX IV alignment sets

## Slide 10: Outline
OCT. 2026
Keyu Zhou
27 July 2023
Survey and Alignment Work at MAX IV
What Does MAX 4U Mean to Alignment?
Alignment requirements for 3 GeV ring
Error budget for MAX 4U
Survey and Alignment Strategy for MAX 4U
Conclusion
Nsls ii-max iv wORKSHOP

## Slide 11
  Emittance 75 pm rad
  Keep the shielding wall
  Keep the injector: accumulation
  Keep existing light source positions
  Limited dark period
  Cost-effective
  Realisable until the early part of the next decade
  No impact on the operation of the 1.5 GeV ring/SPF
What does MAX 4U mean to survey and alignment
MAX 4U goals and boundary conditions
Light sources/Insertion devices could be taken as boundary condition for the network solution, to keep the source positions of the beamlines.
Survey and alignment assumptions based on MAX 4U goals and boundary conditions:
The same fiducialization and alignment system as for 3 GeV ring will be adopted.
Tighter alignment requirements

## Slide 12
Network/
Localization Accuracy
Measurement accuracy
Alignment accuracy might achieve
Proper alignment system
Alignment accuracy achieved
Design review
Network Survey
Fiducialization
Alignment
Alignment accuracy
1
2

## Slide 13
Alignment requirements in R3
3GeV-ring:
  140 integrated magnet blocks in 20 achromats.
  Block size: 256x350x2300-3350 mm.
  Block-to-block alignment requirements:
  100 (goal 50) μm, 1σ
  Roll: 0.2mrad, 1σ.
  Diameter size requirements: down to a few mm
Relative alignment requirement
1 achromat in 3GeV-ring
Global alignment requirement
Mechanical tolerances
Accuracy of the magnets inside one block is guaranteed by machining tolerances.
UC 3 magnet in 3GeV-ring (CAD)
We don’t have intra-girder alignment

## Slide 14
15 μm + 6 μm/m (MPE)
3D Accuracy:
R3 magnet cell misalignment error
Measurement accuracy according to manufacturer
3D misalignment error analysis
Laser tracker survey data from 3 independent surveys in Survey R3-2016, 2017 and 2021
For each survey, 100 stations inside R3 tunnel were used in simulation.
An average measurement distance of 6.1 m in radius in the three surveys.
Weight=1 on magnets nominals as boundary condition for local alignment uncertainty simulation.
Angular uncertainty: 1 arcsecond
Distance uncertainty: 0.00762 mm+0.0025 mm/m
Local alignment uncertainty does not include waviness of network

## Slide 15
R3 magnet cell misalignment error
6.6 m shot length assumed for laser tracker measurement in network survey.
3.5 m shot length assumed for laser tracker measurement in alignment.
New alignment network (no deformation) used for localization
Simulated 6-DOF error of A01M1 Cell
Simulation is based on:
Definition of frame with origin on the beam on the mid-point along a magnet-cell
A 3D fiducial local absolute uncertainty of 63 µm (1σ) is used for simulation
This uncertainty simulation was presented in CDR phase.
It is now updated with new data after relative alignment study

## Slide 16: Outline
Keyu Zhou
27 July 2023
Survey and Alignment Work at MAX IV
Alignment requirement for MAX 4U
Survey and Alignment Strategy for MAX 4U
Survey strategy for MAX 4U
Alignment strategy for MAX 4U
Conclusion
OCT. 2026
Nsls ii-max iv wORKSHOP

## Slide 17
3 GeV ring network survey
3 GeV ring boundary condition:
Insertion device nominals
M1, U1, U2,U3,U4, U5, M2
magnets nominals
Network floor points inside tunnel
Network points at beamline area
Hippie beamline area
Front end area in R3 tunnel
NanoMAX undulator
Magnet cells in one achromat
Concrete gate connecting tunnel and beamline networks

## Slide 18
MAX 4U network survey
Magnet cells nominals will NOT be the same
10 Existing beamlines
1 New beamline under construction
Light sources/ Insertion devices nominals should NOT be changed or moved
TR3 might need realignment
MAX 4U condition
Magnet nominals will NOT be used as boundary conditions anymore.
A new alignment network should be used for the alignment of the magnet blocks.
A complete network survey needs to be done including beamline areas.
12 Insertion devices nominals will be used as network boundary condition
More floor points are added inside R3 tunnel. If floor points should be used as boundary conditions still under discussion
MAX 4U Survey Strategy
TR3

## Slide 19
MAX 4U alignment strategy
Magnet cells will use Identical alignment systems and fiducialization strategies as it is in R3
Relative accuracy between the magnet cells are more important than global accuracy, the closer the magnet cells are, the tighter requirements are needed.
Assumptions:
Measurement project:
Absolute station: Instrument localized with the network, using double face measurement.
Relative station: Instrument localized with neighboring magnet cells that are aligned (measured) in absolute stations, using single face measurement.
Absolute-station #1
(Including network)
Relative-station
Absolute-station #2
(including network)
7 magnet cells in Achromat 3

## Slide 20
MAX 4U alignment strategy
Localization shots
Alignment shots
13.2 m
10 m
6.5 m
Relative-station
Absolute-station #1
Absolute-station #2
Localization shots
Localization shots
Alignment shots
7.4 m
6.5 m
10 m
Relative-station
Absolute-station #1
Absolute-station #2
Alignment shots
Absolute-station #1
Relative-station
Absolute-station #2
Strategy 1
Strategy 2
Strategy 3
Project led by Behrouz Afzali Far

## Slide 21: Preliminary Results (relative uncertainty)
Strategy 2 yields the best results which according to the model, considering the manual uncertainty (16.7 µm), is roughly 40 µm.
If we consider the 120% factor of safety: 48 µm
Across one achromat
Project led by Behrouz Afzali Far

## Slide 22: Outline
Keyu Zhou
27 July 2023
Survey and Alignment Work at MAX IV
Alignment requirement for MAX 4U
Survey and Alignment Strategy for MAX 4U
Conclusion
OCT. 2026
Nsls ii-max iv wORKSHOP

## Slide 23
Survey and alignment assumptions based on MAX 4U goals and boundary conditions:
The same fiducialization and alignment system as on 3 GeV ring will be adopted.
A full network survey including beamline area needs to be taken before but close to the dark period, one option is in Summer shutdown 2030.
Light sources/Insertion devices should be taken as boundary conditions for the network solution, to keep the source positions of the beamlines.
Relative magnet-cell to magnet-cell alignment uncertainty needs to be considered with priority
Conclusion

## Slide 24: Thank you

## Slide 25: Complementary Material

## Slide 26
Minimal kinematic coupling
(one thing at a time)
MAX IV_Alignment _Standard-1.0
Reflector nests close to feet to
minimize alignment iteration
Alignment system

## Slide 27
index + Belleville washer (push-repush )
+spherical bearings + sliding surfaces
1mm
5 μm (one tenth of alignment tolerance)
36 mm
±12.5 mm
Structure
Pitch
Resolution
Full Range
Safe Range
Advantage
Vertical feet
Transversal feet
Threaded rod +spherical bearing
+sliding surfaces
Locking screws
1mm
5 μm
21 mm
±5 mm
Minimal stick-and-slip, Easy and straightforward to use
Alignment system

## Slide 28: Updated error model: magnitudes
No truly complete error model exists; reality is always more complex
 | Magnet misalignment (µm/µrad) [2,3] | Girder misalignment (µm/µrad) [1,4] | BPM "misalignment" (µm/µrad) [5]
Sway | 4 | 27 | 3
Heave | 9 | 21 | 3
Surge | (0) | 16 | (0)
Pitch | (0) | 21 | (0)
Yaw | (0) | 21 | (0)
Roll | 100 | 157 | 100
Sag | - | 20 | -
Bold – based on data (references below)
(parenthesis) – ignored as impact reasoned to be negligible
Red – proxy value used (measured BBA reproducibility, i.e. only includes random component)
Blue – unavailable, historical assumption used. NB! Magnet roll errors show up as skew components in evaluation of series production field measurement data.
Sources
Internal MAX IV report by SAM
M. Johansson et al., "Magnet design for a low-emittance storage ring", Journal of Synch. Rad., July 2014
M. Johansson et al., "MAX IV 3 GeV STORAGE RING MAGNET BLOCK PRODUCTION SERIES MEASUREMENT RESULTS", Proc. of IPAC 2015
Internal communication, Design Office
Experimental data
28

## Slide 29: What is our error model?
Misalignment
Misalignment could be larger that alignment uncertainty because of additional errors related to building deformation over time, temperature, fiducialization, etc.
alignment
measurement
Alignment uncertainty model:
Total (includes the waviness, this is not relevant for realignment)
Local (where nominal points are used to remove the stack-up error)
  Absolute (to the network)
  Relative (cell-to-cell)
These values are given for 3.5m, and a fiducial absolute uncertainty of 63 µm
Local error

## Slide 30: Preliminary Results (absolute uncertainty)
At roughly 3.5 m, considering the network uncertainty (30 µm) and the manual uncertainty (16.7 µm), the absolute uncertainty is obtained as 53 µm.
Across one achromat