## Slide 1
Group 5
Vacuum Systems and mechanical integration, Alignment, DC and pulsed Magnet Systems Reporting back
NSLS-II & MAX IV Workshop: Fourth and Future
Generation Light Source Design Challenges

## Slide 2: Key Takeaways
Vacuum system: both upgrades rely on previous experience and design approaches.
  What are the largest deviations from the previous design, new implementations?
    MAX4U:
    the installation procedure differs significantly from the original one.
    For MAX4U one new RF-shielded bellow (of 25 mm compression stroke) will be added near the arc center to allow baking without venting the long straight sections for IDs (how ever the magnets for the baking must be always removed).
    NSLSII-U:
    Vacuum chambers much smaller ID: 11 mm, alu chambers machined in 2 halves and welded together (NSLSII VCs were extruded), have antechamber thus influence on the magnet design.
    No issue with having the magnet opening in midplane (space for antechamber), although not having antechamber thus more space for magnet assembly might be beneficial.
    Installation process: It will be the same as NSLSII: modules with magnets on girders pre-assembled and later placed in the tunnel and flanged connection done, then pumping etc.
Magnets: Permanent magnets will extensively be used in NSLSII-U. Some challenges in getting material, assembly, integration, installation (previous experience exists: ESRF-EBS, SLSII). At MAX4U seems PM will not be used. CB magnet string considered to have motorized individual magnetic elements which is a big challenge.
NSLSII-U develops an NLK (Non-Linear Kicker) (MIK) based on ceramic blocks that are inserted into metal vacuum chamber (similar to TPS, BESSY…).
  What are experiences from NSLSII/BESSY/TPS? At MAXIV ceramic chamber of the MIK heats up to 41 to 74 deg C (at 400 mA) depending on the operation mode (in 2026).
Notes:   What would you change if you could design MAXIV/NSLSII again?
    MAXIV:
    introduce bellows to the arc section to allow insitu NEG activation (lack of longitudinal stroke was major obstacle),
    more careful management of areas prone to heat up or close to shadowed areas (longer absorbers, larger apertures of sensitive hardware where possible, perhaps fiducialization and alignment of critical components, smaller beam aperture to the FE to shield a vacuum chamber upstream the Front End,
    include PLC of Front end in the ring system not in beamline (so that it can be controlled by the machine easier),
    simpler naming convention for vacuum hardware.
    NSLSII:
    y

## Slide 3: Collaboration opportunities
Exchange regarding vacuum simulations in Molflow+ coupled with Synrad.
  Material surface properties choice: roughness, Reflection studies (experience from EIC, APS).
  Vacuum chamber desorption studies: what has been done at NSLSII? Dipole and 3PW source, Chamber for EIC were measured there.
  NSLSII have a section in ring where components can be tested with beam, could MAXIV use it if need be?
Magnets: rotating coil measurement at NSLSII. NLK at MAXIV experience to share with NSLSII
Alignment: fiducialization procedure, stretched wire measurement, Multiple laser tracker alignment.

## Slide 4: Challenges / Open Questions
Stored beam allowed envelope, ensuring that chambers intercepting photon beam can operate safely (mostly light from IDs).
  At MAXIV/MAX4U photon beam from several IDs (Wiggler, EPU, 3PW) is difficult to handle in the location where photon and electron beam split (magnet bore is the limit),
  What is the beam position used to simulate extreme cases (offset from nominal position, angle). How to simulate vacuum chamber misalignment/manufacturing errors. How does it translate to the allowed beam envelope? At which conditions the beam is dumped?
    MAX4U: with the usually applied offset 0.5 mm and angle some vacuum chambers will not fulfil the design criteria due to excessive heat from photon beam.
  What are the material design criteria for absorbers, etc.? Are they different?
  What is the alignment approach to lumped absorbers or other parts close to the photon beam? Are they individually aligned or rely on mechanical tolerances only to other aligned components?
  Does the 4 GeV option for NSLSII-U put more stringent requirements on the photon absorbers due to higher photon power?
Magnets:
Alignment: