## Slide 1: Normal Conducting magnets for particle accelerators Part I
A. Vorozhtsov

## Slide 2: Magnet types by working principle
Superconducting Magnets. They work only at very low temperatures (liquid or superfluid helium). The high current density possible in their special cables produces a high magnetic field not possible with resistive magnets.
Permanent Magnets. No current flows into these magnets. The field is produced by means of the permanent residual magnetization of special materials. This technology allows the construction of compact magnets with a relatively strong field. No cooling is required.
Normal conducting. They are not magnetic unless a certain current flows into their coils. The field can be increased and concentrated by means of a ferromagnetic yoke. The resistance of the windings dissipates some energy and the resulting heat has to be removed with a water circuit or air flow

## Slide 3: Main components of normal-conducting, iron dominated magnets
Iron ( Pole + Return Yoke)
Excitation Coils
Sensors
Cooling circuits (for water cooled coils, manifold)
Electrical connections
Supports
Alignment target holders
Dipole
H/V corrector
Quadrupole
sextupole

## Slide 4: MAX IV Magnets
MAX IV LINAC DIPOLE magnet DIB
MAX IV LINAC one plane corrector COD
MAX IV LINAC quadrupole QF
MAX IV sextupole SXH
MAX IV R1 magnet block
MAX IV R3 magnet block

## Slide 5: Nomenclature
Magnetic Field (A/m): (the magneto-motive force produced by electric current )
The magneto-motive force creates a Magnetic Flux (Weber)
Permeability of free space: µ0 = 4π×10-7 (H/m)
Relative permeability: µr=µ / µ0 (dimensionless)
µr (free space)=1, µr (Iron) ≈1000
Flux density (Tesla=Weber/m2): The amount of magnetic flux through a unit area taken perpendicular to the direction of the magnetic flux. Also called magnetic induction.

## Slide 6: MAGNETO-STATIC THEORY
F is a function of the two dimensional complex space coordinate z=x+iy is developed from Maxwell’s equations. This function satisfies Laplace’s and Poisson’s equations.
This function is used to describe different two dimensional magnetic fields and their error terms.
Poisson’s Equation
Laplace’s Equation
Maxwell’s Steady State Magnet Equations

## Slide 7: Vector and Scalar Potentials
The function can be expressed as F=A+iV where
  A, the vector potential is the real component
  V, the scalar potential V is the imaginary component
An ideal pole contour can be computed using the scalar equipotential.
The field shape can be computed using the vector equipotential.

## Slide 8: Two dimensional magnetic field
The gaps are regions where current sources and permeable material are absent. Two-dimensional magnet fields can be derived from potential functions which are the solutions to Laplace’s equation.
Bx = Br cos  - B sin 
By = Br sin  + B cos 
An and Bn are the skew and normal field components
n-field index: Dipole n=1 , Quadrupole n=2, Sextupole n=3, Octupole n=4
In Cartesian coordinates, the components are given by:

## Slide 9: Magnet types by their field
For normal(non-skew) the expansion of By(x) y = 0 is a Taylor series:
By(x) = n =1  {bn x (n-1)} = b1 + b2x + b3x2 + b4x3 …..
dipole quad sextupole octupole

## Slide 10: Ideal pole shape
Flux is normal to a ferromagnetic surface with infinite :
Flux is normal to lines of scalar potential, (B = - );
 = 
 = 1
curl H = 0
therefore  H.ds = 0;
in steel H = 0;
therefore parallel H air = 0
therefore B is normal to surface.
So the lines of scalar potential are the perfect pole shapes!
(but these are infinitely long!)
dipole
quadrupole

## Slide 11: The Practical Pole
Practically, poles are finite, introducing errors;
these appear as higher harmonics which degrade the field distribution.
However, the iron geometries have certain symmetries that restrict the nature of these errors.
Dipole:
Quadrupole:

## Slide 12: Shims
The ‘shim’ is a small, additional piece of ferromagnetic material added on each side of the poles – it compensates for the finite cut-off of the pole to reduce “allowed” harmonics
Shims
N
S
  For the dipole, N=1, the allowed error multipoles are n=3, 5, 7, 9, 11, 13, 15, …
  For the quadrupole, N=2, the allowed error multipoles are n=6, 10, 14, 18, 22, …

## Slide 13
Normal Bn and Skew An Magnets
Normal quadrupole
Skew quadrupole
Normal sextupole
Skew sextupole
Rotation by 45 degrees
Rotation by 30 degrees

## Slide 14: Introduction of currents (Ampere’s law)
Now for j  0  × H = j ;
To expand, use Stoke’s Theorem:
for any vector V and a closed curve s :
V.ds = curl V.dS
Apply this to: curl H = j ;
then in a magnetic circuit:
 H.ds = N I;
N I (Ampere-turns) is total current cutting S

## Slide 15: Magnet types
Dipoles
Quadrupoles
Sextupoles
Octupoles
Combined function

## Slide 16: DIPOLE MAGNET
Function: to bend or steer the particle beam
Equation for normal (non‐skew) ideal (infinite) poles: y=±r (r = half gap height)
Fundamental field index N=1
Magnetic flux density in the air gap: By= B1 = const.
Finite poles introduce ‘Allowed’ harmonics : n = 3, 5, 7, ...

## Slide 17: DIPOLE MAGNET (YOKE SHAPES)
“H core”:
Advantages:
Symmetric;
More rigid;
Low A-Turns
Disadvantages:
Needs shims;
Access problems.
''Window Frame”
Advantages:
No pole shim;
Symmetric & rigid;
Disadvantages:
High A-Turns
Major access problems;
Insulation thickness
“C core”:
Advantages:
Easy access;
Classic design;
Low A-Turns;
Disadvantages:
Less rigid;
Needs shims;
Asymmetric.
N
N
N
S
S
S

## Slide 18
Along Path 1
Ampere’s law:
Along path 2
For iron;
DIPOLE MAGNET (EXCITATION)
Along path 3:
and
Finally:
Ampere-turns per pole(dipole), where h- half gap;
Ampere-turns per pole(for all multipoles)
r- aperture radius, n-field index

## Slide 19: QUADRUPOLE MAGNET
Function: focusing the beam (horizontally focused beam is vertically defocused)
Equation for normal (non‐skew) ideal (infinite) poles: 2xy= ±r2 (r - aperture radius)
Fundamental field index N=2
Magnetic flux density : By= B2·x
Finite poles introduce ‘Allowed’ harmonics : n = 6, 10, 14, ...

## Slide 20: SEXTUPOLE MAGNET
Function: to affect the beam at the edges, much like an optical lens which corrects chromatic aberration.
Equation for normal (non‐skew) ideal (infinite) poles: 3x2y ‐y3= ±r3 (r - aperture radius)
Fundamental field index N=3
Magnetic flux density: By= B3·(x2+y2)
Finite poles introduce ‘Allowed’ harmonics : n = 9, 15, 21, ...

## Slide 21: OCTUPOLE MAGNET
Function: Octupole field induces ‘Landau damping’ :
introduces tune-spread as a function of oscillation amplitude;
de-coheres the oscillations;
reduces coupling.
Equation for normal (non‐skew) ideal (infinite) poles: 4(x3y –xy3) = ±r4 (r - aperture radius)
Fundamental field index N=4
Magnetic flux density: By= B4·(x3-3xy2)
Finite poles introduce ‘Allowed’ harmonics : n = 4, 12, 20, ...

## Slide 22: COMBINED FUNCTION MAGNET (Gradient dipole)
Function: specialized dipole magnet which in addition to a bend field at its center has a linear gradient. This magnet is a combined function magnet which simultaneously focuses (or defocuses) and bends the beam.
Equation for normal (non‐skew) ideal (infinite) poles: 4(x3y –xy3) = ±r4 (r - aperture radius)
Fundamental field index N=1 and 2
Magnetic flux density: By= B1+B2·x

## Slide 23: Magnet live cycle

## Slide 24: Input

## Slide 25: An example of a magnet follow-up: quadrupole
definition of the specifications (requirements and constrains)
EM / preliminary mechanical design
mechanical design
technical specifications & procurement
acceptance (reception tests & magnetic measurements)
Units to be produced | 11 + (1) | Installed + (spare)
Electron beam energy range | 10 – 20 | MeV
Full aperture Ø | ≥ 70 | mm
Integrated field gradient range | 0.01(10% margin) – 0.18(20% margin) | T
Effective length | 70 | mm
Good field region radius | 20 | mm
Integrated field gradient quality Δ∫Gdz/∫G(0,0,z)dz | < ±40 | units
Operational mode | DC | 
Overall magnet length | ≤ 200 | mm
Overall magnet width x height | < 400 | mm
Power converter current / voltage | < 10 / < 10 | A / V

## Slide 26: EM / preliminary mechanical design
Aperture R=35 mm, Leff=70 mm => B’(0)=(0.14 – 2.57) => NI (1),
Coil (water / air cooled)=> Copper conductor(VonRoll) => Nw/pole (Current, Voltage)
Yoke material low Hc(residual field, Bpole(min)=50 Gauss) / (solid / laminated)
Yoke length (2)
Pole profile optimization
Coil profile optimization
Yoke cross-section optimization
Harmonic analysis
2D optimization

## Slide 27: 3D optimization
Integrated field
Chamfer profile optimization /Harmonic analysis
Magnetic length
Update of the electrical parameters
The relative integrated gradient errors at GFR boundary with the radius of 20 mm were calculated according to the formula:

## Slide 28: An example of a magnet follow-up: Awake quadrupole Mechanical design / Technical Specification
Main Parameters / Tolerances / 3D model (.step file) => Mechanical design => Technical Specification
Parameter | Value | Unit
BASIC |  | 
Number of magnets | 12 | 
Nominal field gradient | 2.54 | T/m
Aperture diameter | 70 | mm
FIELD QUALITY (for information only) |  | 
Integrated field gradient range ∫Gdl | 0.01 – 0.18 | T
Magnetic length | 71.8 | mm
Good field region diameter | 40 | mm
Integrated gradient homogeneity Δ∫Gdl / ∫Gdl | < ± 5·10-4 | 
ELECTRICAL PARAMETERS |  | 
Nominal current Inom | 9.3 | A
Maximum current Imax | 10 | A
Current density at Imax | 1.2 | A/mm2
Dissipated DC power at Inom | 34 | W
Resistance at 20°C | 391 | mΩ
Inductance | 48.1 | mH
Voltage on magnet Unom (DC) | 3.64 | V
COOLING |  | 
Cooling method | Air, natural convection | 
DIMENSIONS AND WEIGHT |  | 
Yoke length | 40 | mm
Overall length | ~156 | mm
Overall width | ~395 | mm
Overall height | ~342 | mm
Total magnet mass | ~ 23 | kg
Parameter | Value | Unit
Number of coils per magnet | 4 | 
Number of pancakes per coil | 1 | 
Number of turns per coil | 138 | 
Conductor length per coil | ~43 | m
Conductor size on copper | 3.0 × 2.8 | mm × mm
Conductor edge rounding radius | 0.5 | mm
Min. conductor insulation thickness | 0.06 | mm
Max. conductor size with insulation | 3.2 × 3.0 | mm × mm
Ground insulation thickness | 1.5 | mm
Electrical resistance per coil at 20°C | 98 ± 1 | mΩ

## Slide 29: Production follow-up
Preliminary and Final Design Reports
Magnet and tooling drawings
Material certificates
QCR(Yoke, Coils, Magnet)
Samples

## Slide 30: Production follow-up QCR Coil

## Slide 31: Production follow-up QCR

## Slide 32: Production follow-up (QCR)

## Slide 33: REFERENCES
Jack T. Tanabe “Iron Dominated Electromagnets” Design, Fabrication, assembly and measurements.
T. Zickler (CERN) “Basic design and engineering of normal‐conducting, iron‐dominated electro‐magnets”. CERN Accelerator School Specialized Course on Magnets. Bruges, Belgium, 16‐25 June 2009
3) Neil Marks. “Conventional magnets for Accelerators”. Lecture to Cockcroft Institute. 2005